## Slide 1
TAP: Token-Based Adaptive Power Gating
Andrew B. Kahng, Seokhyeong Kang, Tajana S. Rosing, and Richard Strong
UC San Diego
Motivation
More leakage at advanced technology nodes
More cores  longer memory latencies
Long memory accesses ( > 45ns) waste core power!
Goals
Power gate cores during memory accesses
Zero performance hit on the application
Adapt to application behavior and system utilization
Maintain core-voltage noise fluctuations below 5%
Keep core current below peak-current limit
Token-Based Adaptive Power Gating
Programmable Power Gating Switch (PPGS)
Two-stage wake-up sequence
First-stage header switches control peak current
Peak current controls the wake-up latency
More peak current  more voltage noise
State Retention
Architectural registers saved in retention flip-flops
SRAM-cell leakage reduced via source biasing
Complex logic and non-essential flip-flops power gated
Wake-up Sequence
Token packet contains:
Cache level of the miss
ETA of response from next level
Sent by cache controller
PPGS:
Receives tokens
Assigns ETAs to each memory request
Determines core stall window
WUC: Wake-up Controller
PPGS registers core state (idle/active)
WUC determines safe wake-up modes
Aggressive wake-up modes follow lower utilization
Support from NSF, MARCO FCRP (MuSyC and GSRC centers), SRC, Oracle, and Qualcomm is gratefully acknowledged.
Microarchitectural monitoring
Circuit level
Power gating
Power-gating
controller
enable_few
enable_rest
m[0]
m[1]
m[9]
m[0-9]
PPGS
Token controller
WUC
Wake-up
Mode
Request
Wake-up
Mode
Response
Token
Model for Core Wake-up Latency
T = T0(w+βx+Υy+δz)α
w: # of adjacent waking up cores
x: # of diagonal waking up cores
y: # of non-adjacent waking up cores
z: # of adjacent cores at edge of chip
Core Wake-up Stagger
Two or more cores waking up at the same time increases wake-up latency
WUC may add stagger between when two cores start waking up
Stagger’s Effect of Core Wake-up Latency
At 0T stagger, wake-up latency increases with the number of woken-up cores
Stagger reduces wake-up latencies dependence on number of woken-up cores.
A 1T (0.3ns) stagger reduces wake-up latency up to 66%
For 2, 3, and 4 cores waking up simultaneously, a 3T stagger reduces wake-up latency by 18.8%, 31.9%, 40.3%, respectively
Energy Savings Comparison
Overview
Core Power Gating
System Design
Modeling Core Wake-up Latency & Stagger
Results
TAP
experiences 0% performance hit
yields 22.39% energy savings for EV6
5.17X the energy savings of practical DVFS
adapts to memory utilization (bzip2 vs mcf)
Parameter | Value
Core Model | Dec-Alpha EV6 @ 3.3GHz
Functional Units | 6ALU, 2IMULT, 2FPALU
L1/L2 Priv. Caches | 32KB 1cyc/256KB 4.5ns
L3 Cache | 8MB-16way 13ns
Memory | DDR3 2GB 50ns
Core-to-L3 token Lat. | 17.5ns
Core-to-WUC Latency | 5ns
PPGS Wake-up Modes | 4.5ns-9.1ns
EV6 Pipeline Refill Lat. | 2.12ns
EV6 Core Wake-up Eng. | 15,358pJ
EV6 Leakage Power | 0.916 Watts
EV6 Leakage Reduction | 97.65%
EV6 PG Break Even Point | 17.17ns
Assumptions & Sensitivity
UCSDCSE