## Slide 1: NOLO: A No-Loop, Predictive Useful Skew Methodology for Improved Timing in IC Implementation
Tuck-Boon Chan, Andrew B. Kahng, Jiajia Li
VLSI CAD LABORATORY, UC San Diego

## Slide 2: Outline
Background and Motivation
Problem Statement
Our Methodologies
Experimental Setup and Results
Conclusion

## Slide 3: Outline
Background and Motivation
Problem Statement
Our Methodologies
Experimental Setup and Results
Conclusion

## Slide 4: Typical Useful Skew Flow
Useful Skew adjusts clock sink latencies to improve performance and/or timing robustness of IC designs
Clock
7/3
10/0
7/3
FF1
FF2
FF3
Clock period = 10
Min. slack with zero skew = 0
Data path
Clock tree
Delay/Slack/Clock latency
5
5
5

## Slide 5: Typical Useful Skew Flow
Useful Skew adjusts clock sink latencies to improve performance and/or robustness of IC designs
Clock
7/2
10/2
7/2
FF1
FF2
FF3
Clock period = 10
Min. slack with useful skew = 2
Data path
Clock tree
Delay/Slack/Clock latency
7
6
5
Typical useful skew flow
Synthesis
Routing/Route Opt.
Placement/Place Opt.
RTL netlist
CTS/CTS Opt.
Skew Opt.

## Slide 6: “Chicken-and-Egg” Problem
Typical useful skew flow synthesizes and places designs with zero skew  Benefit of useful skew is limited
Synthesis
Routing/Route Opt.
Placement/Place Opt.
RTL netlist
CTS/CTS Opt.
Skew Opt.
Assume zero skew
Apply useful skew

## Slide 7: Back-Annotation Flow
Iteratively back-annotates post-placement useful skew to synthesis  Account for interactions among synthesis, placement and useful skew optimization
Synthesis
Routing/Route Opt.
Placement/Place Opt.
RTL netlist
CTS/CTS Opt.
Useful Skew
Issue: unacceptable large turnaround time
Our goal = predictive, one-pass (no-loop) flow

## Slide 8: Outline
Background and Motivation
Problem Statement
Our Methodologies
Experimental Setup and Results
Conclusion

## Slide 9: NOLO (No-Loop) Useful Skew Optimization Problem
Given a netlist and timing constraints
Determine clock latency for each sink (= flip-flop), using a one-pass implementation flow
Objective: minimize total negative slack (TNS)

## Slide 10: Outline
Background and Motivation
Problem Statement
Our Methodologies
Experimental Setup and Results
Conclusion

## Slide 11: Previous Useful Skew Optimizations
Maximize minimum slack in a circuit
[Fishburn90] formulates linear programming (LP) to optimize clock latencies
[Szymanski92] improves the efficiency of LP by selectively generating constraints
[Wang04] proposes LP-based approach to evaluate potential slacks and optimize clock skew
Maximize all slacks in a circuit
[Albrecht02] formulates useful skew optimization as maximum mean weight cycle (MMWC) problem  optimizes using graph-based method

## Slide 12: MMWC-Based Skew Optimization
Construct sequential graph (vertex = flip-flop, edge = max-/min-delay path, edge weight = setup/hold slack)
Delay/Slack/Clock latency
A
B
C
D
E
20/2
10/10
12/8
10/10
2/18
10/10
+0
+0
+0
+0
+0
Clock period = 20
Initial graph

## Slide 13: MMWC-Based Skew Optimization
Construct sequential graph (vertex = flip-flop, edge = max-/min-delay path, edge weight = setup/hold slack)
Iteratively find critical loop  optimize slacks  contract critical loop into one vertex  update adjacent edges  optimize the rest
Delay/Slack/Clock latency
A
B
C
D
E
20/2
10/10
12/8
10/10
2/18
10/10
+0
+0
+0
+0
+0
D
E
A
B
C
20/6
10/6
12/6
10/14
2/18
10/4
+0
+6
+4
+0
+0
Clock period = 20
Initial graph
After 1st iteration

## Slide 14: MMWC-Based Skew Optimization
Construct sequential graph (vertex = flip-flop, edge = max-/min-delay path, edge weight = setup/hold slack)
Iteratively find critical loop  optimize slacks  contract critical loop into one vertex  update adjacent edges  optimize the rest
Delay/Slack/Clock latency
A
B
C
D
E
20/2
10/10
12/8
10/10
2/18
10/10
+0
+0
+0
+0
+0
D
E
A
B
C
20/6
10/6
12/6
10/14
2/18
10/4
+0
+6
+4
+0
+0
A
B
C
D
E
20/6
10/6
12/6
2/12
10/12
10/12
+8
+6
+4
+2
+0
Clock period = 20
Initial graph
After 1st iteration
After 2nd iteration

## Slide 15: Simple Predictive Flow
Timing analysis at post-synthesis stage
Perform useful skew optimization
Apply resulting useful skew (clock latencies) during following implementation stages
Synthesis
RTL netlist
Routing/Route Opt.
Placement/Place Opt.
CTS/CTS Opt.
Predictive Useful Skew
Maximize ∑ setup slacks
Subject to hold constraints

## Slide 16: Impact of Early Optimization
Post-synthesis useful skew optimization (simple predictive)  Improved clock skew relaxes timing constraints  Correlation between post-synthesis & post-routing slacks↑
With useful skew
Without useful skew
0ps to 150ps
0ps to 250ps
Post-routing critical path corresponds to paths with 0-150 (0-250)ps slacks w/ (w/o) useful skew

## Slide 17: Key Observation
Will the optimization at post-synthesis stage still be valid at post-routing stage?
Recall: Improved correlation between post-synthesis and post-routing slacks
Expect: Post-synthesis optimization leads to similar timing improvement as post-routing optimization
Synthesis
P&R
Useful Skew
Useful Skew
Compare
- Yes

## Slide 18: Improved Predictive Flow
Solution quality of predictive optimization is affected by timing optimizations during P&R (e.g., Vt-swapping)  Predict useful skew based on LVT-only netlist
LVT-only synthesis  estimation of achievable slacks
Synthesis w/ Multi-Vt
Routing/Route Opt.
Placement/Place Opt.
RTL netlist
CTS/CTS Opt.
Predictive Useful Skew
Synthesis w/ LVT
LVT-only netlist
We use setup slacks from LVT-only case and hold slacks from multi-Vt case

## Slide 19: Outline
Background and Motivation
Problem Statement
Our Methodologies
Experimental Setup and Results
Conclusion

## Slide 20: Experimental Setup
Design
Technology 28nm FDSOI, dual-Vt {SVT, LVT}
Signoff corners {125ºC, 0.9V, SS} and {-40ºC, 1.05V, FF}
Tools
  Synthesis: Synopsys Design Compiler vH-2013.03-SP3
  P&R: Synopsys IC Compiler vH-2013.06-SP2
Tool “denoising” execute three separate runs with small perturbation of clock period (-1ps, 0ps, +1ps), take best outcome
Design | Clk period (ns) | #Cells | #Flip-flops | #Paths
aes_cipher | 0.6 | ~23K | 530 | 16251
des_perf | 0.5 | ~11K | 1985 | 23153
jpeg_encoder | 0.6 | ~50K | 4712 | 137333
mpeg2 | 0.4 | ~11K | 3381 | 95490

## Slide 21: Comparison Among Flows
Variants of back-annotation flows
SimPred = simple prediction flow
ImpPred = improved prediction flow
Flow | Back annotate from | Back annotate to
BA-W | Post-placement | Pre-synthesis
BA-I | Post-placement | Pre-placement
BA-II | Post-routing | Pre-synthesis
BA-III | Post-routing | Pre-placement
BA-IV | Post-routing | Pre-CTS

## Slide 22: Experimental Results
Predictive flow (ImpPred) achieves similar / better timing, with much less runtime, compared to the average of back-annotation flow variants (BA avg)
Different back-annotation flows  timing quality varies  Cannot completely resolve the “chicken-and-egg” problem
Chart: TNS (ns)
| -4.996
BA-I | 150
BA-II | 200
BA-III | 170
BA-IV | 144
BA-W | 145
SImPred | 79
ImpPred | 62
BA avg | 161.8
Chart: TNS (ns)
| -5.315999999999999
BA-I | 121
BA-II | 159
BA-III | 138
BA-IV | 131
BA-W | 101
SImPred | 61
ImpPred | 53
BA avg | 130
Chart: TNS (ns)
| -7.59
BA-I | 162
BA-II | 228
BA-III | 191
BA-IV | 157
BA-W | 165
SImPred | 97
ImpPred | 79
BA avg | 180.6
Chart: TNS (ns)
| -18.438
BA-I | 810
BA-II | 981
BA-III | 858
BA-IV | 789
BA-W | 1171
SImPred | 358
ImpPred | 339
BA avg | 921.8
aes_cipher
des_perf
jpeg_encoder
mpeg2
Less runtime
Smaller TNS

## Slide 23: Outline
Background and Motivation
Problem Statement
Our Methodologies
Experimental Setup and Results
Conclusion

## Slide 24: Conclusion
NOLO = a no-loop predictive useful skew optimization flow
Improved prediction of potential slack using LVT-only netlist
Similar or better timing, with much less runtime compared to back-annotation flows
Back-annotation flow cannot completely resolve the “chicken-and-egg” problem
Future Work
  Analyze and apply useful skew across multiple PVT corners
  Study tradeoff among area, power and timing of useful skew optimization

## Slide 25: Acknowledgments
Work supported from Qualcomm, Samsung, NSF, SRC, the IMPACT (UC Discovery) and IMPACT+ centers

## Slide 26
Thank You!

## Slide 27
Backup Slides

## Slide 28
Synthesis
Routing/Route Opt.
Placement/Place Opt.
RTL netlist
CTS/CTS Opt.
Zero-skew flow