## Slide 1: A New Methodology for Reduced Cost of Resilience
Andrew B. Kahng, Seokhyeong Kang and Jiajia Li
UC San Diego VLSI CAD Laboratory

## Slide 2: Outline
Background and Motivation
Problem Statement
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 3: Outline
Background and Motivation
Problem Statement
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 4: Background: Resilient Designs
Detect and recover from timing errors  Ensure correct operation with dynamic variations (e.g., IR drop, temperature fluctuation, cross-coupling, etc.)
Trade off design robustness vs. design quality  E.g., enable margin reduction
Improve performance (i.e., timing speculation)
Chart: Supply voltage (V)
| 0.84 | 0.86 | 0.88 | 0.9 | 0.92 | 0.94 | 0.96 | 0.98 | 1
conventional design | 43.0824 | 51.1636 | 55.8625 | 56.6747
reilient Design | 34.2459 | 33.9939 | 33.2505 | 34.1355 | 34.9294 | 36.0398 | 37.6599 | 39.3021 | 41.0936
Conventional design:
Worst-case signoff
No Vdd downscaling
Resilient design:
Typical-case signoff
Vdd downscaling  reduced energy
15% reduction

## Slide 5: Motivation
Cost of resilience is high
  Additional circuits  area / power penalty
  Recovery from errors  throughput degradation
  Large hold margin  short-path padding cost
Goal: benefits overweigh costs
Razor
Razor-Lite
TIMBER
 | Razor | Razor-Lite | TIMBER
Power penalty | 30% [Das08] | ~0% [Kim13] | 100% [Choudhury09]
Area penalty | 182% [Kim13] | 33% [Kim13] | 255% [Chen13]
#recovery cycles | 5 [Wan09] | 11 [Kim13] | 0 [Choudhury09]

## Slide 6: Outline
Background and Motivation
Problem Statement
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 7: Resilience Cost Reduction Problem
Given: RTL design, throughput requirement and error-tolerant registers
Objective: implement design to minimize energy
Estimation of design energy:
#recovery cycles
Clock period
Error rate [Kahng10]

## Slide 8: Outline
Background and Motivation
Problem Statement
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 9: Related Works
[Choudhury09] masks timing errors only on timing-critical paths to reduce resilience cost
[Yuan13] uses a fine-grained redundant approximate circuits insertion for error masking
[Kahng10] optimizes designs for a target error rate and reduces design energy by lowering supply voltage
[Wan09] optimizes the most frequently-exercised gates for error-rate and energy reduction
Exploration of tradeoffs between cost of resilience vs. cost of datapath optimization has been ignored

## Slide 10: Focus of This Work
#Razor FFs
(resilience cost)
Power/area of fanin circuits
Tradeoff
Chart: #Razor FFs
| 1 | 2 | 3 | 4
Total energy | 10.5684 | 9.9107 | 10.1371 | 10.2531
Energy of non-resilient part | 9.0284 | 9.5715 | 10.0429 | 10.2449
Resilience cost | 1.54 | 0.33922 | 0.094145 | 0.0081938
300 100 50 0
Our work minimizes total energy using the tradeoffs
There is tradeoff between resilience cost vs. cost of datapath optimization …

## Slide 11: Outline
Background and Motivation
Problem Statement
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 12: Overview of Our Methodology
Our flow: pure-resilience  datapath optimizations
Low-cost margin insertion (selective-endpoint optimization)
  Selectively increase margin at endpoint with timing violation
Slack redistribution (clock skew optimization)
  Migrate timing slacks to endpoint with timing violation
 Replace error-tolerant FFs to normal FFs  Reduced resilience cost

## Slide 13: Overall Optimization Flow
Iteratively optimize with SEOpt and SkewOpt
Initial placement (all FFs = error-tolerant FFs)
Energy < min energy?
Save current solution
Margin insertion on K paths based on sensitivity function
Replace error-tolerant FFs w/ normal FFs
SEOpt
Activity aware clock skew optimization
SkewOpt

## Slide 14: Selective-Endpoint Optimization
Optimize fanin cone w/ tighter constraints  Allows replacement of Razor FF w/ normal FF
  Trade off cost of resilience vs. data path optimization
  Question 1: Which endpoint to be optimized?
  Question 2: How many endpoints to be optimized?

## Slide 15: Sensitivity Function
  Which endpoint to be optimized?  Pick endpoints based on sensitivity functions
Vary #endpoints  compare area/power penalty
Candidate Sensitivity Functions
p negative slack endpoint
c cells within fanin cone
Numcri number of negative slack cells

## Slide 16: Iterative Optimization
  Question 2: How many endpoints to be optimized?  Vary #optimized endpoints pick minimum-energy solution
  Optimization Procedure
    Pick top-K endpoints with minimum sensitivity
    Timing optimization on fanin cone of p if ( slack at p is positive) replace with normal FFs
    Error rate estimation
    Check design energy if ( energy is reduced ) store current solution
    Update sensitivity functions; Goto 1

## Slide 17: Clock Skew Optimization
Increase slacks on timing-critical and/or frequently-exercised paths
  Generate sequential graph
  Find cycle of paths with minimum total weight  adjust clock latencies  contract the cycle into one vertex
  Iterate Step 2 until all endpoints are optimized
FF1
FF2
FF3
W12
W23
Clock
Data path
Clock tree
W31
Setup slack of path p-q
Weighting factor
Toggle rate of path p-q
W’
W’
W’
W’ = average weight on cycle

## Slide 18: Outline
Background and Motivation
Problem Statement
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 19: Experimental Setup
Design OpenSparc T1
Technology 28nm FDSOI, dual-VT {RVT, LVT}
Tools
  Synthesis: Synopsys Design Compiler vH-2013.03-SP3
  P&R: Cadence EDI System 13.1
  Gate-level simulation: Cadence NC-Verilog v8.2
  Liberty characterization: Synopsys SiliconSmart v2013.06-SP1
Questions
  How do the benefits/costs of resilience vary with safety margin?
  How do the benefits/costs of resilience change in AVS context?
Module | Description | # of cells
EXU | Integer execution | 18K
MUL | Integer multiplier | 13K

## Slide 20: Methodology Comparison
Reference flows
  Pure-margin (PM): conventional method w/ only margin insertion
  Brute-force (BF): use error-tolerant FFs for timing-critical endpoints
Proposed method (CO) achieves up to 20% energy reduction compared to reference methods
Resilience benefits increase with safety margin
Chart: Energy (mJ)
| PM | BF | CO | PM | BF | CO | PM | BF | CO
Energy w/o resilience | 41.1387 | 40.647 | 40.3599 | 41.0088 | 39.6434 | 32.2459 | 43.0824 | 36.0572 | 31.4047
Energy penalty of additional circuits | 0 | 1.5374 | 0.0018024 | 0 | 1.9129 | 0.63347 | 0 | 2.0765 | 1.1495
Energy penalty of throughput degradation | 0 | 1.4467 | 1.0627e-05 | 0 | 4.8335 | 0.09284 | 0 | 6.8185 | 0.69595
Large margin
Medium margin
Small margin
MUL
Chart: Energy (mJ)
| PM | BF | CO | PM | BF | CO | PM | BF | CO
Energy w/o resilience | 30.8809 | 28.2189 | 27.6593 | 32.7427 | 28.586 | 27.8448 | 32.9936 | 28.1536 | 27.9559
Energy penalty of additional circuits | 0 | 1.5296 | 0.50914 | 0 | 1.9952 | 0.663 | 0 | 2.461 | 0.80293
Energy penalty of throughput degradation | 0 | 0.54953 | 0.26731 | 0 | 1.4996 | 0.5185 | 0 | 2.4264 | 0.77836
EXU
Large margin
Medium margin
Small margin
Small/medium/large margin  safety margin = 5%/10%/15% of clock period

## Slide 21: Energy Reduction from AVS
Adaptive voltage scaling allows a lower supply voltage for resilient designs, thus reduced power
Proposed method trades off between timing-error penalty vs. reduced power at a lower supply voltage
Proposed method achieves an average of 18% energy reduction compared to pure-margin designs  Resilience benefits increase in the context of AVS strategy
Chart: Supply voltage (V)
| 0.84000000000000019 | 0.86000000000000021 | 0.88 | 0.9 | 0.92 | 0.94000000000000017 | 0.96000000000000019 | 0.98 | 1
brute-force | 40.1651 | 41.573 | 42.7234 | 44.2628 | 44.7032 | 44.8982 | 45.2599 | 45.3674 | 46.2223
pure-margin | 43.0824 | 51.1636 | 55.8625 | 56.6747
CombOpt | 34.2459 | 33.9939 | 33.2505 | 34.1355 | 34.9294 | 36.0398 | 37.6599 | 39.3021 | 41.0936
Chart: Supply voltage (V)
| 0.84000000000000019 | 0.86000000000000021 | 0.88 | 0.9 | 0.92 | 0.94000000000000017 | 0.96000000000000019 | 0.98 | 1 | 1.02
brute-force | 29.3591 | 30.2241 | 31.1854 | 32.1372 | 33.0411 | 33.6749 | 34.1929 | 34.7202 | 35.2747 | 36.7424
pure-margin | 32.9936 | 34.6941 | 36.3988 | 40.3993
CombOpt | 27.4048 | 28.2975 | 28.9347 | 29.5377 | 30.4006 | 31.2339 | 32.5962 | 33.7191 | 35.1193 | 36.6723
MUL
EXU
Minimum achievable energy

## Slide 22: Outline
Background and Motivation
Problem Statement
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 23: Conclusion
New design flow for mixing of resilient and non-resilient circuits
Combined selective-endpoint and clock skew optimizations reduce costs of resilience
Up to 20% energy reduction compared to reference methods
Future work
  Unified framework for data- and clock-path optimization
  Study impact of process variation on resilient design methodologies

## Slide 24: Thank you!