## Slide 1: Benchmarking of Mask Fracturing Heuristics
Tuck Boon Chan, Puneet Gupta, Kwangsoo Han, Abde Ali Kagalwalla, Andrew B. Kahng and Emile Sahouria
Notes: Thank you for the kind introduction. Good afternoon, everyone. The title of my talk is “Benchmarking of Mask Fracturing Heuristics”. This is a joint work of UCSD, UCLA and Mentor Graphics.

## Slide 2: Outline
Motivation & Previous Work
Mask Fracturing Problem
ILP-Based Benchmarking
Optimal Benchmark Generation
Conclusions and Future Work
Notes: In this talk, I will first introduce motivation, our contributions, previous work, and then describe the mask fracturing problem.
I will present our key benchmarking methods, which are the ILP-based benchmarking and optimal benchmark generation. And then, I will conclude my talk.

## Slide 3: Growing Mask Fabrication Cost
Photomask manufacturing costs escalating (Multiple patterning, aggressive RETs)
  E-beam mask write time increasing with technology scaling
  Curvilinear ILT shapes  more shots
Calibre pxOPC layout
Source: M. Chandramouli, et al., SPIE BACUS Photomask 2012
Minimizing mask fracturing cost
  Reducing e-beam write time
  Reducing number of shots
Reducing number of shots
Notes: Photomask manufacturing costs are increasing because of multiple patterning and aggressive resolution enhancement techniques.
The increasing e-beam write time with technology scaling is the one key reason. The lower left figure shows the increasing write time. In the figure, x-axis is the technology node and y-axis is the average mask write time relative to 45nm.
Also, use of inverse lithography makes the mask shape curvilinear and increases shot count. In this figure, we see the target shapes are curvilinear.
Therefore, reducing write time or the number of shots is important to reduce the fracturing cost. In this work, we focus on reducing the number of shots.

## Slide 4: Modern Mask Fracturing Challenges
Determine e-beam shots to transfer the circuit pattern to mask
Only non-overlapping shots used  Overlapping shots allowed
  Lower shot count
  NP-hard
E-beam proximity effect due to scattering of electrons
 Blurring of rectangular shots
Target shape
E-beam shot
Overlapping shots allowed (2 shots)
Traditional mask fracturing (3 shots)
Blurred image of a shot
Notes: Here, I will talk about modern mask fracturing challenges.
Mask fracturing is to determine the e-beam shots to transfer the circuit pattern to the mask. Traditionally mask fracturing only used non-overlapping shots as shown on the left here.
However, modern e-beam tools allow shots to overlap. This has helped to reduce shot count as shown in the figure. In this example, we see the number of shots reduced from 3 shots to 2 shots. But, it makes the fracturing problem even harder than the traditional one.
Another challenge is the e-beam proximity effect due to the scattering of electrons. This causes blurring of shots and needs to be accounted for during fracturing.
In this slide, I have discussed two key challenges for modern mask fracturing, which are overlapping shots and e-beam proximity effect. Next, I will summarize previous works.

## Slide 5: Previous Work
Traditional mask fracturing approaches
  Sliver minimization [Kahng et al., BACUS04]
  Recursive approach [Jiang et al., SPIE11]
  Limitations: Non-overlapping shots, proximity effect ignored
Rectilinear polygon covering
  ILP formulation [Heinrich-Litan et al., J. Exp. Alg., 2006]
  Optimal covering for x- or y- direction convex polygons [Franzblau, Theory of Computing, 1984]
  Limitations: Proximity effect ignored
Model-based mask data preparation (MB-MDP)
  Matching Pursuit [Jiang et al., BACUS11]
  Comparison of some heuristics [Elayat et al., SPIE11]
  Limitations: Unclear if heuristics are close to optimal shot count
How can we evaluate the suboptimality of these heuristics?
Notes: Several works have studied mask fracturing problem in previous literature.
For traditional mask fracturing, Kahng et al in 2004 propose sliver minimization methodology. Later, in 2011, Jiang et al propose a recursive approach. However, overlapping shots are not accounted and they ignored e-beam proximity effect.
Another class of related work is the rectilinear covering problem. Here the overlapping shots were allowed, but e-beam proximity effects were ignored.
Recently, several heuristics have been discussed to solve the model-based fracturing problem. In this category, they consider overlapping shots and e-beam proximity effect. As an example, Jiang has presented a matching pursuit based approach, and Elayat has compared a few different heuristics. Although these works consider the overlapping shots and e-beam proximity effect, we do not know how their heuristics are good or bad
Then, how can we evaluate the suboptimality of these heuristics?

## Slide 6: Our Contributions
Methodologies to evaluate mask fracturing heuristics
  ILP-based lower/upper bound estimation
  Benchmark construction with known optimal solution
Allow overlapping shots
Consider e-beam proximity effect
Our method shows suboptimality of a state-of-art prototype version of capability within a commercial tool. (refer to as “PROTO-EDA”)
Benchmark suite with known optimal solution. http://vlsicad.ucsd.edu/ILT/index.html
Notes: To evaluate the suboptimality of mask fracturing heuristics, we propose two methodologies.
First, we have developed an ILP-based method. This method gives tight lower and upper bounds of shot count for any given mask shape. However, this method requires considerable computational effort.
Second, we propose a method to construct benchmark mask shapes with known optimal shot count
Note that in this work we consider overlapping shots and e-beam proximity effect.
In the following discussion, I will show more details about the two methodologies. It shows suboptimality of a state-of art prototype version of capability within a commercial tool. In the following discussion, we will just call this tool PROTO-EDA. Also, we publish a benchmark suite with known optimal solution.

## Slide 7: Outline
Motivation & Previous Work
Mask Fracturing Problem
ILP-Based Benchmarking
Optimal Benchmark Generation
Conclusions and Future Work
Notes: Now, I will describe the mask fracturing problem

## Slide 8: Proximity Model + Sampling
Intensity profile of a shot ()
  Convolution of 2D rectangular function with e-beam proximity kernel
Pixel based e-beam resist model with constant threshold (Rt)
Set of pixels divided into three disjoint sets
  Pd: set of pixels within critical dimension (CD) tolerance of shape boundary
  P1(P0): set of pixels inside (outside) target shape boundary
Example of pixel based target shape
P1
Pd
P0
Intensity profile of a shot s
Notes: Here, we describe some background definitions or models what we use to formulate mask fracturing problem.
To consider e-beam proximity effect, we profile the intensity of a shot. This is modeled by convolving the rectangular function with e-beam proximity kernel.
Then, we use pixel based e-beam resist model with constant resist threshold. If any pixel of intensity is larger than the resist threshold, it becomes an image. The set of pixels is divided into three disjoint sets as shown in lower right figure. Pd is the set of pixels within a given critical dimension tolerance. And, P1 is the set of pixels within the closed boundary of the shape. And, P0 is the set of pixels outside the target shape.

## Slide 9: Problem Formulation
Objective: Minimize total number of e-beam shots
  Inputs: Target shape, set of all candidate shots (S), resist threshold (Rt), e-beam proximity kernel, CD tolerance
  Output: Set of rectangular shots (Smin)
  Constraints:
(inside)
(outside)
Notes: Based on the models described in previous slide, we formulate the mask fracturing problem.
The goal is to minimize the total number of e-beam shots subject to the following constraints. First, any pixel within a given target shape must have larger intensity than the resist threshold. Second, any pixels outside of the target shape should have smaller intensity than the resist threshold. By following these constraints, the printed mask shape is the same with target shape. If any solution has minimum number of shots for a given shape, we say it is optimal.

## Slide 10: Outline
Motivation & Previous Work
Mask Fracturing Problem
ILP-Based Benchmarking
Optimal Benchmark Generation
Conclusions and Future Work
Notes: Next, I will present ILP-based benchmarking which is our first benchmarking method.

## Slide 11: ILP Formulation
Enumerate all possible shots of different sizes and locations  Candidate shot dictionary
Define selection variable for each candidate shot ( if shot s is part of solution, zero otherwise)
Minimize such that
Step size: 0.2nm
Minimum shot size: 13nm
Maximum shot size: 60nm
 Number of variables: 1.19M
60nm
60nm
Notes: Our ILP formulation is fairly straightforward.
We first enumerate all possible shot sizes and locations. Then, we compute the intensity values of each candidate shot. Also, we define a binary selection variable for each candidate shot. And the variable is one if the candidate shot is part of the fracturing solution.
Now, the ILP formulation shown here minimizes the number of shots with the constraints described in the previous slide.
But, the number of variables is very large because we enumerate all possible shot sizes and locations with a find granularity. For a small contact shape shown here, the number of candidate shots is more than one million. Note that it is not possible to solve these problems even with commercial ILP solvers as they run out of memory.

## Slide 12: Reducing Problem Size: Pruning Candidate Shots
Exclude any candidate shot which can expose the intensity greater than threshold to the pixel outside target shape  Cannot be a part of a feasible fracturing solution
Exclude any shot that does not touch any target boundary  If such a shot is part of optimal solution, it can be replaced by a larger shot that encloses this small shot
 Both these candidate shot pruning methods do not affect the optimality of the ILP
Target shape
Candidate shot
Notes: To reduce the number of candidate shots, we use a couple of simple pruning strategies.
The first rule is that if any candidate shot can expose the intensity greater than threshold to the pixel of outside target shape, we exclude such a shot because it cannot be a part of a feasible fracturing solution.
We also exclude any shot that does not touch any target boundary. This is because if such a shot were part of the fracturing solution, it can be replaced by a larger shot that encloses this small shot And, it does not affect the shot count or feasibility.
Both these candidate shot pruning methods do not affect the optimality of ILP. But, even we use these pruning strategies, there are still large amount of candidate shots. So, we use branch and price technique and it is described in the next slide.

## Slide 13: Branch-and-Price (B&P)
Well-known method to solve ILPs with large number of variables using column generation
Start with smaller number of candidate shots in RMP
Pricing to iteratively add new candidate shots
Repeat iterative procedure at each node of branch-and-bound tree
Dual
variables
Insert candidate shots
Initial
Solution
Reduced Master Problem (RMP)
Relaxed LP with
smaller set of
candidate shots
Pricing Problem
Find candidate
shots with
negative reduced cost
None
found
Notes: In addition to the pruning rules, we solve the ILP using branch-and-price. It is a well-known method to solve ILPs with a large number of variables.
In branch-and-price, we start with a smaller number of candidate shots and solve a reduced master problem.
Then a separate pricing problem is solved to find proper candidate shots that must be inserted to the reduced master problem.
The key challenge of this method is to develop fast heuristics to solve the pricing problem. We have developed a two-step heuristic that we discuss in more detail in our paper.

## Slide 14: Experimental Setup
Implemented using C++ (Boost Polygon Library, OpenAccess API and Eigen)
Real ILT shapes obtained by running Calibre pxOPC on 32nm ICCAD’13 contest layouts
Gaussian e-beam proximity model with σ = 6.25nm
Shot size constraints  Minimum (13nm) and maximum (1000nm)
CD tolerance  2nm
B&P  SCIP optimization framework + CPLEX v12.5
  Run on 8-core machine with 12 hour time limit
Notes: This ILP-based method is implemented using C++
We obtain the real ILT shapes by running Calibre on 32nm ICCAD’13 contest layouts and use a Gaussian e-beam proximity model with sigma as 6.25nm.
The minimum and maximum shot sizes are 13nm and 1000nm respectively. And, the CD tolerance is 2nm. All the dimensions are in wafer scale.
We used CPLEX and run on 8-core machine with 12 hour time limit.

## Slide 15: Suboptimality Analysis of Real ILT Shapes
ClipID | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
PROTO-EDA | 9 | 21 | 11 | 25 | 17 | 7 | 9 | 20 | 10 | 15
Lower Bound | 3 | 5 | 2 | 7 | 4 | 2 | 3 | 5 | 5 | 4
Upper Bound | 4 | 21 | 3 | 25 | 7 | 3 | 4 | 8 | 10 | 6
60nm
60nm
6
105nm
280nm
4
111nm
55nm
1
222nm
180nm
2
125nm
143nm
5
75nm
70nm
7
75nm
95nm
3
132nm
137nm
8
118nm
12nm
9
47nm
190nm
10
Upper bound is lower than the shot count of PROTO-EDA (7 out of 10 shapes)
Suboptimality of PROTO-EDA up to 3.6X
Notes: We select 10 real ILT shapes and run it with PROTO-EDA and our ILP-based method.
Our ILP-based method reports the lower and upper bound for each shape. For seven out of 10 shapes, the upper bound is lower than the shot count of PROTO-EDA. In the optimistic assumption, if the upper bound is the optimal shot count, the suboptimality of the PROTO-EDA is up to 3.6X. This implies there is significant room for improving the quality of fracturing solution.

## Slide 16: Outline
Motivation & Previous Work
Mask Fracturing Problem
ILP-Based Benchmarking
Optimal Benchmark Generation
Conclusions and Future Work
Notes: Now, I will explain our optimal benchmark generation method

## Slide 17: Benchmark Generation Overview
Generate benchmark target mask shapes with known optimal fracturing solution
  Resist image of shots (proximity effect + resist)  Generated benchmark
Part of boundary of target mask shape  Boundary segment
Add shots iteratively
  New shot adjacent to existing shots  New boundary segment requiring two shots
Boundary segment that requires exactly two shots
Notes: We generate benchmark ILT mask shapes in a correct-by-construction way.
The resist images of shots are accumulated to generate benchmark. We first define boundary segment as part of the boundary of a target shape. To guarantee the optimality of generated shapes, we generate the boundary segment requiring two shots. In this figure, the red boundary segment requires at least two shots. We first generate such red boundary segment using exactly two shots.
Then, we iteratively add a new shot adjacent to one of the existing shots. Whenever we add a new shot, there is a new boundary segments requiring two shots.
Here, I have shown the overview of benchmark generation. In the next slide, I will explain how we make the boundary segment requiring two shots.

## Slide 18: Boundary Segment
Straight boundary segment
  Maximize coverage of one shot
Concave boundary segment
  Because of concavity of target boundary the longest straight boundary is always longer than the longest concave boundary (LCon(W,H)) at the same slope

2ɤ
Straight target boundary
Llin(W,H)
Image boundary
Inner boundary
Outer boundary
P1
P0
2ɤ
Lcon(W,H)

2ɤ
Lcon(W,H)

2ɤ
Llin(W,H)
Shifted image boundary
P0
P1
Image boundary
P0
P1
P1
P1
(a)
(b)
   Length between blue crossing points is the longest straight boundary (Llin(W,H))
Notes: To determine the boundary segment requiring two shots, we find the longest straight and concave boundary segment for a given shot image.
We assume there is long enough straight boundary. Also, there are inner and outer boundaries considering the CD tolerance. To get the longest straight boundary, we maximize the coverage of one shot. This means the image boundary contacts to the outer boundary of target. At this point, the length of straight line between blue crossing points is the longest straight boundary.
In the same way, we find the longest length of concave boundary segment. I would like to point out that the longest straight boundary segment is always longer than the longest concave boundary segment at the same slope and shot size.
In this slide, I explained how we find the longest straight and concave boundary segment. In the next slide, I will show you how the maximum length covered by one shot can be determined.

## Slide 19: Maximum Length Covered by One Shot
P1
P0
  Corner rounding saturation  Limits maximum length of straight boundary segment that one shot can cover ()
  If straight line or concave boundary segment with length  More than one shot required
Lt
P1
P0
Notes: As the shot size increases, the length of longest boundary segment increases. But, the corner rounding of shot saturates if the shot is large enough. In this figure, even the shot size increase, the length of longest straight boundary segment does not increase. This limits the maximum length of straight boundary segment.
Therefore, we know that more than one shot is required for the target boundary, if the straight or concave target boundary is longer than the maximum length
Now, we know the maximum length covered by one shot.

## Slide 20: Construction of Target Shape
  Main boundary segment (bmain)  Determines number of optimal shots for target shape (green curve)
  Critical boundary segment (bcri)  Part of main boundary segment requiring two shots (red curve)
  Width/height of shot adjusted to get different benchmarks
Intensity > Rt
Intensity < Rt
Intensity > Rt
Intensity < Rt
bcri B2
bmain
Intensity > Rt
Intensity < Rt
bcri B2
bmain
Notes: Here we show an example how we generate benchmark mask shapes with known optimal shot count.
First, we place one shot. Then, we place the second shot by focusing on the upper left corners of shots. The upper left corners should be far apart so that the generated boundary segment requires two shots. In the same way, we add one more shot and it generate a new boundary segment which requires two shots.
Here, we define two kinds of boundary segment.
First, we define the main boundary segment. It determines the number of optimal shots for target shape. In the right figure, the green curve is the main boundary segment. Second, we define the critical boundary segment. it is a part of main boundary segment which requires two shots. The red curve in the right figure is the critical boundary segment.
As shown in this example, we place any two neighboring corners far apart. And the extended main boundary segment includes a new critical boundary segment.
Also, if we do not perturb the main boundary segment, we can freely change the mask shapes by adjusting different width or height.

## Slide 21: Merging and Rotating Target Shapes
  Rotate target shape in multiples  Rectilinear shot, no change in optimal solution
  Merge two target shapes with different critical boundary segments
    One shot from each target selected and stretched
    Other shots which define critical boundary should not be merge-able
P0
bcri
bcri
Stretching
P1
P1
Rotate 90o
P1
P0
Merged shot
bcri
bcri
Notes: Here, we explain merging and rotating rules. First, we can rotate the target shape in 90 degree multiples. The rotated shape is still optimal because all the shots are rectilinear. Second, we can merge two target shapes. When we merge the shapes, we stretch only one shot from each target. The merging shots should be aligned and other shots should not be merge-able. These rules give more flexibility in generating benchmark.

## Slide 22: Arbitrary Generated Benchmarks
Carefully selected shot locations such that optimal solution is known
Suboptimality of PROTO-EDA: 2X – 3X
ClipID | Optimal | PROTO-EDA | Lower Bound | Upper Bound
1 | 3 | 6 | 2 | 3
2 | 16 | 38 | 10 | 34
3 | 17 | 50 | 1 | 48
4 | 7 | 21 | 5 | 7
5 | 3 | 7 | 2 | 3
70nm
70nm
1
102nm
309nm
2
143nm
170nm
3
121nm
145nm
4
61nm
65nm
5
2X
3X
Notes: We generate five arbitrary mask shapes by selecting the shot locations with known optimal solution. Then, we solve the generated shapes using PROTO-EDA and ILP-based benchmarking method. Depending on the target shape, the suboptimality of PROTO-EDA ranges from 2X to 3X. Also, the lower and upper bound from ILP-based solution find near optimal solution in testcase 1, 4 and 5.

## Slide 23: Realistic Generated Benchmarks
Carefully selected shot locations such that optimal solution is known, similar to actual ILT shapes
Suboptimality of PROTO-EDA: 2X – 3.7X
ClipID | Optimal | PROTO-EDA | Lower Bound | Upper Bound
1 | 5 | 10 | 3 | 5
2 | 7 | 26 | 5 | 7
3 | 5 | 12 | 3 | 5
4 | 9 | 20 | 6 | 9
5 | 6 | 15 | 4 | 8
110nm
60nm
1
162nm
190nm
2
80nm
130nm
3
87nm
258nm
4
152nm
157nm
5
2X
3.7X
Notes: Since the arbitrary generated benchmarks are unrealistic, we generate another five realistic mask shapes. We carefully generate the shapes to make it similar to the actual ILT shapes. For these testcases, the suboptimality of PROTO-EDA ranges from 2X to 3.7X. Here, I would like to point out that the generated benchmarks are more wavy compared to actual ILT mask shapes. This makes the suboptimality estimation more pessimistic, but we see there remains considerable opportunity to improve heuristics.

## Slide 24: Conclusions
ILP-based benchmarking of mask fracturing heuristics
  Obtains tight upper/lower bounds for real ILT shapes
Optimal benchmark generation
  Constructive approach to generate mask target shapes with known optimal fracturing solution
  Arbitrary benchmarks  Heuristic 2X - 3X suboptimal
  Realistic benchmarks  Heuristic 2X – 3.7X suboptimal
Future work
  Automatic benchmark generation
  Variable dose and non-rectangular shots
Benchmark suite available at: http://vlsicad.ucsd.edu/ILT/index.html
Notes: In this talk, we propose two methods to benchmark the ILT mask fracturing heuristics.
First, we develop ILP-based benchmarking method and obtain tight upper and lower bounds for real ILT shapes.
Second, we develop the optimal benchmark generation method which generates mask target shapes with known optimal solution. Using the generated benchmarks, we evaluate the heuristic PROTO-EDA and it shows the suboptimality is up to 3.7X.
For future work, we are going to automate the benchmark generation and consider other factors such as variable dose and non-rectangle shots.
Our latest benchmark suite is available at the following link.

## Slide 25: Thank you!
Notes: Thank you for your attention.

## Slide 26: BACK UP

## Slide 27: Benchmark and Real ILT Mask Shapes
70nm
70nm
1
102nm
309nm
2
143nm
170nm
3
121nm
145nm
4
61nm
65nm
5
110nm
60nm
1
162nm
190nm
2
80nm
130nm
3
87nm
258nm
4
152nm
157nm
5
60nm
60nm
6
105nm
280nm
4
111nm
55nm
1
222nm
180nm
2
125nm
143nm
5
75nm
70nm
7
75nm
95nm
3
132nm
137nm
8
118nm
12nm
9
47nm
190nm
10
Arbitrary
generated
benchmarks
(AGB)
Realistic
generated
benchmarks
(RGB)
Actual
ILT mask shapes
Note: Wafer scale

## Slide 28: Pricing: Dual Variables and Reduced Cost
Constraint at every pixel, in ILP has corresponding dual variable,
  Zero for most pixels
  Negative only for
Reduced cost of shot s 

## Slide 29: Pricing: Two-Step Method
Pricing Problem  Find new insertable candidate shots
  Negative reduced cost
  Satisfy pruning and branching rules
Only shots with non-zero intensity at negative dual points can have negative reduced cost
Limit the maximum number of candidate shots inserted back to RMP in each pricing round (500)
Fast Pricer
Iterate over candidate shots within for each negative dual points
Optimal Pricer
Construct boxes around every negative dual point. Iterate over candidate shots that interact with these boxes
No candidate shot found

## Slide 30: Mask Fracturing
Variable shaped e-beam (VSB) tool writes mask pattern
Fracturing  Get rectangular e-beam shots that VSB tool needs to write given mask pattern
E-beam proximity effect due to scattering of electrons
Source: Yu et al., ASPDAC 2013
Fractured mask
Target mask pattern
Source: Bunday et al., Proc. of SPIE, 2008
Scattering of electrons