## Slide 1: Evaluation of BEOL Design Rule Impacts Using An Optimal ILP-based Detailed Router
Kwangsoo Han‡, Andrew B. Kahng‡† and Hyein Lee‡
‡ECE and †CSE Departments, UC San Diego
{kwhan, abk, hilee}@ucsd.edu

## Slide 2: Outline
Motivation
Prior Work
ILP Formulation of Routing Problem
Experimental Results
Conclusions and Future Work

## Slide 3: Patterning Choice  Design Rules  Chip QoR
Which patterning options will give better QoR?
Option 1
Self-aligned double patterning (SADP)
Small metal pitch
7.5T standard cells
Option 2
Litho-etch-litho-etch (LELE)
Large metal pitch
9T standard cells
Will option 1 win?
 Not necessarily
< MinOverlap
< MinSpacing
metal pitch < via pitch
Inserted via
Blocked by the via
Pin access problem
Z
A
B
Standard cell
Z
Impact of patterning choice-induced design rules on chip QoR is not clear
Early evaluation of design rules is important for patterning choice!

## Slide 4: How to Choose Patterning Options?
Patterning option-induced design rules can be evaluated with EDA tools
However, EDA tools have limitations:
  Lack of support for advanced rules
  Heuristics for large-scale optimization may lead to sub-optimal solutions ⇒ cannot see the accurate impact
Our work enables assessment of BEOL ground rule options independently of commercial EDA router
  OptRouter: an Integer linear programming (ILP)-based optimal detailed router
    Compute optimal solutions for small switchboxes
    (sub-20nm relevant) routing options and design rules
  We report routing costs for various BEOL design rules

## Slide 5: Prior Work
Design rule evaluation
  Assessment of gate line-end extension rules [Gupta10]
  UCLA DRE [Ghaida12], Layout pattern-driven DRE [Badr14]
  ChipDRE [Ghaida14]
ILP-based routers
  Global routers: Multicommodity flow-based global router [Carden96], BoxRouter [Cho07], Sidewinder [Hu08]
  Detailed router: MCFRoute [Jia14]
    ILP-based detailed router for DRC fix
    No guarantee of optimal solutions
    No consideration of multi-pin nets

## Slide 6: Outline
Motivation
Prior Work
ILP Formulation of Routing Problem
Experimental Results
Conclusions and Future Work

## Slide 7: Sub-20nm Routing Problem Formulation
Routing resources ⇒ A 3D-mesh graph
  Horizontal and vertical tracks
  Metal layers
A routed net = a set of edges
Objective: Find an optimal routing for a given set of nets under routing constraints
Subject to routing constraints:
  Pin shape
  Via restriction
  Unidirectional routing
  End-of-line (EOL) spacing (SADP-aware)
  Via shape
s
t
Horizontal
tracks
Vertical tracks
Available
layers

## Slide 8: Multicommodity Flow-based ILP
+ more constraints for patterning options, design rules
(Section 3.2)
c: cost, e: edge, f: flow
 Minimize cost
Flow conservation (= connection)
Routing constraints
Objective
For each net routing
Handle Steiner tree
Edge is taken when there is a flow

## Slide 9: Constraints: SADP-Aware Rules
SADP-aware design rules can be checked with end of line (EOL) of each wire segment
EOL in unidirectional routing = via location
(⇒ EOL extension is not considered in this work)
However, via location cannot differentiate case A and B
 Add p variable to indicate from which direction wire comes to a via
< MinOverlap
< MinSpacing
[Xu14]
(a)
(b)
Via
Same via location

## Slide 10: SADP Design Rules with p Variable
p variable: Indicates the direction of EOL
pr,i = 1 : Wire comes from right with EOL at location i
Red points: Forbidden via (EOL) locations to honor minimum overlap/spacing rules
ILP: Mutual exclusion constraints of p variables
pr,i = 1
Forbidden via locations for wires from left
Forbidden via locations for wires from right

## Slide 11: Outline
Motivation
Our Work
Prior Work
ILP Formulation of Routing Problem
Experimental Results
Conclusions and Future Work

## Slide 12: Overall Flow
Various routing options
Via pitches
Double patterning rules
Routing Clips (Switchboxes)
Routing Rules Options 1, 2, ..
Generate Routing Graphs
ILP Formulation
ILP Solver (CPLEX)
Routing cost = Wirelength + 4*#Vias
...
Result of Option1
Result of Option2
Result of OptionN
…

## Slide 13: Experimental Setup: Routing Clip Extraction
Routing clips are extracted from layouts
  Clip size: 1μm X 1μm (7 vertical tracks X 10 horizontal tracks)
Designs implemented with three cell libraries
  8/12-track in 28nm FDSOI and 9-track in 7nm
Select “difficult-to-route” clips based on pin cost metric
  Pin cost = pin area cost + pin spacing cost + #pins [Taghavi10]
An example of routing clips
Chip layout
Blockage
Blockage
Pin
Pin
Pin
Pin
Boundary pins
Boundary pins
Remove internal routings
Keep pin shapes, blockage, routings at boundary
Split into small clips
A routing problem

## Slide 14: Experimental Setup: Routing Rule Options
11 routing options with combinations of SADP rules and #blocked via sites are tested
  RULE1: no restriction (reference for comparison)
Name | SADP rules | Blocked via sites
RULE1 | No SADP | 0 neighbors blocked
RULES 2, 3, 4, 5 | SADP ≥ {M2, M3, M4, M5} | 
RULE6 | No SADP | 4 neighbors blocked
RULES 7, 8 | SADP ≥ {M2, M3} | 
RULE9 | No SADP | 8 neighbors blocked
RULES 10, 11 | SADP ≥ {M2, M3} | 

## Slide 15: Experimental Results: N28-8T
High sensitivity of ∆ Routing cost to #SADP layers (RULES 2, 3, 4, 5)
High sensitivity of ∆ Routing cost to via restrictions (RULES 6, 9)
SADP rules dominate via restriction (RULES 7 ≈ 10 and RULES 8 ≈ 11)
Chart: 
Chart: Clip Index (Sorted ranks of ∆ routing cost )
Infeasible
Routing cost = wirelength + 4*#vias
∆ Routing cost = Routing cost of RULE K – Routing cost of RULE1
Name | SADP rules | Blocked via sites
RULE1 | No SADP | 0 blocked
RULES 2, 3, 4, 5 | SADP ≥ {M2, M3, M4, M5} | 0 blocked
RULE6 | No SADP | 4 blocked
RULES 7, 8 | SADP ≥ {M2, M3} | 4 blocked
RULE9 | No SADP | 8 blocked
RULES 10, 11 | SADP ≥ {M2, M3} | 8 blocked
Hardest
Easiest

## Slide 16: Experimental Results: N7-9T
Chart: Clip Index (Sorted ranks of ∆ routing cost )
Chart: 
Different trends for different libraries
Many dots at zero line ⇒ NOT “difficult-to-route” clips ⇒ Pin cost metric may not be a proper metric to quantify routability
Routing cost = wirelength + 4*#vias
∆ Routing cost = Routing cost of RULE K – Routing cost of RULE1
Infeasible
Name | SADP rules | Blocked via sites
RULE1 | No SADP | 0 blocked
RULES 2, 3, 4, 5 | SADP ≥ {M2, M3, M4, M5} | 0 blocked
RULE6 | No SADP | 4 blocked
RULES 7, 8 | SADP ≥ {M2, M3} | 4 blocked
RULE9 | No SADP | 8 blocked
RULES 10, 11 | SADP ≥ {M2, M3} | 8 blocked

## Slide 17: Conclusions and Future Work
Propose a framework for evaluation of BEOL design rules with OptRouter
Assess routing cost for various BEOL stack options with 28nm 12-track, 8-track and 7nm 9-track
Future / ongoing directions
  EOL extension-aware SADP rule formulation
  Develop a better metric to estimate routability in sub-20nm
  Speedups for routability evaluation with larger routing clips
  Formulate and test other important design rules
Acknowledgement
  We would like to thank Nak Seong of ASML for guidance and many helpful discussions.
Thank you!