## Slide 1: ILP-based co-optimization of cut mask layout, dummy fill and timing for sub-14nm BEOL technology
Kwangsoo Han, Andrew B. Kahng, Hyein Lee and Lutong Wang
{kwhan, abk, hyeinlee, luw002}@ucsd.edu
http://vlsicad.ucsd.edu/
ECE Department, UC San Diego
Notes: Thank you for the kind introduction. Good afternoon, everyone. The title of my talk is “ILP-based co-optimization of cut-mask layout, dummy fill and timing for sub-14nm BEOL technology”.

## Slide 2: Outline
Motivation & Related Works
Our approach:
  ILP-based cut mask optimization
  Post-ILP optimization
Experimental results
Conclusion and Future work
Notes: In this talk, I will first introduce motivation, previous work
and then describe the cut mask optimization problem.
I will present our key methods, an ILP-based cutmask optimization followed by a post-ILP optimization And then, I will show experimental results and conclude my talk.

## Slide 3: Motivation
Self-aligned multiple patterning (SAxP) + Cut process
  Cut shapes and locations determine dummy wires, end-of-line (EOL) extension of wire segments ⇒ affect performance
Cut mask optimization must understand these effects
We propose a step by step co-optimization with EOL extension and dummy fills
Original layout
dummy fill
Final layout
extension
1D wires
Cut masks
cut
Notes: Self-aligned multiple patterning is the leading option in sub-14nm node. And the final patterns are determined by the cut process. The leftmost cartoon shows the original layout; blue rectangles are wire segments. In this process, 1D wires are patterned first. Then, the wires are cut by red-colored cut shapes. So, the final layout is totally different from the original layout. There are EOL extensions and dummy fills. This will affect timing and performance.
So, the cut shapes and locations must be determined carefully considering these impacts.
In this work, we propose a cutmask co-optimization awaring of these effects.

## Slide 4: Related works
[Zhang11] proposes shortest path-based approach
  Improve the printability of cuts
  No timing-aware optimization
  Unrealistic rules
  [Du12] and [Ding14] propose Integer Linear Programming-based approaches
  Minimize the sum of end-of-line (EOL) extensions
  A hybrid optimization of cut masks and e-beam lithography
  No timing-aware optimization
  No consideration of using multiple cut masks
  No consideration of dummy fills
Our work:
co-optimization of (i) cut mask coloring,
(ii) design timing
and (iii) metal density (dummy fill) considering cut mask layout rules
Notes: Recently, several works have studied cut mask optimization problem. Zhang propose a shortest path algorithm to improve the printability of cuts.
But it is not timing –aware, and it’s not flexible regarding realistic design rules.
Du and Ding propose an ILP-based approach to minimize the sum the EOL extensions in a hybrid optimization of cutmasks and e-beam lithography.
But none of them is timing-aware. They also do not consider multiple coloring and dummy fills.
Our main contribution is the co-optimization of cutmask coloring, design timing and metal/mask density considering cutmask layout rules.

## Slide 5: Outline
Motivation & Related Works
Our approach:
  ILP-based cut mask optimization
  Post-ILP optimization
Experimental results
Conclusion and Future work
Notes: Now, I will describe our ILP-based cutmask optimization approach.

## Slide 6: ILP-based Cut Mask Optimization
Definition
  Minimum cut spacing
Objective:
  Minimize the weighted sum of EOL extensions ⇒ timing impact due to EOL extension
Subject to:
  Minimum cut spacing: e.g.,110nm C2C Euclidean distance
  How we assign cuts to different cut masks (color assignment)
  +more (separating? / merging?)
Metal
Cut Mask 1
Forbidden location
Metal
Cut Mask 1
Forbidden location
Extended Metal
Metal
Cut Mask 1
Forbidden location
Extended Metal
Cut Mask 2
Metal
Cut Mask 1
Forbidden location
Notes: This figure shows the unidirectional routed wire segments.
Some cuts are moved due to the minimum cut spacing rule. And we would like to determine the optimal cut location, to minimize the timing impact due to EOL extension.
Still there are some cuts within minimum spacing. So we need more than one cut mask. Here every color represents a different cut mask. We would like to assign colors because of the minimum cut spacing rule.
We formulate our ILP as to minimize the weighted sum of EOL extensions.
Our ILP considers color assignments,
minimum cut spacing rule,
and cut shape. Here we use 110nm C2C Euclidean distance as the spacing rule. And we can control the cut shape by separating two cuts, or merging them according to our need.

## Slide 7: ILP-based Cut Mask Coloring
+ more constraints
w: weight, e: length of extension
 Minimize weighted sum of EOL extensions
Objective
Subject to
Minimum spacing rule
Color assignment
c: 0-1 indicator for color assignment
x: x-coordinate of cut, G: a big constant
Notes: This slide shows details of our ILP formulation.
The objective is to minimize the weighted sum of EOL extensions.
The weight is assigned by each segment’s timing slack, which we will explain later.
The first constraint handles color assignments. For every color of one cut, there is a binary indicator. So for one cut, only one indicator can be non-zero to indicate an assignment to that cutmask.
For non-mergable cuts, the second constraint enforces the minimum cut spacing rule. In the constraint,
“G” is a big constant. The “G\times” part enforces the minimum cut spacing rule only when two cuts are assigned to the same mask. In this way, we can optimize cut locations without the need to know color assignment in advance.
We add more constraints to control cut shapes and I will just introduce one here.

## Slide 8: More Constraints
Two choices
  Separating by at least minimum spacing
  Merging by vertical alignment
 Add 0-1 variable m to select whether to separate or merge cuts
Metal
Cut Mask 1
Extended Metal
(a) Separating
≥ mins
(b) Merging
Separate or Merge?
m: 0-1 indicator for merging
Set A: Separating
Set B: Merging
Notes: The right figure shows an example of our two choices: separating or merging cuts.
If we choose to separate them, they must be at least minimum spacing away.
Or we can merge them vertically into one cut.
In our formulation, we create two sets of constraints. One is for separation. The other is for merging.
We use a binary variable to select from two sets of constraints. The “G\times” part acts similarly to the previous slide as to auto satisfy the other set of constraints. For details, please see Section 3.1 in the paper.

## Slide 9: Modeling Timing Impact of a Wire Segment
Weights on wire segments are determined based on timing criticality
Timing criticality ⇒ net slack = path slack * (stage delay / path delay)
We sort nets based on net slack, and classify them into different groups
  In our experiment, we have two groups
We assign different weights for different groups
  The weight values are obtained based on experiments
Objective:
Path slack = 10ps
Path delay = 200ps
Gate1 + net1 = 50ps
Gate2 + net2 = 40ps
net1
net2
Gate1
Gate2
Net1 slack = 2.5ps
Net2 slack = 2ps
Notes: This slide shows how we do the weight assignment.
We determine the weight for each wire segment based on timing criticality.
To calculate the timing criticality, we calculate net slack; the slack of a net is calculated using the slack of the most critical timing path passing through the net. We distribute the path slack to all nets in the timing path based on the ratio of stage delay to path delay.
We then classify nets into different groups, based on their slack. In our experiment, we have two groups. We assign different weights for different groups based on our experimental results. Here, we use a weight of two for negative net slack, and a weight of 1 for positive net slack.

## Slide 10: Partitioning-based Distributable Optimization
Limitation of ILP-based approach ⇒ Runtime
Split the post-route layout into small clips
  First iteration: optimize all small clips in parallel
  Second iteration: optimize the regions (shaded) near the horizontal boundaries
  Third iteration: optimize the regions (shaded) near the vertical boundaries
First iteration
Clip #2
Clip #3
Clip #6
Clip #5
Clip #4
Clip #7
Clip #8
Clip #9
Min spacing X 4
Second iteration
Horizontal boundaries
Clip #1
Clip #2
Clip #3
Clip #4
Clip #5
Clip #6
Third iteration
Vertical boundaries
Clip #1
Clip #3
Clip #4
Clip #2
Clip #5
Clip #6
Clip #1
Notes: The biggest limitation of Mixed ILP-based approach is runtime. To enable large-scale optimization,
we split the layout into many clips and optimize each clip in parallel. Our typical clip size is 3um by 3um.
In the first iteration, we optimize within each clip, without considering boundaries.
In the second iteration, we slide each clip in y direction and only solve for the shaded region. We fix all the other solutions we get from the first step, to ensure horizontal boundary feasibility.
Then, we slide each clip in x direction and solve again. By completing the third iteration, we will get a feasible solution with runtime linear to #clips.

## Slide 11: Post-ILP Optimization
Cut mask solution when mask density
d3 < d2 < d1
(c)
Propose a heuristic for further cut mask optimization
  Enlarge/insert cuts near wire segments in the descending order of timing-criticality
  Iterative optimization until the total metal density reaches the minimum metal density
  Consider the mask density uniformity among different colored masks
Metal
Cut Mask 1
Cut Mask 2
Cut Mask 3
Target region
(a)
DefineTargetRegion
EnumCandidateCuts
SelectCuts
ILP Solution
Optimized Solution
ρk ≤ ρmin?
Y
N
Candidate cuts on cut mask 1
≥ mins
≥ mins
≥ mins
≥ mins
Candidate cuts on cut mask 2
Candidate cuts on cut mask 3
≥ mins
≥ mins
(b)
Notes: To improve further,
we propose a heuristic considering metal density, mask density and timing.
Our heuristic could remove dummy fills by inserting and enlarging cuts near wire segments in the descending order of timing-criticality.
And it iteratively optimizes until a lower bound of metal density is reached.
During optimization, mask density uniformity is considered.
An example of the flow is shown here. After we get the solution from the previous step,
In Figure (a), DefineTargetRegion selects a candidate dummy fill to be removed according to timing.
The next step then enumerates all possible cuts for each color. Figure (b) shows them separately. Then we select cuts based on the ascending order of mask density. The final choice is a balanced use of all cutmasks.
We loop this process until the minimum metal density is met.

## Slide 12: Overall Flow
Routed layout
Design rules - Min cut spacing - #Cut masks
ILP solver (CPLEX)
ILP
formulation
Optimization for each window
Solve multiple
windows in parallel
Optimized layout
ρk ≤ ρmin?
Yes
ILP-based cut mask optimization
No
Timing/Density-aware post-ILP optimization
Cut mask optimization (layer by layer)
Notes: This slide shows the overall flow of our framework.
Given a routed design
and design rules,
our ILP-based algorithm
generates a mathematical representation of each clip
and calls a commercial solver to solve each clip in parallel.
In the second step, our timing/density-aware post-ILP optimization continues, until we meet the minimum metal density.

## Slide 13: Outline
Motivation & Related Works
Our approach:
  ILP-based cut mask optimization
  Post-ILP optimization
Experimental results
Conclusion and Future work
Notes: Next, I will present our experiments.

## Slide 14: Experimental Setup: Designs and Technologies
Designs: ARM Cortex M0, AES (aes cipher top)[OpenCores]
Technology
  Option 1 (N7): 7nm cell library with scaled 28nm BEOL (back-end-of-line) LEF
  Option 2 (N5): 5nm (scaled 7nm) cell library with scaled 28nm BEOL (back-end-of-line) LEF
SP&R tools: Synopsys Design Compiler (synthesis), Cadence Encounter (P&R)
Tech. | Design | #cells | #nets | Area (um2) | Util. (%) | #segments |  |  |  | 
 |  |  |  |  |  | M2 | M3 | M4 | M5 | M6
N7 | M0 | 8994 | 9048 | 8272 | 81 | 33311 | 21359 | 10606 | 6306 | 2595
 | AES | 13340 | 13602 | 9807 | 86 | 46034 | 29552 | 16935 | 10453 | 4939
N5 | M0 | 8386 | 8440 | 7778 | 76 | 31881 | 20934 | 10534 | 6194 | 2547
 | AES | 11650 | 11912 | 8596 | 81 | 42819 | 28176 | 16223 | 10480 | 4960
[OpenCores] http://opencores.com/
A1
A0
B0
B1
Y
min M2 pitch of 28nm node
min M1 pitch of 28nm node
Scale by 2.5x
OAI22 in 7nm node
Notes: We evaluate using two designs, ARM Cortex M0 and the encryption and decryption module from OpenCores, called AES.
For technology, we choose to use a 7nm library with a scaled 28nm BEOL. (We choose the scaling factors based on ……). We also project to a 5nm foundry node by further scaling.
The SP&R tools we use are Synopsys DC and Cadence Encounter. SP&R results are shown here in the table.

## Slide 15: Experimental Setup: Design of Experiments
Experiment 1: impact of number of cut masks
  Options C1 to C12 for #cut masks
  Technology N7
  Minimum cut spacing: 4 X minimum M2 pitch
  Minimum track occupancy: 80%
Experiment 2: impact of minimum metal density (track occupancy)
  Minimum track occupancy (80%, 85% 90%) with default setup
  Technology N7
  Minimum cut spacing: 4 X minimum M2 pitch
  Option C5 for #cut masks
Experiment 3: impact of minimum cut spacing
  Technology N7 (min cut spacing: 4 X minimum M2 pitch) Technology N5 (min cut spacing: 5 X minimum M2 pitch)
  Minimum track occupancy: 80%
Options for #cut masks | #cut masks for M2 – M6
C1 | 2, 1, 1, 1, 1
C2 | 3, 2, 1, 1, 1
C3 | 3, 2, 2, 1, 1
C4 | 3, 2, 2, 2, 1
C5 | 3, 2, 2, 2, 2
C6 | 4, 2, 2, 2, 2
C7 | 4, 3, 2, 2, 2
C8 | 4, 3, 3, 2, 2
C9 | 4, 3, 3, 3, 2
C10 | 4, 3, 3, 3, 3
C11 | 5, 4, 4, 4, 4
C12 | 10, 10, 10, 10, 10
Notes: We perform three types of experiments on M2 to M6
The first is to investigate the impact of the number of cutmasks. We experiment with 12 different color options, from 1 cutmask to 10 masks. We use a N7 library with a minimum cut spacing of 4 M2 pitches. The minimum metal density is 80%.
The second is to show the impact of the minimum metal density. For unidirectional designs, we could simply focus on track occupancy. We use the same library and spacing rules here. Color options C5 is used. That is three cutmasks for Metal 2, and 2 cutmasks for M3 to M6.
The third experiment shows the impact of the minimum spacing rule as the technology continues scaling. We add a N5 technology. 5x M2 pitch is used as minimum cut spacing for N5.

## Slide 16: Experiment 1: Impact of #Cut Masks
Chart: #Cut masks vs Infeasible clips (%)
| C1 | C2 | C3 | C4 | C5 | C6 | C7 | C8 | C9 | C10 | C11 | C12
ARM Cortex M0 | 20.744 | 7.266 | 1.869 | 0.484 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
AES | 31.263 | 14.429 | 4.983 | 1.436 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
For Cortex M0 and AES
  One mask is not enough for a layer
  C5 (3,2,2,2,2) gives sufficient #cut masks
Options for #cut masks | #cut masks for M2 – M6
C1 | 2, 1, 1, 1, 1
C2 | 3, 2, 1, 1, 1
C3 | 3, 2, 2, 1, 1
C4 | 3, 2, 2, 2, 1
Notes: This slide shows the feasibility with the number of cutmasks. X-axis gives all 12 testcases. Y-axis shows the percentage of infeasible clips.
Testcase C1 to C4 have only one cutmask for some layers, and for all three designs, they all have infeasible clips.
So in N7, one mask for a layer is not enough.
Here, C5, with three cutmasks for M2 and two cutmasks for the others, is the least option to ensure feasibility.

## Slide 17: Experiment 1: Impact of #Cut Masks
#Cut masks ↑  EOL extension (%) ↓
(= extended wirelength/original wirelength x 100)
C5C6 saves 2% for AES (2040µm) and 1% for Cortex M0 (1034µm)
Chart: Overall % EOL extension
| C5 | C6 | C7 | C8 | C9 | C10 | C11 | C12
ARM Cortex M0 | 0.032577 | 0.018642 | 0.0082323 | 0.005576 | 0.0049262 | 0.0048308 | 0.00050284 | 0
AES | 0.045527 | 0.026439 | 0.013995 | 0.0094001 | 0.008125 | 0.0079571 | 0.00078674 | 0

## Slide 18: Experiment 1: Impact of #Stages on Critical Path
Results for Cortex M0 and AES
  % EOL extension of Cortex M0 is always lower than AES
  Worst negative slack (WNS) of Cortex M0 is more impacted by EOL extension and dummy fill than AES
  Change in WNS of Cortex M0 is up to 23ps worse than that of AES
  The accumulative effect of the added stage delay
Chart: Change in WNS due to EOL and dummy fill
| C5 | C6 | C7 | C8 | C9 | C10 | C11 | C12
ARM Cortex M0 | -0.056 | -0.052 | -0.05 | -0.043 | -0.043 | -0.042 | -0.042 | -0.041
AES | -0.033 | -0.036 | -0.034 | -0.032 | -0.032 | -0.032 | -0.032 | -0.031
Design | #stages
M0 | 50
AES | 8
Chart: Overall % EOL extension
| C5 | C6 | C7 | C8 | C9 | C10 | C11 | C12
ARM Cortex M0 | 0.032577 | 0.018642 | 0.0082323 | 0.005576 | 0.0049262 | 0.0048308 | 0.00050284 | 0
AES | 0.045527 | 0.026439 | 0.013995 | 0.0094001 | 0.008125 | 0.0079571 | 0.00078674 | 0
Notes: Next, we could find something interesting about # stages.
% EOL extension for AES is always higher than Cortex M0.
But for WNS, AES is less impacted by up to 30ps.
From the report by Encounter, Cortex M0 has a maximum of 50 stages, while AES has only 8 stages. So this may be caused by the accumulative effect of the added stage delay. More stages simply accumulate the impact.

## Slide 19: Experiment 2: Impact of Minimum Track Occupancy
Post-ILP optimization is beneficial to timing
  Different track occupancy with up to 22ps difference
Chart: Change in WNS for different minimum track occupancy
| ARM Cortex M0 | AES
80% | -0.041 | -0.031
85% | -0.05 | -0.036
90% | -0.059 | -0.053
18ps
22ps
Notes: The next experiment shows the WNS with different minimum metal density.
We have tested three densities 80%, 85% and 90% to show our post-ILP optimization is really beneficial.
For JPEG design, we see more than 100 ps improvement just by decreasing the metal density.
We also compare our results with Encounter metal fill and our’s performance is about on par with them.
Additionally, we consider multiple coloring for the mask.

## Slide 20: Experiment 3: Impact of Minimum Cut Spacing
N5 is more sensitive to #cut masks
  Wire delay is more dominant than the gate delay
  Wire resistance increase is greater than the wire capacitance decrease per unit length
Chart: #Cut masks vs WNS
| Base #Color | Base+1 | Base+2
ARM Cortex M0 N7 | -0.056 | -0.042 | -0.042
ARM Cortex M0 N5 | -0.054 | -0.043 | -0.037
AES N7 | -0.033 | -0.032 | -0.032
AES N5 | -0.039 | -0.037 | -0.028
17ps
11ps
Notes: This experiment evaluates the impact of minimum spacing rule when we project to N5 foundry node. We first find out the minimum color option for each node, and then investigate the performance change if we add one more mask for each layer, or two more masks for each layer.
It turns out N5 is more sensitive to the number of cutmasks.

## Slide 21: Outline
Motivation & Related Works
Our approach:
  ILP-based cut mask optimization
  Post-ILP optimization
Experimental results
Conclusion and Future work
Notes: In this talk, I will first introduce motivation, previous work
and then describe the cut mask optimization problem.
I will present our key methods, an ILP-based cutmask optimization followed by a post-ILP optimization And then, I will show experimental results and conclude my talk.

## Slide 22: Conclusion
ILP-based cut mask optimization
  Minimize the weighted sum of extensions considering color assignment and cut mask layout rules
Timing/Density-aware post-ILP optimization
  Further cut mask optimization that is aware of timing, minimum metal density and mask density uniformity
Experiments in varying contexts give insight into the tradeoff of performance and cost
Follow-up works:
  Use more precise weight assignment in ILP
  Comparison of the best choice of single cuts vs. the worst/random choice
  ECO route for infeasible routing clips to reduce the mask cost
  Co-optimization of routing and cut mask
Notes: In this work, we address the co-optimization of cut mask layout, dummy fill, and timing.
We contributes an ILP-based cutmask optimization to minimize the weighted sum of extensions considering coloring and cutmask layout rules.
Also, we propose a timing/density-aware post-ILP optimization aware of timing, minimum metal density and mask density uniformity.
Our various experiments give insight into the trade off between performance and cost. We also project our work to N5 foundry node.
About future works, we could use more precise weight assignment in ILP. We could also incorporate ECO routing for infeasible clips to reduce the mask cost, as well as to co-optimize cutmask with routing,
Thank you.

## Slide 23: Thank you