## Slide 1: Improved Performance of 3DIC Implementations Through Inherent Awareness of Mix-and-Match Die Stacking
Kwangsoo Han, Andrew B. Kahng and Jiajia Li
University of California at San Diego
http://vlsicad.ucsd.edu/

## Slide 2: Mix-and-Match Integration
Interesting idea proposed by previous works
Integrate slow copies of tiers with fast copies of tiers to improve 3DIC parametric yield == “Mix-and-match” integration
Wafer-to-wafer (die-to-wafer) bonding: integrate SS wafer/die with FF wafer/die (SS Tier 0 wafer/die + FF Tier 1 wafer or FF Tier 0 wafer/die + SS Tier 1 wafer)
Slow Tier 0
Fast Tier 1
Monolithic 3D: adapt process so that Tier 1 is fast if Tier 0 is known to be slow
3D integration
SS Tier 1 wafer/die
FF Tier 0 wafer

## Slide 3: Agenda
Motivation
Related Works
Our Methodology
Experimental Results
Conclusions

## Slide 4: Mix-and-Match Needs Design-Stage Optimization
Mix-and-match integration offers performance benefits over the conventional worst-case analysis
No holistic “design for eventual integration” of 3DICs
  With mix-and-match integration, blue cut has maximum slack, red cut has minimum slack
  Our goal: Study design-stage optimization for mix-and-match
Chart: WNS (ps)
| SS-SS | SS-FF | FF-SS
WNS (ps) | -155 | -80 | -46
75ps
XX-YY = XX Tier 0 + YY Tier 1
Technology: 28FDSOI
3D netlist is bipartitioned with minimum net cut
SS (FF)
FF (SS)
Bad setup and hold slacks
SS (FF)
FF (SS)
Benefit from mix-and-match

## Slide 5: Challenges in Mix-and-Match-Aware Partitioning
Examples with different optimal solutions for different objectives
Assumption: (i) Uniform stage delay (dSS = 30ps, dFF = 10ps) (ii) PathAC: 26 stages, PathBC: 30 stages (iii) Balance criteria: 50% for each die
Objective: (i) Minimize delay of PathAC
(ii) Minimize delay of PathBC
(iii) Minimize worst-case delay over the two paths
(iv) Minimize worst-case delay over the two paths in regime of large VI delay impact (dVI)
20
6
10
A
B
C
dVI = 10ps
Tier 1
Tier 0
DAC = 530ps DBC = 680ps
13
7
5
5
DAC = 640ps DBC = 610ps
15
3
5
3
14
3
6
9
3
1
DAC = 620ps DBC = 620ps
dVI = 60ps
DAC = 680ps DBC = 720ps
18
2

## Slide 6: Challenges in Mix-and-Match-Aware Partitioning
Optimal cut location on one path conflicts with those on other paths
  Example has different optimal solutions for different objectives
Vertical interconnect (VI) delay impact
Asymmetric path delay distribution due to process variation

## Slide 7: Agenda
Motivation
Related Works
Our Methodology
Experimental Results
Conclusions

## Slide 8: Related Works
Mix-and-match die stacking
[Ferri08] integrates fast (slow) CPU die with slow (fast) L2 cache die to improve parametric yield
[Garg13] formulates mathematical programming to optimize mix-and-match stacking
[Chan13] uses mix-and-match stacking to optimize reliability of 3DICs
[Juan14] performs thermal-aware matching and stacking
But no design-stage optimization has been studied
Netlist partitioning for 3DICs
[Li06] uses simulated annealing engine to partition block into tiers
[Thorolfsson10] uses hMetis to partition netlist with minimized #VIs
[Hu10] proposes a multi-level framework for 3D partitioning
[Cong07][Panth15] assign cells to tiers through transformations of a 2D placement
These do not comprehend mix-and-match die stacking

## Slide 9: Agenda
Motivation
Related Works
Our Methodology
Experimental Results
Conclusions

## Slide 10: ILP-Based Partitioning Method
ILP formulation
  Minimize Dmax // Minimize max path delay in regime of mix-and-match
  Such that βi, i’ ≥ xi - xi’ // indicators of VI insertions βi, i’ ≥ xi’ - xi for all adjacent cells
  Delay bound ∑(dij∙(1-xi) + dij’∙xi) + ∑ βi, i’∙dVI ≤ Dmax for all paths
  Area-balancing criterion ∑ ai∙xi - ∑ai∙(1-xi) ≤ α∙∑ai ∑ ai∙(1-xi) - ∑ai∙xi ≤ α∙∑ai
Notations
  Dmax maximum path delay
  xi binary indicator of cell on Tier 0 (xi = 0) or Tier 1 (xi = 1)
  βi, i’ binary indicator of whether a VI (cut) exists
  dij cell delay at jth process corner
  dVI delay impact of VI insertion
  ai cell area
  α area-balancing criterion (e.g., α = 5%)

## Slide 11: Heuristic Partitioning Method (1)
Maximum-cut on timing-critical sequential graph
  Classify paths according to their slacks and VI delay impact Type-I Timing non-critical paths Type-II Timing-critical paths without tolerance of VI insertion  Impact of VI insertion ≥ timing benefit from mix-and-match Type-III Timing-critical paths with tolerance of VI insertion  Impact of VI insertion < timing benefit from mix-and-match
  Extract restricted sequential graph containing only Type-II/Type-III paths
  Collapse vertices connected with Type-II paths into one vertex
  Perform maximum cut on updated graph

## Slide 12: Heuristic Partitioning Method (2)
Timing-aware multi-phase FM partitioning
  Issue: Hard to “foresee” slack benefits with existence of VI delay impact
  Our solution: Cluster cells with given range of cluster size
Moving one cell degrades slack, but following moves compensate VI delay impact
Clustering with cluster size [L2, U2]
Clustering with cluster size [L2, U2]
Clustering with cluster size [Lk, Uk]
Timing-aware FM
Timing-aware FM
Timing-aware FM
…
Partitioning solution
Partitioning solution with maximum slack
One phase

## Slide 13: Agenda
Motivation
Related Works
Our Methodology
Experimental Results
Conclusions

## Slide 14: Design of Experiments
Testcases: ARM Cortex M0 and DMA, AES, VGA from OpenCores website
Technology: 28FDSOI, dual-VT
Tools
  ILP solver: CPLEX v12.5
  Synthesis: Synopsys Design Compiler H-2013.03-SP3
  P&R: Cadence EDI System v12.0
  Signoff timer: Synopsys PrimeTime H-2013.06-SP2
Two sets of experiments
  Validation of our heuristic partitioning method
  Extend existing 3DIC implementation flows with our optimization

## Slide 15: Calibration of Heuristic Partitioning
ILP-based optimization leads to near-optimal solution
Vary delay impact of VI insertion, process corners
Heuristic consistently achieves < 30ps slack difference compared to ILP-based partitioning solution
Chart: WNS (ps)
| 10 | 30 | 50 | 10 | 30 | 50 | 10 | 30 | 50
ILP | 52 | 33 | -2 | 88 | 57 | 45 | 49 | 25 | -10
Heuristic | 51 | 6 | -31 | 85 | 39 | 4 | 47 | 6 | -29
3σ SS + 3σ FF 2σ SS + 3σ FF 3σ SS + 2σ FF
dVI (ps) 10 30 50 10 30 50 10 30 50
Design | Clk period
DMA | 0.6ns

## Slide 16: Validation of Our Method
Extend two existing 3DIC implementation flows (i) GT2012, and (ii) Shrunk2D to include our partitioning method for mix-and-match
Up to 16% performance improvement
Chart: WNS (ps)
| ARM M0 | AES | VGA
Brute-force (orig) | -178 | -181 | -244
Brute-force (opt) | -23 | -8 | -80
Shrunk2D (orig) | -89 | -4 | -47
Shrunk2D (opt) | -13 | 56 | 11
Design | Clk period
M0 | 1.2ns
AES | 1.1ns
VGA | 1.0ns
GT2012 (opt)
GT2012 (orig)

## Slide 17: Agenda
Motivation
Related Works
Our Methodology
Experimental Results
Conclusions

## Slide 18: Futures and Conclusions
Design-stage optimization for mix-and-match die stacking
ILP-based and heuristic partitioning methodologies directly maximize design’s slack in the regime of mix-and-match
Up to 16% timing improvement compared to conventional 3D partitioning solution
Future works
  Integration of design-stage and die- and/or wafer-level optimization
  Clock tree synthesis for mix-and-match stacking

## Slide 19: THANK YOU !