## Slide 1: Floorplan and Placement Methodology for Improved Energy Reduction in Stacked Power-Domain Design
Kristof Blutman† , Hamed Fatemi† , Andrew B. Kahng‡, Ajay Kapoor† , Jiajia Li‡ and Jose Pineda de Gyvez† ‡UC San Diego, †NXP Semiconductors

## Slide 2: Outline
Background and Motivation
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 3: Stacked Power-Domain Design
Battery lifetime is critical to IC designs (e.g., IoT, mobile)
  Misalignment between battery and core voltages  Energy inefficiency in voltage regulator
Improve power delivery efficiency  Battery lifetime ↑
Stacked power-domain design connects two domains with balanced currents in series  Aligned voltages between battery and core (Example: battery voltage = 2V, voltage of each domain = 1V)  Recycling of current between two domains
…
…
…
…
…
…
VR
…
…
…
…
…
…
Top domain
Bottom domain
2VDD
VDD
VSS
Conventional design
Stacked-domain design
VDD
VSS
VR

## Slide 4: Motivation
Battery lifetime: Conventional vs. Stacked-domain designs
Conventional design,
Pbattery_c = Pcore / η
Stacked-domain design,
Pbattery_s = Pstack + PVR / η
Assume same power consumption, i.e.
Pcore = Pstack + PVR
Battery lifetime ratio,
Ts / Tc = Pbattery_c / Pbattery_s = (2 ∙ Istack + IVR) / (2 ∙ η ∙Istack + IVR)
If current is perfectly balanced (IVR = 0), stacked domain provides
  1.25X battery lifetime compared to conventional design, if η = 80%
  2X battery lifetime compared to conventional design, if η = 50%
  Pbattery_c : Battery supply power to conventional design
  Pcore : Total power consumption of core
  η : Voltage regulator efficiency
  Pbattery_s : Supply power to stacked-domain design
  Pstack : Direct power of stacked domain from supply
  PVR : Input power of voltage regulator from supply
  Ts : Battery lifetime of stacked-domain design
  Tc : Battery lifetime of conventional design
  Istack / IVR : Currents corresponding to Pstack and PVR

## Slide 5: Problem Formulation
Given: Netlist, timing constraints, level shifter, voltage regulator efficiency, and power information
Do: Partition netlist into two domains, define layout region of each domain, and place instances and level shifters
Objective: Maximize battery lifetime
Consideration:
Balance current across multiple operating scenarios
Region generation = Constrained layout
Level shifter  Power, area, timing penalties

## Slide 6: Outline
Background and Motivation
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 7: Related Works
Stacked-domain implementation
[Cabe10][Liu13] focus on specific designs (memory, IO)
[Lee15] partition cores (with no connection) into domains
[Blutman16] partition logic and memory into two domains
No fully automated, general flow for stacked-domain design
Netlist partitioning
Move-based partitioning: KL, FM and many extensions
Mathematical programming: [Shih93][Goemans95]
Flow-based approach: [Yang96][Caldwell00]
Do not directly apply to stacked-domain partitioning
Our work: flow-based partitioning with multiple extensions for general stacked-domain partitioning

## Slide 8: Outline
Background and Motivation
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 9: Overall Optimization Flow
Trial placement
: Estimate post-placement timing / current profile
Flow-based partitioning
: Aware of layout, timing, multi-scenario current balancing
Domain region definition
: One continuous region for each domain + minimized boundary length
Re-floorplanning
: Resize floorplan (if necessary) + power planning
Level shifter insertion
: Minimize wirelength penalty
Placement optimization
: Placement legalization + incremental timing fix

## Slide 10: Example of Overall Flow
Flow-based partitioning
(blue = bottom domain,
red = top domain)
Domain region definition
(blue region = bottom domain,
red region = top domain)
Re-floorplanning + level shifter insertion
(yellow = level shifters)
Design: AES (11K instances)
Technology: 28LP

## Slide 11: Flow-Based Partitioning
Current-balanced partitioning with minimized #cuts
Basic flow
  Construct flow-network (cell / cluster  vertex, net  edge, current of cell / cluster  weight)
  Perform max-flow optimization (Ford–Fulkerson)
  Cluster smaller partition together with one neighbor vertex
  Iterate Steps 2, 3 until the balancing constraint is satisfied
a
c
e
f
d
b
a
c
e
f
d
b
c
a, e
f
d
b
c
a, e, f
d
b
a and b are source and sink
All vertices have same weight

## Slide 12: Extensions to Flow-Based Partitioning
Pre-clustering
  Reduce runtime and improve scalability
  Heavy-edge matching (HEM) to cluster cells with dense connections
Multiple operating scenarios
  Balance current between two domains across different scenarios (e.g., function mode and sleep mode)
  Use weighted sum of normalized currents
Critical-path awareness
  Remove V-shaped vertices after each max-flow opt
Layout awareness
  Detect and remove outliers (= instances from large-current partition, but located within small-current region) after each max-flow opt
HEM example
AES, 28LP
Top
Bottom
V-shaped vertices

## Slide 13: Region Definition
Separated regions for each power domain increase complexity for PDN (power delivery network) design  Want one continuous region for each power domain
  Uniformly divide block area into grids
  Define outliers and neighbors Outlier: Grid outside the largest continuous region of the same domain Neighbor: Grid adjacent to the largest continuous region of a different domain
  Calculate cost to swap pairs of (outlier, neighbor) Cost = HPWL (half-perimeter wirelength) increase due to the swap
  Select the pair with minimum cost to swap
  Iterate Steps 2-4 until there is no outlier
Initial placement
Yellow = outliers
Green = neighbors
Post-optimization placement

## Slide 14: DP-Based Boundary Optimization
Gap area must be inserted along the boundary between two domains  Want to minimize the boundary length
Dynamic programming-based optimization
  Constraints = (1) area of each domain remains same, (2) moved instance area should be restricted
  Objective = minimize boundary length
  Index turning points from left to right, then DP formulation is Sol(j) = Min(Sol(i).length + seg(i, j).length), for all i < j
Optimized segment (1, j)
Optimized segment (1, i)
Simplified segment (i, j)
Initial boundary
Optimized boundary

## Slide 15: Level Shifter Insertion
Resize floorplan for space of level shifter insertion
  Preserve trial placement solution
Perform matching-based optimization to insert level shifters  Minimize wirelength penalty
  Enumerate candidate locations between two domains
  Cost = HPWL increase to place particular level shifter at a candidate location
Re-floorplan + level shifter insertion
(red = top domain, blue = bottom domain, yellow = level shifters)

## Slide 16: Outline
Background and Motivation
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 17: Experimental Setup
(mA)
Designs
  Four blocks from OpenCores website in 28nm LP AES (11K), DES (17K), JPEG (42K), VGA (58K)
  Dual-core M4 (113K) industrial design in 40nm
Tools (for OpenCores designs)
  Synthesis: Synopsys Design Compiler vH-2013.12-SP3
  P&R: Cadence Innovus Implementation System v16.1
  Power/timing analysis: Cadence Innovus Implementation System v16.1
Power efficiency of voltage regulators
  Efficiency reduces with smaller current

## Slide 18: Battery Lifetime Improvement
Stacked domain achieve > 10% and 3X battery lifetime improvement in function and sleep modes
Currents are well balanced in both modes
Larger benefits in sleep mode is due to small regulator efficiency
Chart: Design
| AES | DES | JPEG | VGA | M4
Sleep | 4.19 | 5.16 | 2.39 | 1.81 | 3.7
Chart: 
| AES | DES | JPEG | VGA | M4
Func | 1.13 | 1.16 | 1.16 | 1.12 | 1.11
Normalized battery lifetime
Design | #LSs | Currents (func) | Currents (sleep)
AES | 166 | 4.83/5.04 | 0.05/0.04
DES | 135 | 8.83/8.87 | 0.04/0.03
JPEG | 673 | 19.43/23.39 | 0.16/0.16
VGA | 520 | 28.69/32.65 | 0.20/0.17
M4 | 477 | 2.74/3.92 | 0.75/0.77
Sleep mode
Function mode
(top/bottom) domain current unit: mA

## Slide 19: Sensitivity to Level Shifter Cost
Use pessimistic level shifter model with ~ 3X power, area and delay increase
Both delta current and total power increase due to power and delay overheads of level shifters
Optimization minimizes #LSs  Overheads are not large
Chart: 
| Default | Pess
ΔI | 1.1924 | 1.2624
Chart: 
| Default | Pess
Pcore | 7.33 | 7.46
Chart: 
| Default | Pess
ΔI | 1.6 | 1.8332
Chart: 
| Default | Pess
Pcore | 0.16786 | 0.16815
ΔI (mA)
Total power (mW)
ΔI (μA)
Total power (mW)
Function mode
Sleep mode
Design: M4
Technology: 40nm

## Slide 20: Sensitivity to Voltage Regulator Power Efficiency
Better regulator efficiency  Smaller battery lifetime benefits from stacked domain
Sleep mode
Function mode
(mA)

## Slide 21: Outline
Background and Motivation
Related Work
Our Methodology
Experimental Setup and Results
Conclusion

## Slide 22: Conclusion
First comprehensive framework for stacked-domain optimization
Extend flow-based partitioning with layout, timing-path awareness, and multi-scenario balancing
More than 10% and 3X battery lifetime improvement compared to conventional designs in function and sleep modes
Ongoing / Future works
  Predictive methodology to determine block size
  Optimization with > 2 domains and/or in 3DICs

## Slide 23: Thank you!