## Slide 1: Power Delivery Pathfinding for Emerging Die-to-Wafer Integration Technology
Andrew B. Kahng1,2, Seokhyeong Kang3, Seungwon Kim4, Kambiz Samadi5 and Bangqi Xu2
1CSE and 2ECE Departments, UC San Diego, La Jolla, CA, USA
3EE Department, POSTECH, South Korea
4EE Department, UNIST, South Korea
5Qualcomm Technologies, Inc., San Diego, CA, USA
Notes: Good afternoon, everyone. Today I’ll present our work on power delivery pathfinding for emerging die-to-wafer integration technology.
This work is in collaboration with UCSD and Qualcomm.

## Slide 2: Outline
Background and Motivation
Problem Statement
Our Methodologies
Experimental Setup and Results
Conclusion
Notes: This is outline of our work.

## Slide 3: Outline
Background and Motivation
  3D Integration: Die-to-wafer stacking
  Power Delivery Network: Motivation
Problem Statement
Our Methodologies
Experimental Setup and Results
Conclusion
Notes: I’ll first introduce background and motivation of our work.

## Slide 4: 3D Integration: Die-to-wafer stacking
Same area constraint for top and bottom dies
Lack of commercial EDA support
“WoW”: Wafer-on-Wafer
“D2W”: Die-to-Wafer
High yield & flexibility
  - Known good die
  - Good overlay
Heterogeneity
  - Different technologies
Notes: A process node length becomes below 10-nanometers, 3D integration technology has been receiving attention to improve power, performance, area and cost.
However, conventional packaging-driven 3D IC stacking method by Through-Silicon-Vias is not sufficient for high integration density.
It is because of the large size and pitch of the TSV.
More recently, several foundry-driven 3D integration techniques has introduced.
Especially, the die-to-wafer stacking technology is emerging with pros such as high yield, flexibility with reuse known good die and good overlay, and heterogeneity.

## Slide 5: Power Delivery Network: Motivation
nearly-optimal PDN
signal VIs
dense PDN
at higher layer
sparse PDN
at higher layer
iteration & high design space
3D IC – conventional
(bottom tier)
...
...
3D IC – pathfinding
(bottom tier)
One-pass flow
Best routability while
High congestion
Determining a high-quality PDN in 3D IC is challenging
Notes: In the 3D IC, we can maximize the benefits by increasing the number of vertical interconnections between die to die.
But many number of inter-tier vertical interconnects make PDN design more difficult.
As you can see in this figure, there are huge design space of PDN with VIs.
However, [click] conventional PDN design flow includes a lot of iterations for searching good enough PDN.
Thus, [click] accurate design space exploration, also known as pathfinding methodology is required to find optimal PDN quickly.
We can say the pathfinding flow that finds nearly-optimal PDN with best routing capacity while satisfying IR drop limit without iterations.

## Slide 6: Power Delivery Network: Motivation
There are vast number of PDN candidates
However, design-specific PDN choices at the “Pareto frontier” of IR drop vs. routability are not addressed even in 2D ICs
Chart: Worst IR drop
Tradeoff borderline
PDN candidates
Worse
Better
Manually designed PDN
Notes: There are many number of PDN candidates in design space,
Human designer can finds quite good PDN manually, but we do not even really know how much of this ‘quite good PDN' is optimized in design space.
Moreover, there is tradeoff between IR drop and routability in a PDN.
So, choice of design-specific PDN at the Pareto frontier like this figure is challenging.

## Slide 7: Outline
Background and Motivation
Problem Statement
Our Methodologies
Experimental Setup and Results
Conclusion
Notes: Now I will introduce problem statement of power delivery pathfinding problem.

## Slide 8: Problem Statement
Power Delivery ‘Pathfinding’ Problem
Given
  a placed circuit design with known cell
  VI locations and BEOL stack
Determine
  PDN with best routability
Constraints
  worst IR (WIR) drop and technology
Notes: We define problem statement as follows.
With given a placed circuit design with known cell library, VI locations and BEOL stack.
We should determine PDN with best routability while satisfying worst IR drop limit and design rules.

## Slide 9: Outline
Background and Motivation
Problem Statement
Our Methodologies
  How to represent “routability” of BEOL?
  Power Delivery Pathfinding Flow
  WIR & Routability Modeling
Experimental Setup and Results
Conclusion
Notes: This section includes details of our pathfinding,
but Before I explain our methodology, I will first introduce how to represent routability of BEOL.

## Slide 10: How to represent “routability” of BEOL?
[Kahng18] gives a methodology to rank BEOL stack options according to an intrinsic routing capacity
“”, maximum cell swap count before exceeding a pre-defined design rule violation (DRV) threshold
Mesh-like placement is used to train the model of PDN routability with measured by random neighboring cell swap
Notes: So far, there has been no metric expressing the routability of BEOLs including PDNs.
Recently, a method to define an intrinsic routing capacity of BEOL stack has proposed.
They have proposed a novel metric ‘K’ and ‘K-threshold’.
The K-threshold is represent routability.
It is because this K-threshold value is maximum cell swap count before exceeding a pre-defined design rule violation threshold.
Therefore larger K-threshold represent better routability of BEOL.
We can find K-threshold with mesh-like placement.
The mesh-like placement is a placed netlist with same standard cell and simple interconnection.
The mesh-like placement is used to train the model of PDN routability with measure K-threshold by random neighboring cell swap.
As you can see in below figure, routing difficulty is gradually increased with random cell swap.
So, routability of a specific PDN can be defined as K-threshold with this flow.

## Slide 11: Power Delivery Pathfinding Flow
Circuit design-independent knobs |  | 
Metal stripe width (w) | Metal stripe set-to-set pitch (p) | Metal stripe space (s)
Model-based PDN pathfinding flow which gives the optimal PDN design considering both IR drop requirement and routability requirement
Notes: This is our power delivery pathfinding flow.
We can make many number of PDNs with a given design-independent knobs.
[click] circuit design-independent knobs, such as metal stripe width, pitch and space of PDN structure should be determined by pathfinding flow.
So we can pick some number of PDNs with design-independent knobs, than we trains the IR drop model and routability model with mesh-like placement.
Then we can find nearly-optimal PDN with trained IR drop and routability model according to design parameter.

## Slide 12: WIR & Routability Modeling
Static IR analysis to collect WIR data
Routability as with mesh-like placement with VIs
To compare the routability ranking of PDNs, we use Spearman’s rank correlation coefficient
Spearman’s correlation coefficient: ,
if
Where = Rank of X and Y
Hybrid Surrogate Worst IR drop Model
Hybrid Surrogate Routability Model
Multivariable linear regression
MARS
RedHawk Static IR Analysis
Routability Analysis
PDNi
PDNi
PDNi
PDNi
Worst IR Dropi
PDNi
PDNi
PDNi
PDNi
K-thresholdi
Dataset
Dataset
PDNi
PDNi
PDNi
PDNi
PDNi
PDNi
PDNi
PDNi
PDNi
PDNi
WIR model
Routability model
Notes: We use commercial EDA tools such as ANSYS RedHawk and Cadence Innovus to train worst IR drop and routability model.
We can make PDN dataset with circuit-independent knobs, then IR drop and routabiliy analysis be performed.
In the routability case, we use the mesh-like placement to train.
For WIR model, we use uniform power consumption.
Especially, we use Spearman’s rank correlation coefficient to compare the routability ranking between estimated K-threshold with model and actual K-threshold with EDA tool.
It is because relative ranking is more important than the absolute value of K-threshold to compare PDN’s routability.
Spearman’s coefficient effectively describe correlation between two rank ordered groups.
So we determine accurate hybrid surrogate routability model which has more strong correlation of ranking.

## Slide 13: Outline
Background and Motivation
Problem Statement
Our Methodologies
Experimental Setup and Results
  Scalability Study
  Sensitivity Study: VI density
  IR drop & Routability Model
  Verification on Real Design
Conclusion
Notes: Now I will talk about our experimental setup and results to verify our pathfinding flow.

## Slide 14: Experimental Setup
We use 8-track cells in 28nm technology
For each model, we use 67% for training and the 33% for testing of the overall dataset (overall 256 #PDNs)
MARS implementation in Python3 from the Py-earth package
Reference PDN design |  |  |  | 
Metal layer | Direction | Width (um) | Spacing (um) | Pitch (um)
M2 | H | Standard cell power rails |  | 
M3 | V | 0.4 | 10 | 20
M4 | H | 0.4 | 0.8 | 12
B1 (M7) | V | 8.0 | 16.0 | 60
B2 (M8) | H | 10.0 | 20.0 | 70
Circuit design |  |  |  | 
#Insts | 25000 |  |  | 
Utilization | 0.7 |  |  | 
VI density | 0.05 |  |  | 
Notes: We use 8-track cells in FDSOI 28nm technology.
For each model, we use 67% for training set and the 33% for testing set of the overall dataset.
And MARS regression model implementation in Python3 from the Py-earth package.
The table is specification of reference PDN structure. we vary M2 to B2, and M3, 4, B1 and B2 to find optimal PDN.

## Slide 15: Scalability Study
Sweep all design-independent knobs
24 #PDNs with 75(small)% - 175(big)%
#instances does not change routability rank ordering of PDNs
Thus, we fix #insts = 25K for the reference design
Chart: #instances
| 25000 | 50000 | 75000 | 100000
pM3_small | 23 | 15 | 14.5 | 13.5
pM3_big | 23.5 | 15 | 14.5 | 14
pM4_small | 23 | 14.5 | 14 | 13.5
pM4_big | 24.5 | 15.5 | 15 | 14
pM7_small | 23 | 15 | 14.5 | 13.5
pM7_big | 24 | 15 | 14.5 | 14
pM8_small | 23 | 14.5 | 14.5 | 13.5
pM8_big | 23.5 | 15 | 14.5 | 14
sM3_small | 23.5 | 15 | 14.5 | 14
sM3_big | 23.5 | 15 | 14.5 | 13.5
sM4_small | 23.5 | 15 | 14.5 | 14
sM4_big | 23.5 | 15 | 14.5 | 14
25K 50K 75K 100K
BEOL routability ranking is maintained!
Notes: First we analyze scalability of our flow.
We sweep all design-independent knobs to make 24 #PDNs and get K-threshold value of each PDNs.
Although there are duplicate K-threshold values, there is no change of routability ranking of PDNs.
Thus, small design is sufficient to use our pathfinding flow for the reference design.

## Slide 16: Sensitivity Study: VI density
Target VI density | #VIs | VI density
0.025 | 684 | 0.027
0.05 | 1242 | 0.049
0.075 | 2052 | 0.082
0.01 | 2736 | 0.011
0.025 | 6266 | 0.025
Chart: (b) Sensitivity of metal pitch
| 2.6666666666666668E-2 | 0.02 | 1.6E-2 | 1.3333333333333334E-2 | 1.1428571428571429E-2
Lowest_layer_2.5% | 23.5 | 23.5 | 24 | 24 | 24
Lowest_layer_7.5% | 23.5 | 23.5 | 23.5 | 23.5 | 23.5
Lowest_layer_10% | 23 | 23 | 23.5 | 23.5 | 23.5
Lowest_layer_25% | 21.5 | 22 | 22 | 22 | 22
Highest_layer_2.5% | 23 | 23.5 | 24 | 24 | 24
Highest_layer_7.5% | 23 | 23.5 | 23.5 | 23.5 | 23.5
Highest_layer_10% | 22.5 | 23 | 23.5 | 23.5 | 23.5
Highest_layer_25% | 0 | 22 | 22.5 | 22 | 22
Chart: (a) Sensitivity of metal width
| 0.03 | 0.04 | 0.05 | 0.06 | 6.9999999999999993E-2
Lowest_layer_2.5% | 23.5 | 23.5 | 23.5 | 23.5 | 23
Lowest_layer_7.5% | 23.5 | 23.5 | 23.5 | 23 | 23
Lowest_layer_10% | 23.5 | 23 | 23 | 23 | 23
Lowest_layer_25% | 22 | 22 | 21 | 22 | 21.5
Highest_layer_2.5% | 24 | 23.5 | 23.5 | 23 | 23
Highest_layer_7.5% | 23.5 | 23.5 | 23 | 22.5 | 22.5
Highest_layer_10% | 23.5 | 23 | 23 | 22.5 | 22.5
Highest_layer_25% | 22.5 | 22 | 9 | 0 | 0
Bottom
layer
Top
layer
Bottom
layer
Top
layer
Sweep VI density from 2.5% to 25%
Simultaneously sweep metal width or pitch
Routability suddenly decrease as VI density increase in higher metal
Kth
Kth
VI density
PDN density
Easily
BREAKDOWN!
Notes: We attached VI pins to B2 metal layer of PDN with same pitch, and we sweeps VI density.
VI density describe #Vis to #nets.
Our target VI density range is from 2.5% to 25%, but slightly different from actual density.
As you can see in right graph, if the top layer is more dense with high VI density, it causes sudden breakdown of routability.
Therefore, the PDN design in the 3D IC should be carefully determined with consideration of vertical interconnections.

## Slide 17: IR drop & Routability Model
We sweep the value of each knob from 75% to 125% of its reference value (e.g., 0.3um to 0.5um for M3 stripe width)
IR drop model  average 4.02mV (resp. 4.05mV) error for the training (resp. testing) dataset
Routability model  average 0.98 (strong) correlation coefficient
Chart: Actual WIR (V)
Chart: Actual Kth
Total 256 #PDNs
Notes: In this slide, I will explain the result of IR drop and routability model selection.
We sweep the value of each design-independent knob from 75% to 125% of its reference value.
The total number of PDNs is 256.
The reason that the variation range is 50% is because, when the number is changed more than that, stripes are overlapped.
As I mentioned in the previous slide, two models are trained with two regression method.
In this mesh-like placement case, multivariable regression method shows accurate result.

## Slide 18: Verification on Real Design
Chart: Actual Kth
| 4.3100000000000027E-2
near-optimal PDN | 13.38
reference PDN | 11.9
worst PDN | 9.08
Chart: Actual Kth
| 1.1299999999999977E-2
near-optimal PDN | 2.08
reference PDN | 1.9
worst PDN | 1.72
Improvement
AES cipher
JPEG encoder
9.5% (resp.12.4%) improvements for the AES cipher (resp. JPEG encoder) testcase over five denoising runs while satisfying IR drop constraint
Improvement
IR drop limit
IR drop limit
Notes: Finally, we have applied a trained model with mesh-like placement to the real design.
To improve accuracy, the results are expressed as the mean value of five denoising runs.
In the graphs, the right y-axis is the K-threshold value predicted by mesh-like placement.
The left Y-axis represents the actual K-threshold value in each design, and the x-axis represents the actual worst IR drop.
In our flow, it is more important to predict the ranking order of PDNs than the absolute value of K-threshold.
We set the worst IR drop constraints as same as reference PDN.
So near-optimal PDN shows almost 9.5% and 12.4% routability improvements for the AES cipher and JPEG encoder respectively.

## Slide 19: Conclusion and Future Goals
We study the impact of VI density on design routability and build a VI-aware routability model
Propose an interface to properly combine IR drop analysis of PDN configurations and corresponding impact on routability
On a 28nm design, our model identifies a nearly-optimal PDN out of 256 possibilities
The first to propose such a pathfinding methodology to identify optimal PDN configurations for D2W-based designs
Ongoing / future works
  BEOL layer stack combination choice
  Verification with other technology and design
  Consider height of layer

## Slide 20: Thank You!
Notes: Thank you for your attention.

## Slide 21: PDN Design Knobs
Circuit design-independent knobs | 
Metal stripe width (w) | Width of PDN stripe for each layer
VDD/VSS stripe set-to-set pitch size (p) | Set-to-set distance of VDD/VSS PDN stripe for each layer
VDD/VSS stripe spacing (s) | Spacing between VDD/VSS PDN stripe for each layer
Circuit design-dependent knobs | 
#Instances | Instances in one tier of 3D IC
Utilization | Row utilization of circuit
VI density | The ratio of #VIs to #nets

## Slide 22: 3D mesh-like placement

## Slide 23: Sensitivity Study: width and pitch

## Slide 24: Sensitivity Study: utilization

## Slide 25: Interpolation & Extrapolation of Routability Model
Chart: Interpolation
Chart: Interpolation
Chart: Extrapolation
Chart: Extrapolation
Predicted Kth
Predicted Kth

## Slide 26: Testcase Information
Testcases | Clk period | #Insts | #Nets | Util | #VIs(~5%)
AES cipher top | 1.4 ns | 10623 | 10882 | 0.727 | 529
JPEG encoder | 1.4 ns | 23883 | 27161 | 0.727 | 1292