## Slide 1
CoRe-ECO: Concurrent Reﬁnement of Detailed Place-and-Route for an Efﬁcient ECO Automation
Chung-Kuan Cheng1, Andrew B. Kahng1,2, Ilgweon Kang3, Minsoo Kim2,
Daeyeal Lee2, Bill Lin2, Dongwon Park2, and Mingyu Woo2
1Department of Computer Science and Engineering, University of California, San Diego
2Department of Electrical and Computer Engineering, University of California, San Diego
3Digital & Signoff Group, Cadence Design Systems Inc.
[Paper ID : 103]

## Slide 2: Challenges in Layout Refinement (ECO*) Flow
DRV Correction Flow
Partitioning/Floor-planning
Routing
(Through the commercial tool)
Gate-level Netlist
(After Logic-Synthesis)
Placement
Standard-Cell
Library
#DRV* < 300?
DRV-Clean Layout
DRV Correction
(Through manual stitch/modify)
Placement Adjustment
Swap
Cell Swap/Flip/Shift
Master Cell Change
Pin-length Extension
Routable?
Correct DRVs (Re-Route)
No
Finish
Iterative Manual Placement Refinement & Re-routing
[Design Rule Complexity Rising , semiengineering.com]
[Source: https://www.imec-int.com/en/imec-magazine/imec-magazine-november-2018/the-supervia-a-promising-scaling-booster-for-the-sub-3nm-technology-node]
Fewer routing tracks
Higher pin density
Complex design rules
* ECO : Engineering Change Order
* DRV : Design Rule Violation

## Slide 3: Concurrent Refinement Framework at the ECO stage
Concurrent optimization of DP, DR, and cell replacement for each local window (i.e., switchbox)

## Slide 4: Refinement Operations
Placement Adjustment
Pin-length Extension
(Cell Replacement)
Initial Placement
Horizontal Shifting
Horizontal Flipping
Cell Swapping
Vertical Shifting
Initial Placement
Pin-length Extension

## Slide 5: Overall ECO flow using CoRe-ECO framework
Initial Detailed P&R Result (DEF)
LEF/DEF Conversion
(pinLayout)
Standard Cell Library (LEF)
Switchbox Generation
(pinLayout)
CoRe-ECO SMT Code Generation
(smt2)
Non-overlapping Switchbox?
Remaining DRVs?
SMT Solutions to DEF Conversion
ECO Result (DEF)
Yes
Yes
Yes
Routable?
Yes
No
No
No
Another Round?
Final ECO Result (DEF)
ECO Result (DEF)
ECO w/ CoRe-ECO Framework
No
SMT Solving
Multi-threaded
DRV Correction

## Slide 6: Switchbox Generation
Local window with 1 DRV, displayed by the commercial tool
Visualization of the generated switchbox

## Slide 7: SMT Code Generation – Grid-based Place-and-Route Architecture
External Pin Candidates (PEX)
Cell Placement Grid
Internal Pin Candidates (PIN)
Pins on Metal1
Pins on Metal2
Pins on boundary
of switchbox
Standard Cell Instance
M1 Track
Origin of Cell Instance
Routing Grid

## Slide 8: SMT Code Generation – Placement and Routing Model
[Ilgweon Kang et al., Fast and precise routability analysis with conditional design rules, SLIP 2018]
Cell Placement Formulation
  Relative Positioning Constraints between Adjacent Cells
Detailed Routing Formulation
  Grid-based Routing Graph using Multi-Commodity Flow
Notations for the proposed framework
  Conditional Design Rules
(a) MAR(Minimum Area Rule)
(b) EOL (End-Of-Line Spacing)
(c) VR (VIA Rule)

## Slide 9: SMT Code Generation – Dynamic Cell Allocation (DCA)
Flow Capacity Control (from Placement)
Flow Variable Connection (to Route)

## Slide 10: SMT Code Generation – Perturbation-Minimized Optimization
Lexicographic Multiple-Objective Optimization

## Slide 11: Experimental Results – Statistics
EUV-Loose (EL) : MAR/EOL/VR = 1/1/1
EUV-Tight (ET) : MAR/EOL/VR = 1/2/1

## Slide 12: Experimental Results – Detailed ECO Operations
DRV Reduction by CoRe-ECO rounds for AES (4T/ET/MPO2)
Example of refinement operations
in the proposed ECO flow (Index 38)
Switchbox with 3 DRVs
Routable solution of
the CoRe-ECO framework

## Slide 13: Summary
We propose a novel concurrent reﬁnement framework (CoRe-ECO) for the automated ECO flow by devising a dynamic cell allocation (DCA), merging the reﬁnement steps into a single-step optimization.
CoRe-ECO provides simultaneous and perturbation-minimized reﬁnements of DP-, DR-, and cell-optimized layout solutions to address the DRVs during the ECO stage.
CoRe-ECO is capable of achieving a DRV-clean layout solution by ripping up and reﬁning a local window of the whole layout design.
CoRe-ECO successfully resolves an average of 58.6% (range: 33.3% to 100.0%) of remaining post-ECO route DRVs on M1-M3 layers, across a range of benchmark circuits with various cell architectures, with no adverse effect on total routed wirelength (average of 0.003% reduction).

## Slide 14: Thank you