## Slide 1: Optimization of Overdrive Signoff
Tuck-Boon Chan, Andrew B. Kahng, Jiajia Li and Siddhartha Nath
VLSI CAD LABORATORY, UC San Diego

## Slide 2: Outline
Motivation
Design Cone
Dominance of Modes
Problems and Methodologies
Experimental Setup and Results
Conclusions and Ongoing Works

## Slide 3: Outline
Motivation
Design Cone
Dominance of Modes
Problems and Methodologies
Experimental Setup and Results
Conclusions and Ongoing Works

## Slide 4: Motivation
Mode = (voltage, frequency) pair
Multi-mode operation requires multi-mode signoff
  Example: nominal mode and overdrive mode
Selection of signoff modes affects area, power
Our Goal: Optimally select signoff modes
  Improve performance, power, or area
  Reduce overdesign
NOM
OD
NOM
OD
time
Vdd
tnom
tOD
tnom
tOD

## Slide 5: Fix Nominal Mode
fnom = 500MHz
Vnom= 0.9V
< 87 mW
87 - 89 mW
90 - 92 mW
90 - 92 mW
93 - 95 mW
> 95 mW
1.05
1.07
1.09
1.11
1.13
1.15
1.17
1.03
1000
950
900
850
800
Overdrive Voltages (V)
Overdrive Frequencies (MHz)
93 - 95 mW
Different overdrive modes  20% power range
The average power of circuits signed off with different overdrive modes
Average power = r x POD + (1-r) x Pnom
  r is the duty cycle of overdrive mode

## Slide 6: Fix Nominal Mode + OD Frequency
Power of circuits signed off with different overdrive voltages
Low signoff voltage  large # of buffers
High signoff voltage  high dynamic power
Chart: Overdrive Voltages (V)
| 1.03 | 1.05 | 1.07 | 1.09 | 1.11 | 1.129999999999989 | 1.149999999999989 | 1.170000000000002
950 MHz | 100.3 | 96.58 | 95.73 | 94.04 | 91.35 | 86.79 | 86.89 | 89.18
14%
fnom = 500MHz
Vnom = 0.9V
fOD = 950MHz

## Slide 7: Outline
Motivation
Design Cone
Dominance of Modes
Problems and Methodologies
Experimental Setup and Results
Conclusions and Ongoing Works

## Slide 8: Tradeoff between Frequency & Voltage
Voltage scaling  frequency vs. voltage tradeoff curves
Maximum frequency increases essentially linearly with supply voltage
We approximate such curves as straight lines
Chart: Voltage (V)
| 0.9 | 0.950000000000001 | 1.0 | 1.05 | 1.1 | 1.149999999999997 | 1.2
INV chain with LVT cells | 500 | 550 | 599 | 640 | 680 | 721 | 766
INV chain with HVT cells | 500 | 561 | 622 | 683 | 738 | 808 | 850

## Slide 9: Design Space for Signoff
Design space for signoff is the set of all possible combinations of signoff modes
Example: design space for two-mode signoff is all combinations of two points in the plane
Voltage
Frequency
Mode  (voltage, frequency)
Circuit  (frequency vs. voltage tradeoff) curve

## Slide 10: Design Cone
Design cone is the union of all the feasible operating modes (frequency, voltage pairs) for circuits signed off at one mode
Determined by tradeoff between frequency and voltage (slopes of frequency vs. voltage tradeoffs)
Indicates the solution space for signoff mode selection
Voltage
Frequency
A
The design cone of mode A

## Slide 11: Estimation of Design Cone
Slope of frequency vs. voltage tradeoff (MHz/V) mainly determined by threshold voltages
Gate type, fanout have little influence
Wire resistance also has little influence
  10,000X change in resistance  <2% change in slopes
VT | Fanout | Gate Types |  | 
 |  | INV | NAND | NOR
LVT | 4 | 887 | 800 | 936
LVT | 16 | 776 | 787 | 877
HVT | 4 | 1167 | 1176 | 1260
HVT | 16 | 1126 | 1217 | 1246

## Slide 12: Estimation of Design Cone
Slope of frequency vs. voltage tradeoff (MHz/V) mainly determined by threshold voltages
Gate type, fanout have little influence
Wire resistance also has little influence
  10,000X change in resistance  <2% change in slopes
VT | Fanout | Gate Types |  | 
 |  | INV | NAND | NOR
LVT | 4 | 887 | 800 | 936
LVT | 16 | 776 | 787 | 877
HVT | 4 | 1167 | 1176 | 1260
HVT | 16 | 1126 | 1217 | 1246

## Slide 13: Estimation of Design Cone
Slope of frequency vs. voltage tradeoff (MHz/V) mainly determined by threshold voltages
Gate type, fanout have little influence
Wire resistance also has little influence
  10,000X change in resistance  <2% change in slopes
VT | Fanout | Gate Types |  | 
 |  | INV | NAND | NOR
LVT | 4 | 887 | 800 | 936
LVT | 16 | 776 | 787 | 877
HVT | 4 | 1167 | 1176 | 1260
HVT | 16 | 1126 | 1217 | 1246

## Slide 14: Estimation of Design Cone
Slope of frequency vs. voltage tradeoff (MHz/V) mainly determined by threshold voltages
Gate type, fanout have little influence
Wire resistance also has little influence
  10,000X change in resistance  <2% change in slopes
VT | Fanout | Gate Types |  | 
 |  | INV | NAND | NOR
LVT | 4 | 887 | 800 | 936
LVT | 16 | 776 | 787 | 877
HVT | 4 | 1167 | 1176 | 1260
HVT | 16 | 1126 | 1217 | 1246

## Slide 15: Estimation of Design Cone
Slope of frequency vs. voltage tradeoff (MHz/V) mainly determined by threshold voltages
Gate type, fanout have little influence
Wire resistance also has little influence
  10,000X change in resistance  <2% change in slopes
VT | Fanout | Gate Types |  | 
 |  | INV | NAND | NOR
LVT | 4 | 887 | 800 | 936
LVT | 16 | 776 | 787 | 877
HVT | 4 | 1167 | 1176 | 1260
HVT | 16 | 1126 | 1217 | 1246

## Slide 16: Estimation of Design Cone
Slope of frequency vs. voltage tradeoff (MHz/V) mainly determined by threshold voltages
Chart: Voltage (V)
| 0.9 | 0.950000000000001 | 1.0 | 1.05 | 1.1 | 1.149999999999997 | 1.2
AES with LVT cells | 503.5602 | 549.152 | 596.5228 | 636.168 | 677.8367 | 719.0983 | 757.4597
AES with HVT cells | 500.5247 | 559.1135 | 619.665 | 675.8866 | 742.7122 | 796.3605 | 848.0638
INV chain with LVT cells | 500 | 550 | 599 | 640 | 680 | 721 | 766
INV chain with HVT cells | 500 | 561 | 622 | 683 | 738 | 808 | 850
We use inverter chains with LVT- and HVT-only cells to estimate the boundary of design cone

## Slide 17: Outline
Motivation
Design Cone
Dominance of Modes
Problems and Methodologies
Experimental Setup and Results
Conclusions and Ongoing Works

## Slide 18: Dominance
One mode is outside of the design cone of the other  positive / negative timing slacks
LVT
HVT
Voltage
Frequency
A
Design Cone of mode A
C
Negative Slack
Positive Slack
B
Above the design cone  Negative timing slacks
Below the design cone  Positive timing slacks

## Slide 19: Dominance
LVT
HVT
B
Voltage
Frequency
A
Mode A is the dominant mode
Design Cone of mode A
One mode is outside of the design cone of the other  positive / negative timing slacks
M2 shows positive timing slacks w.r.t. M1  M1 is the dominant mode

## Slide 20: Dominance
One mode is outside of the design cone of the other  positive / negative timing slacks
M2 shows positive timing slacks w.r.t. M1  M1 is the dominant mode
LVT
HVT
B
Voltage
Frequency
A
B’
Mode A is the dominant mode
Shift mode B to B’
 reduce voltage and power
 retain same performance
Design Cone of mode A
Positive timing slacks indicate overdesign
Positive Slack

## Slide 21: Equivalent Dominance
When two modes exhibit equivalent dominance
  No one is dominated by the other
  They are in each other’s design cone
Mode A and B exhibit equivalent dominance
Voltage
Frequency
A
B
Multi-mode signoff at modes which do not exhibit equivalent dominance leads to overdesign

## Slide 22: Outline
Motivation
Design Cone
Dominance of Modes
Problems and Methodologies
Experimental Setup and Results
Conclusions and Ongoing Works

## Slide 23: The 3+1 Problems
Overdrive signoff has four parameters
  Nominal mode: ,
  Overdrive mode: ,
Given fnom, fOD and Vnom, search for VOD
Given fnom, fOD and VOD, search for Vnom
 Minimize power
Given Vnom, VOD and fnom, search for fOD
Given Vnom, VOD and fOD, search for fnom
 Maximize performance under power constraints
fnom
Vnom
fOD
VOD

## Slide 24: The 2+2 Problems
Overdrive signoff needs four parameters
  Nominal mode: fnom, Vnom
  Overdrive mode: fOD, VOD
FIND_OD: given (fnom, Vnom), search for (fOD, VOD)  maximize fOD s.t. average and peak power satisfy constraints
FIND_VOLT: given fnom and fOD, search for Vnom and VOD  minimize average power

## Slide 25: Reduction from 2+2 to 3+1
2+2 problems can reduce to 3+1 problems by sweeping one unknown parameter
fnom
fOD
fnom
fOD
Sweep Vnom
Vnom_{1, 2, ...}
3+1 Problem Solver
VOD_1,
VOD_2,
...
Miminum Pavg
Corresponding Vnom
Vnom
VOD
fnom
Vnom
fnom
Vnom
Sweep VOD
VOD_{1, 2, ...}
3+1 Problem Solver
fOD_1,
fOD_2,
...
Maximum fOD
Corresponding VOD
fOD
VOD
Reduction of FIND_OD problem
Reduction of FIND_VOLT problem

## Slide 26: Methodologies for 3+1 Problems
Given fnom, fOD and Vnom, search for VOD
Given fnom, fOD and VOD, search for Vnom
 Minimize power
Voltage
Frequency
Nominal Mode
Vnom
fnom
fOD
Voltage
Frequency
Overdrive Mode
VOD
fnom
fOD
Solution space
Exhaustive search on the solution space defined by given parameters and design cone

## Slide 27: Methodologies for 3+1 Problems
Voltage
Frequency
Nominal
Mode
Vnom
fnom
VOD
Voltage
Frequency
Overdrive Mode
VOD
Vnom
fOD
Solution space
Scale frequency along the solution space until the power constraint is hit
Given Vnom, VOD and fnom, search for fOD
Given Vnom, VOD and fOD, search for fnom
 Maximize performance under power constraints
Notes: ----- Meeting Notes (1/23/13 10:30) -----

## Slide 28: Common Design Practice Today: Signoff & Scale (FIND_OD)
Sign off circuit at nominal mode
Frequency
Voltage
Nominal Mode
Vnom
fnom
VOD
Overdrive Mode
fOD
Scale the voltage to increase frequency until the power constraint is hit
Simplifies the design process, but ignores second (OD) mode in the signoff

## Slide 29: Proposed Flow (FIND_OD)
Signoff & scale at nominal mode to estimate the maximum overdrive frequency (fest)
Voltage
Frequency
Nominal Mode
Vnom
fnom
fest

## Slide 30: Proposed Flow (FIND_OD)
Signoff & scale at nominal mode to estimate the maximum overdrive frequency (fest)
Determine several approximate overdrive modes based on fest and the design cone
Voltage
Frequency
Nominal Mode
Vnom
fnom
fest
Approximate overdrive modes

## Slide 31: Proposed Flow (FIND_OD)
Signoff & scale at nominal mode to estimate the maximum overdrive frequency (fest)
Determine several approximate overdrive modes based on fest and the design cone
Implement voltage scaling on each approximate overdrive mode until hit the power constraint
Overdrive Mode
(highest fOD)
Voltage
Frequency
Nominal Mode
Vnom
fnom
fest

## Slide 32: Proposed Flow (FIND_VOLT)
Exhaustive search for Vnom  minimum power at nominal mode
Voltage
Frequency
fnom
fOD
Voltage
Nominal power
Vnom

## Slide 33: Proposed Flow (FIND_VOLT)
Exhaustive search for Vnom  minimum power at nominal mode
Estimate the design cone of selected mode
Voltage
Frequency
fnom
fOD
Voltage
Vnom

## Slide 34: Proposed Flow (FIND_VOLT)
Exhaustive search for Vnom  minimum power at nominal mode
Estimate the design cone of selected mode
Exhaustive search for VOD within the design cone  minimum average power
Voltage
Frequency
fnom
fOD
Voltage
Vnom
VOD

## Slide 35: Outline
Motivation
Design Cone
Dominance of Modes
Problems and Methodologies
Experimental Setup and Results
Conclusions and Ongoing Works

## Slide 36: Experimental Setup
Design: AES (~15K instances) from OpenCores
Technology: TSMC 65nm
Comparison
  Signoff&Scale applies traditional signoff and scale methodology
  Proposed implements our proposed flow
  Exhaustive Search uses exhaustive search

## Slide 37: Experimental Results (FIND_OD)
Proposed flow improves performance by 7%
 | Signoff & Scale | Proposed Flow | Exhaustive Search
fOD (MHz) | 711 | 764 | 768
VOD (V) | 1.14 | 1.14 | 1.15
Area (µm2) | 31029 | 32016 | 32020
POD (mW) | 49.13 | 49.14 | 49.76
Pavg (mW) | 21.73 | 20.90 | 20.24
# P&R runs | 1 | 7 | 32
Nominal mode: fnom = 500MHz Vnom = 0.9V
Flow requires about 22% runtime compared to exhaustive search with similar area (-0.01%), power (+3%) and performance (-0.5%)

## Slide 38: Experimental Results (FIND_VOLT)
Flow requires about 27% runtime compared to exhaustive search with similar area (-0.01%), power (+8%)
 | Proposed Flow | Exhaustive Search
Vnom (V) | 0.92 | 0.91
VOD (V) | 1.02 | 1.01
Area (µm2) | 30948 | 30960
POD (mW) | 41.08 | 30.38
Pavg (mW) | 22.28 | 20.61
# P&R runs | 9 | 33
fnom = 500MHz / fOD = 600MHz
Signoff & Scale is not applicable to FIND_VOLT

## Slide 39: Recent Updates
Problem: too many SP&R runs
Approach:
  Use power models for global optimization
  Avoid implementing circuits at each mode
Construct power model adaptively
Small constant # runs is enough  scalable

## Slide 40: Global Optimization Flow
  Iteratively sample and refine the power models
Sample (SP&R)
Construct power models
Estimate optimal
signoff modes
Sample (SP&R)
Refine power models
Circuit information
Power models
Estimated optimal mode
Circuit information

## Slide 41: Example
Chart: Signoff Voltage (v)
| 0.9 | 0.92 | 0.94 | 0.96 | 0.98 | 1.0 | 1.02 | 1.04 | 1.06 | 1.08 | 1.1 | 1.12 | 1.139999999999998 | 1.159999999999998 | 1.180000000000002 | 1.2
1st | 19.178 | 18.8167 | 18.4797 | 18.1721 | 17.8988 | 17.665 | 17.4758 | 17.3367 | 17.2534 | 17.2318 | 17.2784 | 17.4003 | 17.6053 | 17.902 | 18.3004 | 18.8115
2nd | 19.1097 | 18.6331 | 18.1978 | 17.8091 | 17.4724 | 17.193 | 16.9767 | 16.8296 | 16.7584 | 16.7703 | 16.8737 | 17.078 | 17.3943 | 17.8355 | 18.4167 | 19.156
real | 18.83 | 18.382 | 17.311 | 17.248 | 16.622 | 16.882 | 16.979 | 16.668 | 16.259 | 16.745 | 17.204 | 16.618 | 17.573 | 17.503 | 17.498 | 19.272
  Performance of the proposed global optimization
Frequency = 800MHz , Voltage = ?
0.90V
1.20V
1.10V
1.08V
1.06V

## Slide 42: Outline
Motivation
Design Cone
Dominance of Modes
Problems and Methodologies
Experimental Setup and Results
Conclusions and Ongoing Works

## Slide 43: Conclusions & Ongoing Works
Conclusions
  Study the problem of signoff mode selection
  Propose the concept of design cone
  Show that mutual equivalent dominance is required for signoff mode selection to avoid overdesign
  Propose methodologies for signoff mode selection
Ongoing Works
  More accurate estimation of design cone
  Consider additional tradeoffs of design metrics such as area, reliability

## Slide 44: Acknowledgments
Work supported by IMPACT, SRC, NSF, Qualcomm and Samsung

## Slide 45
Thank You!