## Slide 1: Reliability-Constrained Die Stacking Order in 3DICs Under Manufacturing Variability
Tuck-Boon Chan, Andrew B. Kahng, Jiajia Li
VLSI CAD LABORATORY, UC San Diego

## Slide 2: Outline
Motivation and Problem Statement
Modeling
Our Methodologies
Experimental Setup and Results
Conclusion

## Slide 3: Outline
Motivation and Problem Statement
Modeling
Our Methodologies
Experimental Setup and Results
Conclusion

## Slide 4: Reliability Challenges for 3DICs
Stacking of multiple dies increases power density
High power density  high temperature
  3DICs with four tiers increase peak temperature by 33°C
Reliability (e.g., EM) highly depends on temperature
Chart: Tier #
| 1 | 2 | 3 | 4 | 5
Temp. | 47 | 61 | 71 | 78 | 82
Bottom tier
Top tier (nearest to heat sink)
35°C
Temperature range in a 5-tier 3DIC

## Slide 5: Context: Stacking of Identical Dies
Chart: Frequency vs. Voltage @ 85°C
| 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2
FF | 950 | 1126 | 1264 | 1387 | 1487
TT | 707 | 878 | 1022 | 1146 | 1275
SS | 498 | 654 | 799 | 943 | 1059
Chart: Power vs. Voltage @ 85°C
| 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2
FF | 0.0843 | 0.1105 | 0.1418 | 0.1794 | 0.2233
TT | 0.0694 | 0.0895 | 0.1125 | 0.1384 | 0.1691
SS | 0.0653 | 0.0836 | 0.1041 | 0.128 | 0.154
Identical dies in 3DIC stack
 Can change stacking order
Dies in stack can have different process corners, but must meet same performance spec
Adaptive Voltage Scaling (AVS)  each die has different Vdd
Slower dies have higher Vdd  power↑, temp↑, MTTF↓
Target frequency

## Slide 6: Motivation
Stacking style: ordered selection of dies with particular process variations
Heat sink
Letters S, T and F indicate the (slow, typical, fast) process corners
Strings over {S, T, F} indicate stacks (left-to-right corresponds to bottom-to-top)
Stacking style “FTS”
TSV
TSV
MOSFET
Fast-corner die
Bottom tier
MOSFET
Slow-corner die
Top tier
TSV
TSV
MOSFET
Typical-corner die
Middle tier

## Slide 7: Motivation
Stacking style: ordered selection of dies with particular process variations
Different stacking style  different mean time to failure (MTTF)
Goal: find the optimal stacking style  improve reliability
Chart: Stacking styles
| SSS | SST | SSF | STS | STT | STF | TSS | TST | TSF | SFS | SFT | SFF | TTS | TTT | TTF | FSS | FST | FSF | TFS | TFT | TFF | FTS | FTT | FTF | FFS | FFT | FFF
MTTF | 3.7922 | 3.8088 | 3.827 | 4.237 | 4.2575 | 4.2769 | 4.5414 | 4.5623 | 4.5845 | 4.734 | 4.7578 | 4.779 | 5.0876 | 5.1125 | 5.1364 | 5.5218 | 5.5468 | 5.5753 | 5.7025 | 5.7309 | 5.758 | 6.2065 | 6.236 | 6.2673 | 6.9751 | 7.0116 | 7.0471
Letters S, T and F indicate the (slow, typical, fast) process corners
Strings over {S, T, F} indicate stacks (left-to-right corresponds to bottom-to-top)
Different stacking orders of {F, T, S} die  up to 44% ∆MTTF

## Slide 8: Stacking Optimization Problem
Given N dies with distinct process variation
Such that frequency of each die in a stack = freq
Objective to maximize summation of MTTFs of stacks

## Slide 9: Outline
Motivation and Problem Statement
Modeling
Our Methodologies
Experimental Setup and Results
Conclusion

## Slide 10: Reliability Model for 3DICs
Electromigration is now a dominant reliability constraint
 Our work focuses on EM
We use Black’s equation to estimate MTTF of a die (MTTFdie)
  MTTF exponentially depends on temperature
Failure rate (λ) is the number of units failing per unit time
During the useful-life period λ is constant  MTTF = 1 / λ (1)
Any failure of any die causes a stack to fail  λstack = ∑ λdie (2)
(1) and (2)  MTTFstack = 1 / (∑1/MTTFdie)
λ
Time
Useful-life period

## Slide 11: Bin-Based Model for Process Variation
Each die exhibits distinct process variation
 find the optimal stacking style is intractable
We classify dies into constant number of process bins
  Dies with similar process variations are classified to one bin
  We assume same process variation for dies in one bin
-3σ -1.5σ 0σ 1.5σ 3σ
# of dies
Bin 1
Bin 2
Bin 3

## Slide 12: Outline
Motivation and Problem Statement
Modeling
Our Methodologies
Experimental Setup and Results
Conclusion

## Slide 13: Determinants of 3DIC Reliability
Peak temperature defines the MTTF of the 3DIC
Two factors have significant impacts on temperature of 3DIC
Process variation
Same performance requirement for all dies
Adaptive voltage scaling is deployed
Slower dies have higher Vdd, power, higher temperatures
Stacking order
Primary mechanism for thermal dissipation in a 3DIC is through heat sink
Vertical temperature gradient exists in 3DICs
Dies on bottom tiers have higher temperatures
Worst-case peak temperature (= minimum MTTF) happens where slow dies are on bottom tiers (far from the heat sink)

## Slide 14: Rule-of-Thumb
Rule-of-thumb: to optimize reliability of a 3DIC, the slowest dies should be located closest to the heat sink
For a stack with particular composition of dies, the optimal stacking order is determined by rule-of-thumb
Chart: MTTF (year)
| 7.2744754315 | 7.5132362964199944 | 7.563335544579993 | 7.6483407433300004 | 7.7983789512200001 | 7.9292365610799944 | 7.9347399146999997 | 8.0144701261800009 | 8.0690927873900016 | 8.0802333878700008 | 8.2020357207700005 | 8.4733423511799995
STTTF | 0.53795 | 0.53906 | 0.53581 | 0.53623 | 0.53533 | 0.5366 | 0.53493 | 0.53609 | 0.53554 | 0.53512 | 0.53589 | 0.53579
Letters {S, T, F} indicate process corners
Strings indicate stacking order
Locating slow dies close to the heat sink helps improve MTTFs of 3DICs

## Slide 15: “Zig-zag” Heuristic Method
Zig-zag heuristic method is based on rule-of-thumb
Stack dies from slow to fast, from top tiers to bottom tiers
Complexity of stacking optimization is NP-hard, but zig-zag is O(n·log(n)) (n = number of dies)
Top tier (nearest to heat sink)
Bottom tier

## Slide 16: ILP-Based Method
ILP formulation
  Maximize ∑MTTFi·Ci
  Such that ∑Ci·Yq,i = Xq
  // each input die should be used exactly once and consistent with its process bin
  Ci ≥ 0 // number of output stacks implemented with ith stacking style cannot be negative
Notations
  Ci is the number of stacks implemented with ith stacking style
  MTTFi is the MTTF of stack implemented with ith stacking style
  Yq,i is the number of dies belong to qth bin contained in ith stacking style
  Xq is the number of dies classified to qth bin

## Slide 17: Outline
Motivation and Problem Statement
Modeling
Our Methodologies
Experimental Setup and Results
Conclusion

## Slide 18: Experimental Setup
Design: JPEG from OpenCores
Technology: TSMC 65nm
Libraries: characterized using Cadence Library Characterizer vEDI9.1
  Process corner: SS, TT, FF
  Temperature: 45 °C – 165 °C
  Voltage: 0.9V – 1.2V
LP solver: lp_solve 5.5
Thermal analysis: use Hotspot 5.02
  Chip thickness = 50 μm
  Convection capacitance = 140.4J/K
  Ambient temperature = 60 °C

## Slide 19: Improvement on MTTF
Stacking optimization (ILP-based and zig-zag) increases the MTTFs of stacks
Chart: MTTF (year)
| 0.2 | 0.6 | 1
ILP | 7.3944 | 7.4811 | 7.5706
Zig-zag | 7.403 | 7.5499 | 7.6658
Greedy | 6.7017 | 6.3555 | 5.9714
Random | 6.9313 | 6.7146 | 6.4525
Average MTTF of stacks

## Slide 20: Variation of MTTF
Stacking optimization (ILP-based and zig-zag) increases the MTTFs of stacks
Stacking optimization (ILP-based and zig-zag) reduces the variation in MTTFs
Chart: MTTF (year)
| σ=0.2 | σ=0.6 | σ=1.0 | σ=0.2 | σ=0.6 | σ=1.0 | σ=0.2 | σ=0.6 | σ=1.0 | σ=0.2 | σ=0.6 | σ=1.0
 | 7.3944 | 7.4811 | 7.5706 | 7.403 | 7.5499 | 7.6658 | 6.7017 | 6.3555 | 5.9714 | 6.9313 | 6.7146 | 6.4525
 | 7.68 | 8.12 | 8.17 | 7.77 | 7.96 | 8.44 | 8.82 | 9.59 | 11.4 | 8.01 | 8.45 | 9.11
 | 7.3 | 7.34 | 7.29 | 7.39 | 7.51 | 7.62 | 5.72 | 4.61 | 3.16 | 6.4 | 5.88 | 4.95
 | 7.5256 | 7.7127 | 7.8778 | 7.5458 | 7.7061 | 7.937 | 7.7319 | 8.0583 | 8.4522 | 7.4731 | 7.6148 | 7.7799
 | 7.3944 | 7.4811 | 7.5706 | 7.403 | 7.5499 | 7.6658 | 6.7017 | 6.3555 | 5.9714 | 6.9313 | 6.7146 | 6.4525
 | 7.68 | 8.12 | 8.17 | 7.77 | 7.96 | 8.44 | 8.82 | 9.59 | 11.4 | 8.01 | 8.45 | 9.11
 | 7.3 | 7.34 | 7.29 | 7.39 | 7.51 | 7.62 | 5.72 | 4.61 | 3.16 | 6.4 | 5.88 | 4.95
 | 7.5256 | 7.7127 | 7.8778 | 7.5458 | 7.7061 | 7.937 | 7.7319 | 8.0583 | 8.4522 | 7.4731 | 7.6148 | 7.7799
ILP-based Zig-zag Greedy Random

## Slide 21: Variability Can Help !
Manufacturing variation can help improve MTTF of stacks
Chart: σ
| 0.2 | 0.6 | 1 | 1.4
Zig-zag (MTTF_avg) | 7.3 | 7.47 | 7.63 | 7.8
Zig-zag (MTTF_min) | 7.27 | 7.39 | 7.51 | 7.62

## Slide 22: Variability Can Help !
Manufacturing variation can help improve MTTF of stacks
  Supply voltage can exceed the maximum allowed value
 Benefit from process variation disappears when the variation exceeds a particular amount
Limited amount of process variation can help improve reliabilities of 3DICs with stacking optimization
Chart: Supply voltage (V)
| 0.2 | 0.6 | 1 | 1.4 | 1.8
Max. supply voltage | 1.016 | 1.077 | 1.146 | 1.227 | 1.33
Min. supply voltage | 0.946 | 0.876 | 0.823 | 0.731 | 0.64
σ

## Slide 23: Outline
Motivation
Modeling
Problem and Methodologies
Experimental Setups and Results
Conclusion

## Slide 24: Conclusion
We study variability-reliability interactions and optimization in 3DICs
We propose “rule-of-thumb” guideline for stacking optimization to reduce the peak temperature and increase MTTFs of 3DICs
We propose ILP-based and zig-zag heuristic methods for stacking optimization
We show that limited amount of manufacturing variation can help to improve reliabilities of 3DICs with stacking optimization
Future Work
  Optimize on other objectives (power variation)
  Different performance requirements for dies

## Slide 25: Acknowledgments
Work supported from Sandia National Labs, Qualcomm, Samsung, SRC and the IMPACT (UC Discovery) center

## Slide 26
Thank You!