## Slide 1: Timing Margin Recovery With Flexible Flip-Flop Timing Model
Andrew B. Kahng and Hyein Lee
UC San Diego VLSI CAD Laboratory

## Slide 2: Outline
Preliminary
Motivation
Related Work
Sequential LP-based Optimization
Experimental Results
Conclusions and Future Work

## Slide 3: Preliminary: Static Timing Analysis
Timing corners
  Min corner: the corner where gate/wire delay is minimum
  Max corner: the corner where gate/wire delay is maximum
Timing modes
  Scenarios where different functions are performed in a design
  Test mode, function mode, etc.
Types of analyses
  Graph-based analysis: Considers only the worst/best case
  Path-based analysis: Considers input vectors for more accurate analysis

## Slide 4: Preliminary: Flip-Flop (FF) Timing Model
FF timing components
  Setup time: the minimum amount of time input data should be steady before clock
  Hold time: the minimum amount of time input data should be steady after clock
  Clock-to-q (c2q) delay: the delay of output from clock
Conventional timing model: Setup/hold time and c2q delay are fixed values

## Slide 5: Motivation: Flexible FF Timing
Setup/hold time/c2q delay is NOT a single value
Various setup-hold-c2q sets can be used for timing analysis ⇒ Flexible FF timing model ⇒ Reduce pessimism
setup
hold
c2q1
c2qn
...
setup-hold-c2q
flexible model
⇒ Tradeoff among setup/hold/c2q delay

## Slide 6: Motivation: Why Flexible FF Timing?
If data paths are independent of each other in PBA,
  Using fixed FF timing model can loose performance optimization opportunity
  Flexible timing model could reduce pessimism
470ps
480ps
460ps
470ps
460ps
480ps
FF3
FF1
FF2
setup: 10ps
c2q: 20ps
setup: 10ps
c2q: 20ps
setup: 20ps
c2q: 10ps
Total: 500ps
Total: 500ps
Total: 500ps
20ps
10ps
10ps
20ps
 520ps?
 500ps!

## Slide 7: Related Work
Setup-hold time interdependency
  Characterization [7] [8] [10]
  Timing analysis [1] [2] [3] [4] [5] [6]
  However, no consideration of c2q delay
Setup-hold-c2q interdependency [1]
  Propose a timing analysis method by exploiting flexible flip-flop timing model
  However, iterative search can result in suboptimal solutions
Our work
  Based on setup-hold-c2q interdependency
  Linear programming-based global optimization
  Mode/corner-specific timing analysis by exploiting flexible FF timing model

## Slide 8: Outline
Preliminary
Motivation
Related Work
Sequential LP-based Optimization
Experimental Results
Conclusions and Future Work

## Slide 9: Problem Formulation
Objective: Find the best combination of setup/hold time and c2q for each FF to minimize setup/hold violations
Solution space: 3d surface  not easy to obtain an accurate analytical model with three variables
To reduce the dimension, we divide setup-hold-c2q optimization into: setup-c2q optimization + hold-c2q optimization
setup
c2q
hold
c2q
C2q-setup-hold surface
setup
hold
c2q

## Slide 10: Problem Formulation: Sequential LP
Solve two sub-problems sequentially
  The solution from one problem ⇒ used as input to another problem
  The sequence of solving problems can change depending on which problem is more critical
Setup-c2q optimization
  Maximize setup slack
  Subject to
    c2q + dmax + Tsu + Ssu ≤ P
    c2q = f(Tsu)
    L ≤ Tsu ≤ U
Hold-c2q optimization
  Maximize setup and hold slack
  Subject to
    c2q + dmax + Tsu + Ssu ≤ P
    dmin + Sh > Th
    c2q = f(Th)
    L ≤ Th ≤ U
Where dmax/dmin : max/min data path delay, Tsu: setup time, Th: hold time, Ssu: setup slack, Sh: hold slack

## Slide 11: Timing Signoff Across Corners/Modes
Setup/hold time does not have to be a single value across corners/modes!
Timing signoff across corners
  Max delay corner  hold violation , setup violation  ⇒ Select optimal setup time first
  Min delay corner  setup violation , hold violation  ⇒ Select optimal hold time first
Timing signoff across modes
  Scan test mode  hold violation  ⇒ Select optimal hold time first
Notes: The flexible flip-flop timing model is helpful especially for multi-corner multi-mode timing analysis.
This is because, we don’t need to use a single value for each of setup time, hold time and c2q delay.
For example, considering multiple corners, we have less hold time violations and more setup time violations at max delay corner.
So, we can first optimize setup time.
Similarly, at min delay corner, we have less setup time violations and more hold time violations.
In this case, we can optimize hold time first.
For multi-mode analysis, the same method can be applied.
For instance, scan test mode can have more hold time violations because scan paths have less number of stages.
In this case, we can optimize hold time first.

## Slide 12: New Timing Signoff: Max Corner
Setup-c2q optimization is performed first
setup-c2q optimization
for max delay paths
hold-c2q optimization
for hold violated paths
Annotate setup/c2q to each FF
Annotate hold/c2q to each FF

## Slide 13: Characterization
Setup-hold-c2q curves are characterized with exhaustive SPICE simulation
  Setup-hold-c2q triplets are obtained at every 5ps of timing points
Use a pulse as the input data to characterize setup/hold time interdependency
  setup time: data rise to clock rise, hold time: clock rise to data fall, c2q: clock rise to q rise
c2q
setup time
hold time
clock
data
input
q output
data slew
clock slew
(for rising edge triggered FF and rise input)

## Slide 14: New Timing Signoff: Overall Flow
Extract path timing information
LP formulation
with flexible flip-flop timing model
Solve Sequential LP
(STA_FTmax , STA_FTmin)
Annotate new timing model
for each flip-flop
Solution
Netlist (and SPEF, if routed)
Timing signoff with annotated timing

## Slide 15: Outline
Preliminary
Motivation
Related Work
Sequential LP-based Optimization
Experimental Results
Conclusions and Future Work

## Slide 16: Experimental Setup
Testcases
  Open source designs with 65nm foundry technology
Commercial flow
  Logic synthesis: Synopsys Design/DFT Compiler H-2013.03-SP3
  P&R: Cadence Encounter Digital Implementation System XL 10.1
  Timing signoff: Synopsys PrimeTime H-2013.06-SP2
  LP solver: CPLEX 12.5.1
Our method is compared with
  Conventional: Conventional fixed FF timing model
  [4]: Flexible setup/hold time with fixed c2q delays
  cTool: a commercial tool with setup-hold pessimism reduction functionality

## Slide 17: Experiment Results
Results of corner-specific timing analysis at max/min corner
In mode-specific analysis, the summation of setup/hold slacks is improved
Our method fixes negative setup/hold time violations “for free”
Chart: 
| tv80s | aes | conmax | dma | jpeg
conventional | -0.10026 | -0.14107 | -0.099829 | -0.11536 | -0.1006
[4] | -0.10026 | -0.14107 | -0.099829 | -0.11536 | -0.1006
cTool | -0.10026 | -0.14107 | -0.099829 | -0.11536 | -0.1006
proposed | 0.029398 | -0.011706 | 0.026902 | 0.015337 | 0.026599
Worst setup slack
Chart: 
| tv80s | aes | conmax | dma | jpeg
conventional | -0.080351 | -0.1004 | -0.079641 | -0.080224 | -0.11886
[4] | -0.058134 | -0.079006 | -0.049685 | -0.05445 | -0.11465
cTool | -0.080351 | -0.1004 | -0.079641 | -0.080224 | -0.11886
proposed | -0.034216 | -0.04902 | -0.039368 | -0.037923 | -0.067508
Worst hold slack
[ns]

## Slide 18: Conclusion
We exploit a flexible flip-flop timing model: three-dimensional tradeoff among setup time, hold time and clock-to-q delay
We apply sequential LP-based approaches for multi-corner/mode timing signoff
Worst slack improves by 48ps on average and by up to 130ps with 65nm technology (inverter delay = ~50ps)
Future work
  Demonstration with advanced technologies
  More accurate timing model of setup-hold-c2q tradeoff
  Circuit optimization by exploiting FF timing model flexibility

## Slide 19: Thank you!