## Slide 1: A Deep Learning Methodology to Proliferate Golden Signoff Timing
Seung-Soo Han+, Andrew B. Kahng$, Siddhartha Nath$ and Ashok S. Vydyanathan$
$UC San Diego, USA
+Myongji University, S. Korea

## Slide 2: Outline
Motivation
Previous Work
Our Work
Modeling Methodology
Results
Conclusions

## Slide 3: Discrepancy in Path Slack
T1 and T2 are commercial signoff timing tools
With exactly the same inputs (.v, .spef, .lib), slack correlation is poor
110ps slack divergence  20% performance difference  one node of Moore’s Law scaling!
Chart: T1 Path Slack (ns)
 | -1.6072 | 1.0929
110 ps
IDEAL SLOPE = Perfect Correlation

## Slide 4: Challenges in Timing Signoff
Multiple commercial signoff tools
Tools have high license fees
Tool complexities grow with each release
  Millions of lines of complex code
  Diverge from published documentation
  Use proprietary timing calculators / engines
Design teams have cost and budget constraints
  Cannot own licenses from multiple tools
Design teams benefit if they can correlate with another tool
  Understand overdesign / underdesign
  implementation tool, signoff tool at each optimization loop

## Slide 5: Outline
Motivation
Previous Work
Our Work
Modeling Methodology
Results
Conclusions

## Slide 6: Previous Work
Path slack modeling and correlation
  Kahng13 – internal incremental STA vs. signoff tool
  Ganapathy10 – quantify impact of manufacturing variation with SPICE
  Tetelbaum07 – root-sum-square model of stage delay vs. SPICE
STA tools comparisons
  Mishra09, Rakheja10, Motassadeq11 compare timing reports and report discrepancies between tools

## Slide 7: Outline
Motivation
Previous Work
Our Work
Modeling Methodology
Results
Conclusions

## Slide 8: Key Contributions
We correct timing divergence between tools by exploiting big-data mindsets and machine learning techniques
GTX: models for timing elements from NLDM lookup tables in foundry timing libraries
Validation across multiple technology nodes and designs in both SI and non-SI modes
GTX reduces divergence by up to 6.6 (139.3ps to 21.1ps) at 45nm and 5.5 (32.5ps to 5.9ps) at 28nm

## Slide 9: Outline
Motivation
Previous Work
Our Work
Modeling Methodology
Results
Conclusions

## Slide 10: Modeling Elements
Setup time of launch flip-flop
Cell delay models for each pin-to-pin arc of all cell types, input slews, loads
Wire delay models with different wire R, C and input slews
Stage delay model derived from cell and wire delay models
All models combined to develop path slack model
Layered model structure  “deep”
Setup time
Cell delay
Wire delay
Stage delay
Path slack

## Slide 11: Modeling Flow
Model development is a one-time effort
Incrementally refine models with new designs
Artificial
Circuits
Train
Validate
Test
New
Designs
MODELS
(Path slack, setup time, stage, cell, wire delays)
If
error > threshold
Outliers
(data points)
ONE-TIME
INCREMENTAL
Real
Designs

## Slide 12: Outline
Motivation
Previous Work
Our Work
Modeling Methodology
Results
Conclusions

## Slide 13: Experimental Setup and Testcases
Technology: 45nm and 28nm FDSOI
Obtain netlist (.v), SPEF (.spef), SDC (.sdc) post SP&R
  Both timing tools are given identical inputs
Testcases
  Real designs – to validate and test models
    leon3mp, jpeg, aes, dma
  Artificial – to develop models using fine-grained control of timing parameters
Machine learning techniques
  Artificial Neural Networks, Random Forests, Support Vector Machine Regression, Least-Squares Regression
Dataset sizes
  Training > 100K, validation ~20K, test > 100K

## Slide 14: Correlating Two Signoff Tools
Original is the difference between two golden timing tools
GTX is the result after fitting
Path slack divergence reduces from 89ps to 22ps, i.e., ~4
Chart: Range (Max - Min) (ns)
| Path slack | Setup time | Stage delay | Cell delay | Wire delay
Original | 0.0892 | 0.012 | 0.117 | 0.4544 | 0.1948
GTX | 0.0223 | 0.0012 | 0.0238 | 0.0519 | 0.0286
4
5
8
9

## Slide 15: Path Slack from Timing Reports
Delay divergence reduces from 39ps to 0.5ps
Slack divergence reduces from 249ps to 3ps
Instance
(Cell)
Dir
Delay(T1)
Delay(T2)
Delay()
FE_CN_C274/A1 (NAND2X7)
IN
0.0447
0.0452
0.0062
FE_CN_C274/ZN (NAND2X7)
OUT
0.0565
0.0545
0.1076
FE_CN_C277/A (BUFFX8)
IN
0.0110
0.0082
0.0044
FE_CN_C277/Z (BUFFX8)
OUT
0.0272
0.0266
0.0664
FE_CN_C294/A1 (OAI22X4)
IN
0.0825
0.0837
0.0225
…
…
slack (VIOLATED)
-0.339
-0.342
-0.588
…
r
f
r
r
r
FE_CN_C281/A (INVX8)
IN
0.0057
0.0051
0.0023
FE_CN_C281/ZN (INVX8)
OUT
0.0215
0.0213
0.0264
f
r
FE_CN_C286/A2 (XOR2X4)
IN
0.0070
0.0072
0.0066
FE_CN_C286/Z (XOR2X4)
OUT
0.0332
0.0352
0.0581
f
f
…
…
FE_CN_C294/ZN (OAI22X4)
OUT
0.0677
0.0598
0.0781
f

## Slide 16: Correlating Signoff and Design Tools
GTX can correlate timing between signoff and design implementation tools
Path slack divergence reduces from 163ps to 23ps, i.e., ~7
Chart: Range (Max - Min) (ns)
| Path slack | Setup time | Stage delay | Cell delay | Wire delay
Original | 0.1628 | 0.0324 | 0.1742 | 0.1466 | 0.0439
GTX | 0.0231 | 0.0041 | 0.0222 | 0.0221 | 0.015
7
8
6
3

## Slide 17: Incremental Modeling
Incremental modeling applied to a new design, x5_jpeg
Path slack divergence reduces from 36ps to 18ps
Chart: Range (Max - Min) (ns)
| Path slack | Stage delay | Cell delay | Wire delay
Original | 0.0892 | 0.2906 | 0.2227 | 0.428
GTX | 0.036 | 0.0704 | 0.0832 | 0.2569
Incr. GTX | 0.0182 | 0.0194 | 0.0272 | 0.0268
2
4
3
9

## Slide 18: Outline
Motivation
Previous Work
Our Work
Modeling Methodology
Results
Conclusions

## Slide 19: Conclusions and Future Work
Timing correlation with multiple tools can help design teams fix overdesign / underdesign
Commercial signoff tools’ reports diverge significantly!
GTX builds predictive models that reduce timing divergence between tools by up to 6.6at 45nm and 5.5at 28nm FDSOI
Validation across multiple tools, designs and foundry technology libraries
Ongoing work
  Expand GTX to CCS models
  Methodology to integrate GTX into timing closure flows
  Methodology to characterize libraries for “ideal” delay per unit length

## Slide 20: Thank You

## Slide 21: Modeling Techniques
All techniques tried for each model
Following techniques minimize both MSE and range of errors
  Setup time – Artificial Neural Networks
  Cell delay – Artificial Neural Networks
    LSQR (for upstream slew correction)
  Wire delay – Support Vector Machine Regression
  Stage delay – Support Vector Machine Regression
  Path slack – Random Forests