## Slide 1: OCV-Aware Top-Level Clock Tree Optimization
Tuck-Boon Chan, Kwangsoo Han, Andrew B. Kahng, Jae-Gon Lee and Siddhartha Nath
VLSI CAD LABORATORY, UC San Diego

## Slide 2: Outline
Motivation and Previous Work
Our Approach
Experimental Setup
Results and Conclusions

## Slide 3
Complex timing constraints across process, voltage, temperature and operating scenarios
On-chip variation  more design margin
Clock tree consumes up to 40% power  aggressive power reduction  complex clock tree with clock logic cells (CLCs) such as, clock gating, divider, MUXes
Clock Tree Synthesis Is Challenging!

## Slide 4: Top-Level Clock Tree Problems
CGC
DIV
MUX
Sinks 1
Sinks 2
CTS with long non-common paths
CLCs
Top-level tree
Bottom-level trees
Clock root
The “top-level” clock tree comprises of all transitive fanins to CLCs starting from a clock root pin
Trees below the CLCs are the bottom-level trees
Industry tools do not always optimize the top-level clock trees
Results in large skews with multi-corner multi-mode (MCMM) scenarios

## Slide 5: Top-Level Clock Tree Optimization
Optimizing the “top-level” clock tree involves handling of complex clock logic cells
The optimization involves
  CLC placements
  Buffer insertion
  Minimizing non-common paths
  Balancing the tree based on timing information (WNS, TNS across setup and hold corners)
CGC
Sinks 2
DIV
MUX
Sinks 2
CGC
DIV
MUX
Sinks 1
Sinks 2
CTS with long non-common paths
CTS with reduced non-common paths

## Slide 6: Previous Works
Rajaram and Pan (2011)
  Reduce non-common path delay by reallocating clock pin locations of soft-IP blocks
  Insert buffers to minimize difference in clock latency among subtrees across PVT corners
  Do not consider CLCs, timing between sink groups, wirelength
Tsai (2005), Velenis et al. (2003)
  Minimize effect of OCV during CTS but do not handle CLCs or MCMM scenarios
Lung et al. (2010)
  Optimize clock skew using LP and account for delay variation across PVT corners
  Ignore non-common paths and CLC placement

## Slide 7: Outline
Motivation and Previous Work
Our Approach
Experimental Setup
Results and Conclusions

## Slide 8: Our Work
Current CTS tools
 Balance bottom-level clock trees
 Optimize CLC placement
 Multi corner multi mode (MCMM) optimization
Our method
Focus on top-level clock tree
Simultaneously optimize CLC placement and balance clock tree across multi corner multi mode
Extract timing constraints from bottom level clock trees  capture accurate MCMM constraints

## Slide 9: LP-Based Optimization
  Objective: a weighted sum of
  worst negative slack (WNS)
  total negative slack (TNS)
  non-common paths
  wirelength of a clock tree
  Variables: CLC locations and net delays
    Model delay from pin I to pin J as a linear function of Manhattan distance  Captures impact of CLC placement
pin i
pin j
CLC
CLC
    Manhattan distance
    Delay
    Delay is linear function of the Manhattan distance with uniform buffer insertion!
  Extract insertion and timing constraints from bottom level clock trees to estimate slacks of critical paths
  Delays across different PVT corners are normalized to a reference corner for MCMM optimization

## Slide 10: Example
tp are the terminal pins
d(i,j) : delay from pin i to pin j
d (1,2) = 2ns
t1
t3
t4
t5
Top level
Bottom level
root
CLC
1ns
Sink group 3
Critical path delay = 3ns
d (1,3) = 0.5ns
d (4,5) = 1ns
t2
3ns
d (3,4) = 0.5ns
Sink group 2
Sink group 1
Example: Make d(1,2) = 4ns  improves timing

## Slide 11: Our Heuristics
To implement our optimization in an industrial CTS flow, we implement three heuristics
  Algorithm 1: Extract top-level clock tree
  Algorithm 2: Create Steiner points
  Algorithm 3: Insert buffers

## Slide 12: Extract Top-Level Clock Tree
Inputs
  Initial clock tree; cells in the tree are vertices and connections between them are edges
  List of vertices that belong to CLCs
Algorithm description
  Obtain transitive fanins of all CLCs
  Remove clock routes to the fanin cells
  Remove buffers and reconnect nets accordingly
Output
  List of top-level clock cells and connections between them

## Slide 13: Output of Algorithm 1
CLC
FF group 1
CLC
FF group 2
CLC
CLC
Algorithm 1

## Slide 14: Create Steiner Points
Inputs
  Top-level clock tree
  List of vertices that belong to CLCs
Algorithm description
  Find pin-pair that minimize the sum of the difference in sink latency and the delay due to Manhattan distance
  Merge the pin-pair that has minimum sum of difference by inserting a new Steiner point
  Repeat until all driving pins have a single connection
Output
  A binary top-level clock tree and connections between them

## Slide 15: Output of Algorithm 2
i
j1
j2
j3
j4
j1.L = j2.L = j3.L << j4.L
i
j1
j2
j3
j4
j2'
i
j1
j2
j3
j4
j2'
j1'
i
j1
j2
j3
j4
j2'
j1'
j4'
i
j1.L
j3.L
j2.L
j4.L
Manhattan distance & sink latency

## Slide 16: Insert Buffers
Inputs
  Two pin nets of top-level clock tree
  Required delay of each nets
Algorithm
  Calculate the number of buffers required to meet the delay target as a function of net and buffer delays
  Calculate the minimum wirelength required to insert the number of buffers
  Determine whether to insert in L-shape or U-shape manner
Output
  Two pin nets of top-level clock tree that buffers are inserted
Algorithm 3
Algorithm 3
L-shape
U-shape

## Slide 17: Outline
Motivation and Previous Work
Our Approach
Experimental Setup
Results and Conclusions

## Slide 18: CTS Testcase Requirements
Realistic and resemble clock trees typically seen in SoC blocks
Include CLCs and top-level hierarchies
Combinational logic and critical paths across sink groups
Multiple clock roots and generated clocks

## Slide 19: Our CTS Testcases
We develop generators for high-speed CTS testcases typically found in CPU/GPU blocks in modern SoCs
Implement clock roots that are outputs of PLLs as well as crystal oscillators
Implement different types of CLCs
  Glitch-free clock MUX
  Dividers
  Clock-gating cells
Multiple generated clocks for debug, tracing, IO, peripherals

## Slide 20: Examples of CTS Testcases
DIV2
clk
DIV2
DIV4
DIV8
scan_clk
m_clk
CGC
CGC
MUX
MUX
MUX
MUX
CGC
SINKS
MUX
MUX
SINKS
SINKS
SINKS
MUX
MUX
DIV4
DIV2
DIV8
CGC
scan_clk
CGC
CGC
CGC
clk
m_clk
MUX
SINKS
SINKS
SINKS
MUX
MUX
MUX
Clocks to all sink groups are generated clocks
Top-level has up to two levels of hierarchy
Reconvergent paths
Top-level has up to two levels of hierarchy

## Slide 21: Experimental Setup
Six high-speed testcases
P&R tool is an industry tool
CTS uses MCMM scenarios
Timing analysis tool is Synopsys PrimeTime
LP-solver is CPLEX
Flow implemented in Tcl

## Slide 22: Operating Conditions
Parameters | Value
PVT corner for setup @ 1.25GHz | SS, 0.85V, 125C
PVT corner for hold @ 1.25GHz | FF, 1.05V, 125C
PVT corner for setup @ 1.67GHz | SS, 1.10V, 125C
PVT corner for hold @ 1.67GHz | FF, 1.30V, 125C
Max. transition for clock paths | 55ps
Max. transition for data paths | 12.5% of clock period
Timing derate on net delay (early/late) | 0.90/1.19
Timing derate on cell delay (early/late) | 0.90/1.05

## Slide 23: Our Optimization Flow
Placed design
CTS
Remove buffers from top-level tree
CLCs placement & buffer insertion
Placement legalization
Route top-level clock
Routing + optimization
Routing + optimization
Compare post-route metrics
Reference CTS flow
Our optimization flow
Post-CTS opt
Initial clock tree
Post-CTS opt
DRC & timing fix
DRC & timing fix

## Slide 24: Outline
Motivation and Previous Work
Our Approach
Experimental Setup
Results and Conclusions

## Slide 25: Results: Improved Timing
Our formulation focuses on minimizing setup WNS
Improved setup WNS up to 320ps
Hold WNS is worsen but < 70ps
Chart: Setup WNS (ns)
| T1 | T2 | T3
Reference | -0.58 | -0.32 | -0.19
Optimized | -0.46 | 0 | -0.18
Chart: Hold WNS (ns)
| T1 | T2 | T3
Reference | -0.04 | 0 | 0
Optimized | -0.11 | -0.04 | -0.05

## Slide 26: Results: Improved WL, Power
Metric | T1 | T2 | T3
Wirelength (WL) | 46% | 41% | 51%
Switching Power | 23% | 15% | 28%

## Slide 27: Conclusions
Industry tools do not optimize the top-level clock tree always
We develop an optimization formulation for the top-level tree and solve it using three heuristics
We develop realistic high-speed CTS testcases typically seen in clock trees of CPU/GPU
Our optimization flow improves setup WNS by up to 320ps, wirelength by up to 51% and dynamic power by up to 28%
Ongoing works include
  Handling obstacles
  Accounting for optimal buffering solutions
  Creating testcases for other important SoC elements
  Joint optimization of the top- and bottom-level trees

## Slide 28: Thank You