## Slide 1: New Game, New Goal Posts: A Recent History of Timing Closure
Andrew B. Kahng
UCSD CSE and ECE Departments
abk@ucsd.edu
http://vlsicad.ucsd.edu

## Slide 2: What is Timing Closure?
Most critical phase of modern system-on-chip implementation
  No timing closure = no tapeout
Timing closure is end result of
  Years of methodology/script/signoff development
  Months of block- and top-level final physical implementation
  Weeks of final pass including manual noise, DRC fixes
Changes
  Process/device technology
  Modeling standards
  EDA tooling
  Design methodology
  Signoff criteria
Demand for innovations in timing closure

## Slide 3: Agenda
Timing Closure and New Contexts
Example Challenges
Example Near-Term Mitigations
Futures and Conclusions

## Slide 4: Traditional View of Timing Closure
N. MacDonald, Broadcom Corp., “Timing Closure in Deep Submicron Designs”, 2010 DAC Knowledge Center article
TOP-LEVEL NETLIST / SPEF
BLOCK-LEVEL NETLIST / SPEF
Timing Closed
Static Timing Analysis for all Modes / Corners
About 5 iterations
Violation Classes Addressed for Each Iteration (in order of priority)
(1) Electrical Rule Violations
(2) Noise Violations
(3) Setup Violations
(4) Hold Violations
Breakdown of Timing Violations on per Block Basis
Manual Repair of Timing Failures
(1) Vt Swap, Resizing, Buffer Insertion, NDR Changes, Useful Skew
Operations Permitted at Each Iteration (in order of preference)
(2) Vt Swap, Resizing, Buffer Insertion, NDR Changes
(3) Vt Swap, Resizing, Buffer Insertion
(4) Vt Swap, Resizing
(5) Vt Swap

## Slide 5: Context I: Race to End of Roadmap
Paper model to v1.0 SPICE model: ~12 months @N10
Many near-term “red bricks”: ArF, Cu, low-k, …
Foundry-fabless dynamics: who gives up margin ?
Time constants limit design-manufacturing co-evolution
(Years) Tech development, app market definition, architecture/front-end design
(Months) RTL-to-GDS implementation, reliability qualification
(Weeks) Fab latency, cycles of yield learning, design re-spins, mask flows
(Days) Process tweaks, design ECOs
Mismatches among these time constants
Model-hardware miscorrelation
Model guardbanding
Faster node enablement is challenging !!

## Slide 6: Context II: Low-Power Grand Challenge
Low power =
High complexity
multiple supply voltages, power and clock gating, DVFS, MTCMOS, multi-Lgate, …
Increased timing closure burden
Mobility
Big data
Green datacenters
Cloud
Internet of Things

## Slide 7: Recent History
20nm
90nm
45/40nm
28nm
16/14nm
10nm
≤7nm
65nm
BTI
Temp inversion
Noise
MCMM
Maxtrans
EM
AOCV / POCV
PBA
Fixed-margin spec
Multi-patterning
Cell-POCV
MOL, BEOL R 
Dynamic IR
Fill effects
Layout rules
BEOL, MOL variations
Signoff criteria with AVS
SOC complexity
LVF
MIS
Phys-aware timing ECO
Min implant

## Slide 8: Changes I
Rise of MOL and BEOL  resistivity, variability impacts
  Multi-patterning  BEOL corner explosion
Criticality of margin reduction
  Higher-dimensional delay/slew modeling; color-aware P&R + signoff
M2
M1
V1
V0
Mint
Vint
M0G
Fin
Poly
M0A
MOL
M3
M2
M1
spacing
Inter-metal dielectric
Inter-layer dielectric
BEOL
Liberty Variation Format (LVF) shows reduced pessimism

## Slide 9: Changes II
Rapid, near-universal adoption of adaptivity (e.g., AVS)
  “setup violation” becomes hazy; removes “DC” part of timing margin
Path-based analysis with SI enabled is needed earlier in flow
  Runtime, license cost overheads
Performance monitor
Control block
Supply voltage
Circuit
Chart: Runtime (s)
| gba | pba | gba | pba
runtime (s) | 40 | 159 | 17 | 86
AES
JPEG
Runtime of pba vs. gba to find top 10K timing paths with SI enabled (28 FDSOI)
See: http://vlsicad.ucsd.edu/Publications/Conferences/311/c311.pdf
http://vlsicad.ucsd.edu/Publications/Conferences/325/c325.pdf
pba has >4x runtime

## Slide 10: New Game, New Goal Posts?
Design Synthesis/Opt
Architecture; RTL; SP&R; Timing/Noise ECOs
Technology and Design Enablement
SPICE; ITF; Library/IP; Testchips
Analysis
MIS; SHPR; SI; PBA; -dynamic
Modeling
LVF; BEOL/MOL σ’s; Lib groups
Signoff
Yield vs. Slack; MCMM; TBC; AVS; Corner vs. Flat Margins
Timing Closure
OLD
NEW
1 mode
Setup-hold
SI
Cw only
NLDM
MCMM
Cell-POCV / LVF
Dynamic IR
Wide/exploding corners, corner reduction, cross-corners (BEOL Cw, Ccw, RCw, temp, VDD)
Flat margin selection
Noise closure
Aging/AVS

## Slide 11: Agenda
Timing Closure and New Contexts
Example Challenges
Example Near-Term Mitigations
Futures and Conclusions

## Slide 12: Multi-Input Switching
Multi-input Switching (MIS) = More than one input switches at the same time
Conventional timing libraries consider only single-input switching (SIS)
MIS can significantly change arc delays  Need more comprehensive timing model
Chart: FO3 Stage Delay (s)
| Normal VDD | 80% VDD
rise_MIS | 1.684e-11 | 2.456e-11
rise_SIS | 1.561e-11 | 2.251e-11
fall_MIS | 8.494e-12 | 1.229e-11
fall_SIS | 1.45e-11 | 2.166e-11
Technology: 28FDSOI
Design: chained NAND2 gates with FO3

## Slide 13: BEOL Multi-Patterning Impacts
Mandrel
Mwidth
Mspace
Spacer
Swidth
Wire1width = Mwidth
Mx metal
Wire2width = Mspace – 2*Swidth
Floating fill wires
Line-end extensions
Line-end cuts
Mandrel

## Slide 14: Placement-Sizing Interference
New “interferences” between post-layout optimization and P&R
Rules for device layers (FEOL) become considerably more complex and restrictive
  Minimum implant width rules for implant region
  Minimum notch and jog width rule for oxide diffusion (OD)
HVT
HVT
LVT
HVT
LVT
LVT
HVT
HVT
OD
Cell boundary

## Slide 15: Placement-Sizing Interference (cont.)
Drain-to-drain abutment (DDA)
Example solution
Intertwine the historically separate tasks of P&R and post-route optimization
Cell boundary
Active region
Poly
Power/ground
Connection
D
D
D
S
S
D
√
DDA
violation
Min implant width
violation
Min implant width
violation
Min jog/notch width
violation

## Slide 16: Corner Explosion
Operating modes: nominal, turbo, LP1, LP2 …
FE corners: FF, FFG, FS, SF, TT, SSG, SS …
BE corners: C-worst, Cc-worst, RC-best …
Temp corners: temperature inversion corners …
Split corners: memory, logic rails with synch interfaces
×
×
×
×
NOM
Turbo
NOM
lifetime
Vdd
M2
M3
M1
S2
W2
T2
H2
Inter-layer dielectric
Inter-metal dielectric
H1
T1
T3
 | ΔW | ΔT | ΔH
Typical | typical | typical | Typical
C-best | min | min | max
C-worst | max | max | min
RC-best | max | max | max
RC-worst | min | min | min
FF
SS
SSG
FFG
TT
Transistor speed

## Slide 17: Agenda
Timing Closure and New Contexts
Example Challenges
Example Near-Term Mitigations
Futures and Conclusions

## Slide 18: I. Improved Variation Modeling
Monte Carlo path delay simulation shows asymmetric path delay distribution under process variation  Need separate σ values for setup and hold analysis
LVF can handle such non-Gaussian distribution
(from [Rithe et al.])

## Slide 19: II. Tightened BEOL Corners (“TBC”)
Routed design
Timing analysis using conventional BEOL corners (CBC)
ECO
using CBC
violation = 0?
done
Conventional Signoff
No
Routed design
Classify timing critical paths
GTBC
GCBC
ECO
using CBC
Timing analysis using TBC
violation = 0?
Timing analysis using CBC
violation = 0?
ECO
using TBC
done
Our work
No
No
[ICCD14]
Notes: This slide summarizes our approach to reduce the cost of pessimism. In a conventional flow, given a routed design, we will run timing analysis. If there are timing violations, we will fix them in the ECO step. In this work, we first analyze and classify the timing critical paths into two groups. GTBC are the paths which have enough wire averaging and GCBC are those which do not. For the paths in GTBC, we signoff these paths using tightened BEOL corners. For the remaining paths, we will use the conventional BEOL corners. Since a lot of paths will use TBC, this makes the timing signoff a lot easier.

## Slide 20: Pessimism in Conventional BEOL Corners (CBC)
Assumption: a max (setup) path pj is “safe” when the delay evaluated at a given CBC is larger than nominal delay + 3σj dj(YCBC) ≥ 3σj + dj(Ytyp)
For a given path, we can compare the statistical delay variation and the delay obtained from a given CBC αj = 3σj / Δdj(YCBC) Δdj(YCBC)= [dj(YCBC) - dj(Ytyp)] YCBC  {Ycw, Ycb, Yrcw, Yrcb}
A small αj implies there is a large pessimism
delay
-3σ
dj(YCBC)-dj(Ytyp)
3σj
Large pessimism
Notes: To quantify the pessimism of the conventional BEOL corner, we assume that a setup critical path is safe when the delay at a CBC corner is larger than the nominal delay plus three sigma delay variation.
For a given path, we can compare the statistical delay variation and the delay at a CBC corner to obtain a scaling factor “alpha”. The value of alpha is an indicator of pessimism. For example, when the alpha is small, it means that the delta delay at a corner is larger than the mean plus 3sigma delay variation. Therefore, when the alpha is small, there is a large pessimism.

## Slide 21: Scaling Factor α  Delay Variation @Cw,RCw
Paths with small Δdrcw and Δdcw have large α
E.g., there are αj > 0.6 when ((Δdrcw < 3%) AND (Δdcw < 3%))
Identify paths for tightened BEOL corners based on Δdrcw and Δdcw
α
Δd(Ycw)/d(Ytyp)
Δd(Yrcw)/d(Ytyp)
Notes: As shown in the figure, we figure out that the paths with small delta delay at the C-worst and RC-worst corners have a large alpha. For example, the alpha is larger than 0.6 when delta delay at the C-worst and RC-worst corners are smaller than 3% of the nominal delay. This means that by checking the delta delay we can identify the paths for tightened corner.

## Slide 22:  Practical Filter for TBC-Amenable Paths
Acw
Arcw
Gtbc = paths which can be safely signed off using tightened corners: (Path with (Δdcw larger than Acw)) OR (Path with (Δdrcw larger than Arcw))
Δd(Ycw)/d(Ytyp)
Δd(Yrcw)/d(Ytyp)
Notes: Based on the analysis, we propose to filter the paths by using two threshold values. When the delta delay of a path at the Rcworst is larger than the threshold value Arcw OR if the delta delay at Cworst is larger than the Acw, we put the path in the group Gtbc, which will use the tightened corner.

## Slide 23: Benefits of Tightened BEOL Corners
WNS and TNS are reduced by up to 100ps and 53ns
  #Timing violations reduced by 24% to 100% [Moore’s Law: 1% / week !]
  TBC-0.6 : more benefits
  Tradeoff between reduced margin vs. #paths which use TBC
Chart: WNS (ns)
| LEON | SUPERBLUE12 | NETCARD
CBC | -0.0458 | -0.1335 | -0.1537
TBC-0.5 | -0.0458 | -0.1335 | -0.14648
TBC-0.6 | 0 | -0.0333 | -0.091184
TBC-0.7 | -0.0103 | -0.0594 | -0.10634
Chart: TNS (ns)
| LEON | SUPERBLUE12 | NETCARD
CBC | -2.519 | -7.2903 | -80.351
TBC-0.5 | -2.519 | -1.9858 | -60.186
TBC-0.6 | 0 | -0.434 | -27.039
TBC-0.7 | -0.0432 | -0.8938 | -36.337
Chart: #Timing violations
| LEON | SUPERBLUE12 | NETCARD
CBC | 170 | 246 | 1422
TBC-0.5 | 170 | 35 | 1229
TBC-0.6 | 0 | 20 | 1078
TBC-0.7 | 12 | 19 | 1276
Notes: This slide shows our experimental results for a 28nm technology. In this experiment, we try different tightened corner, TBC-0.5, 0.6 and 0.7. A smaller number means the tightened corner has smaller variation compared to the CBC. For example, TBC-0.5 means the variation in the TBC is about half of that in CBC. The results show that, by using the tightened corners, we can reduce WNS and TNS by upto 100ps and 53ns. Meanwhile, the number timing violations are also reduced. From the figure, we can see that the tightened corner with an alpha value 0.6 is better compared to an alpha value 0.5 and 0.7. When the alpha value is too small, not many paths can use the tightened corners because many of the paths do not have enough averaging to use the tightened corner. But when the alpha value is too big, the different between the conventional corner and tightened corner becomes smaller, so there is not much benefit to use the tightened corner.

## Slide 24: III. Flexible FF Timing  Margin Recovery
setup
c2q
hold
c2q
C2q-setup-hold surface
setup
hold
c2q
Setup time, hold time and clock-to-q (c2q) delay of FF ⇒ values interdependent, but NOT fixed
Flexible FF timing model can exploit operating (function/test) modes ⇒ “Free” pessimism reduction in STA
Sequential LP:
  setup-c2q opt
  hold-c2q opt
Goal: Find best {setup, hold, c2q} for each FF instance
[ISQED14]
hold
c2q1
c2qn
...
setup-hold-c2q
flexible model
setup-hold-c2q
fixed model
Notes: For conventional FF timing model, setup/hold/clock-to-q delay is given as fixed values according to input slew and output load. However, setup and hold times and c2q delay are not single values. That is, there’s a tradeoff relationship among them.
As shown in the right figure, setup and hold times can have smaller values at the expense of c2q delay.
Also, there’s a tradeoff between setup and hold times.
Combining with c2q delay, we can have multiple setup-hold time curves.
In this work, we try to use these tradeoff relationship for timing analysis.
With flexible FF timing model, we can reduce pessimism in conventional timing analysis.

## Slide 25: Flexible Timing Model  Reduce Pessimism
Independent datapaths in PBA: using fixed FF timing model loses performance optimization opportunity
470ps
480ps
460ps
470ps
460ps
480ps
FF3
FF1
FF2
setup: 10ps
c2q: 20ps
setup: 10ps
c2q: 20ps
setup: 20ps
c2q: 10ps
Total: 500ps
Total: 500ps
Total: 500ps
20ps
10ps
10ps
20ps
 520ps?
 500ps!

## Slide 26: Improved Timing Signoff Flow
Extract path timing information
LP formulation
with flexible flip-flop timing model
Solve Sequential LP
(STA_FTmax , STA_FTmin)
Annotate new timing model
for each flip-flop
Solution
Netlist (and SPEF, if routed)
Timing signoff with annotated timing
Takeaways
Fix timing violations “for free”
48ps average improvement of slack over 5 designs in a foundry 65nm technology
Next
Better exploitation of disjoint cycles/modes
More accurate modeling of setup-hold-c2q tradeoff
Circuit optimization should natively exploit FF timing model flexibility
Notes: This chart shows the overall flow of our proposed method.
With a placed and/or routed netlist, we extract path timing information.
Based on that, we formulate LP with pre-characterized flexible flip-flop timing model.
After solving the LP, we annotate the new timing values to each flip-flop in the design.
Finally, we perform timing signoff with the annotated timing.

## Slide 27: IV. Better Signoff Definition
VBTI : Voltage for BTI-aging estimation
Vlib : Supply voltage for timing library characterization
Vfinal: Vdd of a circuit with AVS at end-of-lifetime
Vlib
VBTI
Derated library
|Vt|
Circuit implementation and signoff
circuit
BTI degradation and AVS
Vfinal
?
Chicken & Egg Loop
  VBTI and Vlib depend on aging during AVS (Vfinal)
  Vfinal depends on circuit
  Circuit implementation depends on VBTI and Vlib
[DATE13]

## Slide 28: Observations and Heuristics
  Observation #1: Vfinal is not sensitive to cells along the timing-critical path
  Observation #2: ΔVt with a constant Vfinal throughout lifetime ≈ adaptive Vdd
Solve “Chicken & Egg Loop” by having VBTI = Vlib = Vheur≈ Vfinal
Heuristic #1: Use average of critical path replicas to estimate Vfinal (Vheur)
Heuristic #2: approximate Vdd in AVS by constant Vheur

## Slide 29: Experimental Results: A “Knee” Point
 | Low Vlib | High Vlib
Low VBTI | Slower circuit Less aging | Faster circuit Less aging
High VBTI | Slower circuit More aging | Faster circuit More aging
Experiment setup:
DC/AC BTI @ 125°C
32nm PTM technology
4 benchmark circuit implementations
Optimistic aging library  large power penalty
Our method finds “Knee” point for balanced area and power tradeoff
Overly pessimistic aging library  large area penalty
Ignore AVS  larger area

## Slide 30: Agenda
Timing Closure and New Contexts
Example Challenges
Example Near-Term Mitigations
Futures and Conclusions

## Slide 31: Food for Thought
EDA tool innovation in timing closure space has been helpful
  E.g., physically-aware ECO, dynamic IR-aware STA, …
Process and device innovation will continue to challenge timing closure
  “Actual” foundry-specific metal fill early in design
  Process enhancement (e.g., air gap)
  Self-heating from high current density in FinFET
What about SoC-level design closure complexity?
  Better timing budgeting, constraints evolution, coordination of top- vs. block-level effort

## Slide 32: Look Out For …
Margin becomes scarcer
  Low-hanging fruits being rapidly harvested
  Critical: better analysis accuracy, model-hardware correlation at extreme modes
BEOL + MOL + Multi-Patterning
  Resistance scaling, pitch scaling, variation  delicate balancing act
  Need better modeling and corner definition
  Bring together library, placement, routing, STA
Variation modeling
  Statistical SPEF
  LVF, unified model of PVT variation (reduce #libraries!)
Signoff
  Wide adoption of adaptivity (e.g., AVS) with new signoff criteria/goals
  Design-specific tightened corners
  Cross corners (FSG, SFG)
Thermal and stress?
3D integration!

## Slide 33: Thanks to …
Rob Aitken for inviting this talk
Christian Lutkemeyer, Isadore Katz, Sorin Dobre, Tuck-Boon Chan, Kwangok Jeong, Nancy MacDonald and John Redmond for discussions and inputs
UCSD VLSI CAD Laboratory students: Hyein Lee, Jiajia Li, Mulong Luo, Yaping Sun, Wei-Ting Jonas Chan

## Slide 34: THANK YOU !

## Slide 35: Backup Slides

## Slide 36: Delay Variation
α
α
Δdelay at C-worst [d(Ycw) – d(Ytyp)] / d(Ytyp)
Some paths have α > 1.0  a CBC can underestimate delay variations
But these paths have larger delays at the other corner
C-worst corner underestimates delay variations, but these paths are dominated by the RC-worst corner
α < 1.0  delay variations are covered by the RC-worst corner
C-worst is the dominant corner Δdelay at C-worst > Δdelay at RC-worst
RC-worst is the dominant corner Δdelay at RC-worst > Δdelay at C-worst
Δdelay at RC-worst [d(Yrcw) – d(Ytyp)] / d(Ytyp)
Notes: In these figures, we show the alpha value for different critical paths at the C-worst corner and the RC-worst corner. A red dot is a path which has a large delta delay at the C-worst corner, and a blue dot is a path which has a larger delta delay at the RC-worst corner. In this experiment, we can see that some of the paths have alpha larger than 1.0. This means that the Cworst corner actually underestimates the delay variation compared to the statistical analysis. However, these paths are dominated by the RC-worst corner, and the alpha value at the RC-worst corner is smaller than one.

## Slide 37: Aging Signoff Corner with AVS
Timing signoff: ensure circuit meets performance target under PVT variations & aging
Conventional signoff approach:
  Analyze circuit timing at worst-case corners
  Fix timing violations, re-run timing analysis
What is the Vdd signoff corner for aging + AVS?
 |  | Circuit performance model (Vlib) | 
 |  | Low Vdd | High Vdd
BTI model (VBTI) | Low Vdd | Slower circuit Less aging | Faster circuit Less aging
 | High Vdd | Slower circuit More aging | Faster circuit More aging
?
?
Too optimistic
Too pessimistic

## Slide 38: Minimum Implant Area Constraint
Small feature sizes cannot be patterned with ArF
One example of challenges: control of implant area
 Minimum implant area is constrained
  A narrow cell cannot be sandwiched
  with different Vt cells
250nm
365 nm
248 nm
193 nm
180nm
130nm
90nm
65nm
45nm
436 nm
32nm
22nm
Source: L. Liebmann and A. Torres, DAC, 2011
Vt1
Vt2
Vt2
Min implant area constraint
Violation