## Slide 1: Revisiting and Bounding the Benefit From 3D Integration
Wei-Ting J. Chan†, Andrew B. Kahng†‡ and Jiajia Li†
†ECE and ‡CSE Departments, UC San Diego
{wechan, abk, jil150}@ucsd.edu
Notes: Thanks you for the introduction.

## Slide 2: Outline
Motivation
Previous Work
Implementation in Various Dimensions
Netlist Structure vs. 3D Benefit
Conclusions

## Slide 3: Motivation
3DIC is a promising technology in “More-than-Moore” era
3DIC with > 2 tiers is expected to achieve more benefits
  [Song15]: Three-tier 3DIC achieve 15% more power reduction compared to two-tier 3DIC
But: No upper bounds on power and area benefits from 3DIC have ever been established !
Goal: study upper bound of power and area reduction for 3DICs

## Slide 4: Outline
Motivation
Previous Work
Implementation in Various Dimensions
Netlist Structure vs. 3D Benefit
Conclusions

## Slide 5: Previous Work (Power Benefit)
Many previous works on 3DIC optimization
  More details are given in Table I of the paper
Evaluations include both power and wirelength benefits
Chart: Year
| 2013 | 2011 | 2015 | 2015 | 2013 | 2014 | 2014 | 2012 | 2012 | 2013 | 2015 | 2013 | 2013 | 2014 | 2015 | 2010
2-tier | 9 | 15 | 39 | 17 | 0 | 21 | 20 | 0 | 0 | 22 | 3 | 7 | 37 | 37 | 13 | 35 | 20 | 19 | 0 | 13
3-tier | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 36 | 0
4-tier | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 28 | 23 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 6: Previous Work (Wirelength Benefit)
Chart: Year
| 2007 | 2011 | 2015 | 2007 | 2003 | 2006 | 2013 | 2014 | 2009 | 2010 | 2009 | 2012 | 2012 | 2012 | 2013 | 2013 | 2013 | 2014 | 2010 | 2010
2-tier | 50 | 13 | 46 | 0 | 50 | 30 | 26 | 26 | 9 | 20 | 4 | 37 | 0 | 0 | 32 | 25 | 16 | 48 | 14 | 33 | 19 | 40 | 0 | 21
3-tier | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 42 | 0
4-tier | 0 | 0 | 0 | 0 | 0 | 54 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 41 | 28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Many previous works on 3DIC optimization
  More details are given in Table I of the paper
Evaluations include both power and wirelength benefits
No previous work proposes upper bounds on 3DIC power and area reductions
Chan et. al derive an upper bound of 67% on WL reduction

## Slide 7: Outline
Motivation
Previous Work
Implementation in Various Dimensions
Netlist Structure vs. 3D Benefit
Conclusions

## Slide 8: Implementation in Various Dimensions
Key idea: Infinite dimension gives us a bound on what 3 dimensions can deliver
Infinite dimension: netlist optimization with zero wireload model
3D (w/ N tiers): placement and routing with shrunk LEF (by 1/) and annotated TSV RC
Best 2D conventional implementation: vary key parameters  select best solution
  Parameters = synthesis frequency/utilization, placement utilization, BEOL options
Pseudo-1D: placement and routing with large layout aspect ratio (e.g., 10:1)

## Slide 9: Benefit Evaluation Flow: 3DIC (w/N Tiers)
Cells and BEOL are scaled according to tier number T (X/Y to )
2D P&R are spilt into M x M to apply FM-based partitioning
RC of TSV are annotated according to tier number
  RC of cut nets = RC of 6 metals N + TSV (N-1)
Cell and BEOL LEFs
Scaled X/Y to
2D P&R
Split floorplan into M x M grids
FM-based min-cut partition for N tiers
RC-annotation
for TSVs
Incremental
optimization
Power Evaluation

## Slide 10: Benefit Evaluation Flow: Conventional 2D
Chart: Clock period (synthesis) (ns)
| 0.72 | 0.8 | 0.88
0.8 ns | 119.145 | 123.1588 | 128.1768
1.0 ns | 96.8421 | 92.8367 | 90.2178
Clock period (PnR)
Synthesis frequency
Tight (loose) timing: Slightly smaller (larger) synthesis clock period  Smaller power after P&R
Chart: Placement utilization
| 0.6 | 0.7 | 0.8 | 0.9
 | 95.7421 | 92.8367 | 90.7714 | 91.2585
Placement utilization
Unimodal model:
Too compact  routing congestion
Too sparse  longer wirelength
Search within multiple design parameters to find optimum implementations

## Slide 11: Benefit Evaluation Flow: Pseudo-1D
Pseudo-1D implementations use floorplans with very large aspect ratios
Routing along the long side is difficult
PnR Aspect ratio = 10:1 to emulate 1D placement
Limited routing channels along the long side

## Slide 12: Infinite-Dimension Bound on 3D Power Benefits
Chart: Power (mW)
| 0.8 | 0.9 | 1 | 1.1000000000000001
Pseudo1D | 20.6927 | 16.1989 | 14.172 | 11.9503
2D | 17.5641 | 14.1392 | 12.3755 | 10.6273
3D (2 tier) | 16.7947 | 13.6175 | 11.2579 | 9.8955
3D (3 tier) | 15.9435 | 12.6794 | 10.9315 | 9.7643
3D (4 tier) | 14.7266 | 11.8899 | 10.76 | 9.121
infiD | 11.2415 | 9.7387 | 8.0244 | 7.4152
Chart: Power (mW)
| 0.6 | 0.7 | 0.8 | 0.9
1D | 51.4081 | 39.9703 | 32.2447 | 27.2588
2D | 46.5914 | 36.083 | 30.587 | 26.0559
3D_2 | 42.16 | 33.6948 | 27.9289 | 24.1615
3D_3 | 40.5429 | 31.8559 | 25.9245 | 22.5286
3D_4 | 38.6544 | 29.7242 | 24.7336 | 21.4045
infiD | 28.0798 | 22.5067 | 19.1162 | 16.9203
CORTEX M0
AES
Iso-performance power comparison among implementations in different dimensions
Gaps between infinite dimension vs. 2D  maximum 3D benefits = 36% and 20% for M0 and JPEG
36%
20%
clock period (ns)
clock period (ns)
infD

## Slide 13: Infinite-Dimension Bound on 3D Area Benefits
Iso-performance area comparison among implementations in different dimensions
3D integration offers very small (< 10%) area benefits over 2D
3D integration may have converted area benefit into power benefit (e.g., buffer sizing or duplication)
Chart: Area (um2)
| 0.8 | 0.9 | 1 | 1.1000000000000001
Pseudo1D | 10506.043 | 9527.56 | 9209.654 | 8651.464
2D | 9793.752 | 8951.592 | 8944.721 | 8608.43
3D_2 | 9559.62 | 8873.084 | 8622.059 | 8565.005
3D_3 | 9500.999 | 8760.837 | 8695.075 | 8482.299
3D_4 | 9441.106 | 8715.806 | 8672.896 | 8478.062
infiD | 8842.757 | 8378.034 | 8267.961 | 8125.199
3D (2 tier)
3D (3 tier)
3D (4 tier)
Chart: Area (um2)
| 0.6 | 0.7 | 0.8 | 0.9
1D | 10705.085 | 9864.824 | 9279.104 | 8914.906
2D | 10197.79 | 9302.718 | 9053.458 | 8931.198
3D_2 | 9814.628 | 9369.584 | 8976.735 | 8820.752
3D_3 | 9756.237 | 9302.569 | 8944.751 | 8786.486
3D_4 | 9736.586 | 9173.596 | 8850.786 | 8705.556
infiD | 9124.569 | 8764.159 | 8561.416 | 8517.042
CORTEX M0
AES
clock period (ns)
clock period (ns)
10%
10%
infD

## Slide 14: Impact of Clock Skews on 3D Benefits
Implementations with higher dimensions are more susceptible to clock skews
  Lower wire delays lead to less hold time margin
  P&R added more buffers to reduce the skew
AES
CORTEXM0
2D (0%)
2D (0%)
Clock uncertainty (% of clock period)
11%
6%
1%
5%
-3%
-21%
Power (mW)
Power (mW)
infD

## Slide 15: Outline
Motivation
Previous Work
Implementation in Various Dimensions
Netlist Structure vs. 3D Benefit
Conclusions

## Slide 16: Netlist Structure vs. 3D Benefits
Observation: 3D benefits vary across designs
Goal: Find parameter(s) to indicate 3D benefits
Studied parameters
  Timing slack distribution (Low correlation)
  Fanout / fanin distribution (Low correlation)
  Rent parameter (i.e., Rent exponent) (High correlation)
Rent Parameter
Empirical observation T = t∙gp
  T = #terminals
  t = constant
  g = #gates
  p = Rent exponent (indicator of netlist complexity)
“Surface area to volume” power law: e.g., has p = 0.5

## Slide 17: New Connection between Rent and 3D Benefit!
More complex netlists demonstrate higher max 3D power benefit
Benefits increase for higher-dimension implementations
Chart: Placement-based Rent parameter
| 0.63 | 0.66 | 0.69 | 0.71 | 0.74
3D (2 tier) | 0.043002 | 0.057652 | 0.059351 | 0.078565 | 0.11651 | 0.082242
3D (3 tier) | 0.070921 | 0.098836 | 0.10258 | 0.1346 | 0.18925 | 0.20328
3D (4 tier) | 0.099876 | 0.12518 | 0.13625 | 0.16719 | 0.24012 | 0.2497
InfiDi | 0.21841 | 0.26248 | 0.29809 | 0.33867 | 0.42275 | 0.45426
Rent (input / actual) | Power (mW) | Area (um2)
0.50 / 0.63 | 46.4 (100%) | 39552 (100%)
0.55 / 0.66 | 46.8 (101%) | 40262 (102%)
0.60 / 0.69 | 46.7 (101%) | 40404 (102%)
0.65 / 0.71 | 47.4 (102%) | 40532 (102%)
0.70 / 0.74 | 46.9 (101%) | 40607 (103%)
Higher complexity:
Max benefit = 42%
Lower complexity:
Max benefit = 22%
Power benefit to 2D
Iso-power post-synthesis netlists
More complex netlists
infD

## Slide 18: Rent and 3D Benefit: Real Designs
VGA
JPEG
LEON3MP
CORTEX M0
AES
Placement-based Rent exponent is well correlated with 3D benefits
Rent parameter is possibly a simple indicator of 3D power benefits
Placement-based Rent parameter

## Slide 19: Rent Parameter Modulation for 3D
Attempt to synthesize same design into netlists of different Rent parameters
  Binning cells in 28FDSOI into four types {2-input, 3-input, 4-input, >4-input}
Rent parameter modulation: scale area of cells by different ratios
Rent | 2-input | 3-input | 4-input | >4-input
0.600 | 1 | 0.5 | 1 | 1
0.605 | 2 | 0.5 | 1 | 1
0.611 | 1 | 1 | 1 | 1
0.653 | 2 | 1 | 0.5 | 0.5
0.656 | 2 | 0.5 | 0.5 | 0.5
0.663 | 1 | 0.5 | 1 | 0.5
Example of Rent parameter modulation in commercial synthesis tool

## Slide 20: Ongoing: Dimension-Aware Implementation
Observations:
  Rent parameter increases when more cells with high pin counts
  Observe correlated Rent parameter vs. % of >3-input cells
Future work:
  Direct control in academic logic synthesizer
Design: JPEG
Placement-based Rent parameter

## Slide 21: Ongoing: Dimension-Aware Implementation
Design: JPEG
Shapes = set of implementations w/ different Rent; Colors = dimensions
infD (≈ post-synthesis) power: x > +, 3D power: x ≈ +, 2D power: x < +
Implementation | Rent
O | 0.600
X | 0.605
 | 0.611
 | 0.653
 | 0.656
 | 0.663
Placement-based Rent parameter
infD

## Slide 22: Takeaways
  Synthesis optimization changes Rent parameter of netlists
  Design implementation (synthesis, P&R) should be aware of dimension
    Netlists with simple connections can be implemented in any dimension
    Netlists with complex connections are more suitable for 3D implementation
    (This is not surprising)

## Slide 23: Outline
Motivation
Previous Work
Implementation in Various Dimensions
Netlist Structure vs. 3D Benefit
Conclusions

## Slide 24: Conclusion and Future Goals
Revisit 3D power and area benefit
Implementation with infinite dimension upper-bounds 3D power and area benefits
Correlation between placement-based Rent parameter and 3D benefits
Ongoing/future work: Dimension-aware design implementation