## Slide 1: IncPIRD: Fast Learning-Based Prediction of Incremental IR Drop
Chia-Tung Ho and Andrew B. Kahng
UC San Diego VLSI CAD Laboratory
Notes: Thank you for the kind introduction. My advisor is Andrew Kahng at UCSD.
My work is about predicting incremental IR drop when ECOs are made to the floorplan or the PDN structure.

## Slide 2: Outline
Background and Problem Statement
Related Work
Our Methodology
Experimental Setup and Results
Conclusion
Notes: In my talk, I start with background and problem statement.
I will review some related works, then describe our learning-based methodology

## Slide 3: Challenge: Incremental IR Analysis for Floorplan/PDN
To meet PPA of modern high-performance designs, many iterations of PDN design, IR analysis, and Floorplanning/Placement are needed
Key Challenge: Fast and accurate incremental IR prediction to reduce design time and improve convergence
A12 SoC
Notes: My work addresses the challenge of INCREMENTAL IR analysis.
In SOCs such as from companies like Apple, required PPA depends on [CLICK] MANY ITERATIONS
among PDN design, IR analysis, and Floorplaning/Placement.
[CLICK] The challenge is to reduce the time of this loop, to allow more design optimization and better convergence in the schedule. So, we want fast and accurate incremental IR prediction .

## Slide 4: Background: Fixing IR Drop Violations
Traditional layout-based techniques for ﬁxing IR drop violations:
  macro/cell block movement
  macro/cell block change
  modiﬁcation of the PDN to have a denser grid
  adding/moving power pads
Layout view
Simulation view
MNA System Equations: Gx=b
Notes: From the LAYOUT perspective, power is delivered from flip-chip package through power bumps, to transistors – through the PDN mesh.
From the SIMULATION perspective, resistances are extracted from metal segments and tap current sources are modeled from cell/macro blocks.
KCL, KVL, and branch equations in the circuit network give us the [CLICK] Modified Nodal Analysis system equations, Gx=b.
Here, G is the NxN conductance matrix, x is the nodal voltage vector, and b is the current source vector.
SO: HOW do physical designers fix IR drop violations? Let’s look at these methods briefly.
1 min

## Slide 5: Background: Fixing IR Drop Violations
Traditional layout-based techniques for ﬁxing IR drop violations:
  macro/cell block movement
  macro/cell block change
  modiﬁcation of the PDN to have a denser grid
  adding/moving power pads
Layout view
Simulation view
A
B
F
D
E
C
 Tap current source location / value change
IR Hot Spot
A
E
F
D
B
C
MNA System Equations: Gx=
Notes: Given an IR Drop Map, aggressor macro/cell block movement or change can mitigate the worst IR drop.
[Click] This is [POINT TO SLIDE] because the LOCATION or VALUE of tap current sources will be changed.

## Slide 6: Background: Fixing IR Drop Violations
Traditional layout-based techniques for ﬁxing IR drop violations:
  macro/cell block movement
  macro/cell block change
  modiﬁcation of the PDN to have a denser grid
  adding/moving power pads
Layout view
Simulation view
 Resistance network changes
A
B
F
D
E
C
A
B
F
D
E
C
MNA System Equations: x=
IR Hot Spot
Notes: If there are available interconnect resources, designers can change the PDN to a denser grid.
[Click] This changes the resistance network in the simulation view.
And, it also increases the dimension of the conductance matrix, G.

## Slide 7: Background: Fixing IR Drop Violations
Traditional layout-based techniques for ﬁxing IR drop violations:
  macro/cell block movement
  macro/cell block change
  modiﬁcation of the PDN to have a denser grid
  adding/moving power pads
Layout view
Simulation view
 voltage source location change
A
B
F
D
E
C
Add power pad
A
B
F
D
E
C
IR Hot Spot
MNA System Equations: x=
Notes: Last, the designer can assign an additional power bump near the IR hotspot if there is an available bump.
[Click] This will change the voltage source location, conductance matrix, and current source vector as well.
OUR GOAL is to predict the new IR drop map after any of these layout-based IR fixing techniques.

## Slide 8: Problem Statement
Given: LEF, DEF, current distribution, ANSYS RedHawk (RH) v15.1 technology ﬁle, RH IR drop ﬁle, and RH power pad ﬁle of ﬂoorplan design
Train Incremental IR Predictor: Extract features from input and train a learning-based model to predict static IR drop
Output: Static IR drop of each power node that has tap current source attached
XGBoost
Train
Given
Output: IR drop prediction
LEF, DEF,
RedHawk Technology,
IR drop, Power pad files
Notes: Here is our problem statement.
We are GIVEN: LEF, DEF, current distribution, and ANSYS RedHawk technology file, RedHawk IR drop file, power pad file of floorplan.
[CLICK] We WANT TO PREDICT the updated STATIC IR MAP. To do this, we extract features from the input and train a learning-based model. Specifically, our work uses the XGBoost package.
[CLICK] FINALLY, the OUTPUT will be a MAP of updated static IR drop for each power node that had tap current source attached.

## Slide 9: Outline
Background and Problem Statement
Related Work
Our Methodology
Experimental Setup and Results
Conclusion
Notes: Let me now say a bit about related works, and how our work is DIFFERENT.

## Slide 10: Related: Simulation-Based IR Analysis Works
IR drop analysis
  [Zhao02] proposes hierarchical IR drop analysis
  [Chen01] [Chou11] use krylov subspace methodology to solve Gx=b iteratively.
  [Su03] [Huang07] [Zhuo08] [Yang11] exploit multi-grid techniques to solve IR analysis.
  [Qian05] develops random walk algorithms for solving IR analysis.
   Reanalyze modified design as a whole even when the power grid has only been modified locally
Incremental IR drop analysis
  [Sun11] [Chang12] [Lee17] exploit sparse recovery and orthogonal matching pursuit to reduce the dimensionality of incremental IR drop problem
   When design changes significantly, runtime complexity is similar to performing power grid simulation on the entire design
Notes: There are many related simulation-based IR analysis works.
For IR drop analysis, hierarchical method, krylov subspace, and multi-grid technique have been proposed.
However, THESE methods are typically NOT INCREMENTAL: They re-analyze a modified design from scratch, even when the power grid has only been modified locally.
[CLICK] For incremental IR drop analysis, THESE methods use sparse recovery and orthogonal matching pursuit to reduce the dimensionality of the incremental IR drop problem.
But, when the design is changed significantly such as pitch modification of PDN, the runtime complexity is similar to that of performing power grid simulation on the entire design.

## Slide 11: Related: Machine Learning-Based (Incremental) IR Estimation
[Zhang17]: fast power integrity classifier to detect IR/EM hotspots using ML
 Hotspot location and worst IR drop value, both of which may be needed in
PDN design context, are not provided
[Lin18] [Fang18] propose ECO-based dynamic IR drop prediction methods to reduce the TAT for ECO steps involving cell location changes.
 Model retraining for different designs; unclear performance of IR drop
prediction when PDN is modified.
Our method (“IncPIRD”) can predict (updated) IR drop at each instance node without solving Gx=b for entire/significantly modified system.
Can handle layout modifications to macro/cell block locations, PDN structure, and power pads
Can be used across different block/chip sizes and designs without model retraining
Notes: There are ALSO several machine learning-based (Incremental) IR estimation works in recent years.
ZHANG develops a fast power integrity classifier to detect IR/EM hotspots with ML techniques, but does not provide hotspot location and worst IR drop value, which may be needed in PDN design.
LIN and FANG propose ECO-based dynamic IR drop prediction methods to reduce the turnaround time for ECO steps involving cell location changes. These models require retraining for different designs and the model performance is unclear when the PDN is modified.
So, the contributions of our work, which we call “IncPIRD”, are:
First, we predict (updated) IR drop at each instance node without solving Gx=b for the entire system
Second, we handle the above-mentioned types of layout modifications: to macro/cell block locations, PDN structure, and power pads.
Third, IncPIRD can be used across different block/chip sizes and designs without model retraining.
2 and half mins

## Slide 12: Related: Machine Learning-Based (Incremental) IR Estimation
[Zhang17]: fast power integrity classifier to detect IR/EM hotspots using ML
 Hotspot location and worst IR drop value, both of which may be needed in
PDN design context, are not provided
[Lin18] [Fang18] propose ECO-based dynamic IR drop prediction methods to reduce the TAT for ECO steps involving cell location changes.
 Model retraining for different designs; unclear performance of IR drop
prediction when PDN is modified.
Our method (“IncPIRD”) can predict (updated) IR drop at each instance node without solving Gx=b for entire/significantly modified system.
Can handle layout modifications to macro/cell block locations, PDN structure, and power pads
Can be used across different block/chip sizes and designs without model retraining
IncPIRD makes progress toward combining (1) FLEXIBILITY of simulation-based methods with (2) SPEEDUPS and SCALABILITY of machine learning-based methods !!!
Notes: In summary, IncPIRD makes progress toward combining the FLEXIBILITY of simulation-based methods with the SPEEDUPS AND SCALABILITY of machine learning-based methods.
6:40

## Slide 13: Outline
Background and Problem Statement
Related Work
Our Methodology
Experimental Setup and Results
Conclusion
Notes: I will now introduce the IncPIRD methodology.

## Slide 14: IncPIRD Training Flow
Input: LEF, DEF, current distribution, RH technology ﬁle, RH IR drop ﬁle, and RH power pad ﬁle
Output: A learning-based model to predict static IR drop. (gray box)
Objective: Minimize Mean Absolute Error (MAE)
Notes: Here is our IncPIRD training flow.
Given LEF, DEF, current distribution, and ANSYS RedHawk technology file, IR drop file, and power pad file of floorplan:
We extract input features and train our model with Mean Absolute Error objective function as shown in the gray box.

## Slide 15: IncPIRD Prediction Flow
Input: LEF, DEF, current distribution, RH technology ﬁle, RH IR drop ﬁle, and RH power pad ﬁle
Predict: Static IR drop of each power node that has tap current source attached
Model Update Conditions :
  Symbolic IR drop:
  Effective resistance:
Notes: Here is our IncPIRD Prediction flow.
Firstly, the input files are as same as in the training flow.
IncPIRD predicts the IR drop of each power node that has tap current source attached, after incremental modification of the PDN have been made by designers.
Our model update conditions are related to symbolic IR drop and Effective resistance which will be introduced in detail when I describe our robustness experiment.
If the new electrical features do not satisfy the model update conditions, IncPIRD will update the model automatically.
As shown in the BIG LOOP, the iteration between IncPIRD incremental IR prediction AND the PDN layout modification ends when there is no IR violations.

## Slide 16: Input Features
Name | Description
 | Width of the Chip/Block
 | Length of the Chip/Block
 | Pitch of top horizontal metal layer
 | Pitch of top vertical metal layer
 | Pitch of intermediate horizontal metal layer
 | Pitch of intermediate vertical metal layer
 | Pitch of lower metal layer
 | Pulldown component at node n
 | Pullup component at node n
 | Pulldown component of node n’s Neighbor1
 | Pullup component of node n’s Neighbor1
 | Pulldown component of node n’s Neighbor2
 | Pullup component of node n’s Neighbor2
Name | Description
 | Width of the Chip/Block
 | Length of the Chip/Block
 | Pitch of top horizontal metal layer
 | Pitch of top vertical metal layer
 | Pitch of intermediate horizontal metal layer
 | Pitch of intermediate vertical metal layer
 | Pitch of lower metal layer
 | Pulldown component at node n
 | Pullup component at node n
 | Pulldown component of node n’s Neighbor1
 | Pullup component of node n’s Neighbor1
 | Pulldown component of node n’s Neighbor2
 | Pullup component of node n’s Neighbor2
Chip/PDN structural features
Electrical features
Notes: Now that we have seen the big picture of IncPIRD, I will now introduce the input features.
The first part is Chip/PDN structural features, chip width/length and the pitch of PDN metal layers.
[Click] The second part is Electrical features, Pulldown and Pullup component.

## Slide 17: Electrical Features
Pullup Component of node n, :
Pulldown Component of node n, :
An example of
An example of
Name | Description
 | tap current source
 | Effective resistance of minimum-resistance path resistance between power pads and tap current source
 | Effective resistance of minimum-resistance path resistance between power pads and node
 | minimum-resistance path resistance value between tap current source and node
 | Symbolic IR drop value at node
Name | Description
Notes: In this slide, we introduce electrical features.
The first one is Pullup Component. To compute the Pullup Component at node n, we calculate the effective resistance between power pads and node n as shown in the figure.
In this simple example, the Pullup component of node n is calculated with the minimum-resistance path resistances between power pads and node n.
[Click] The second one is Pulldown Component, also called symbolic IR drop. To compute the Pulldown Component at node n, we superpose the effective IR drop caused by each current source.
1 min

## Slide 18: Partition-Based Electrical Features Extraction
Spatial locality characteristics of (flip-chip) power grids
Current load window based internal node calcualtion
Inter-partition current load propagation on boundary node for
Global power pad-aware extraction
Illustration of partitions in the PDN.
Partition Boundary
Current load window
Power pads
Tap current sources
Notes: Here is our partition-based electrical feature extraction methodology.
We exploit the spatial locality characteristics of (flip-chip) power grids.
[Click] In the figure below, there are four partitions and their current windows. The larger current window is used to reduce the Pulldown component error on the boundary nodes.
To extract , we calculate the of internal nodes in the partition by considering the tap current sources in its current load window.
[Click] If on the boundary of one partition exceeds a threshold, its neighboring partitions’ Pulldown component needs to be calculated with the current loads in the partition.
[Click] All of the power pads in the design are used to extract of each partition nodes.
1:40
Extracting 〖𝑃𝐶〗_𝑑𝑜𝑤𝑛:
  For a given partition, we calculate the 〖𝑃𝐶〗_𝑑𝑜𝑤𝑛 of internal nodes of the partition by considering the tap current sources in its current load window.
  If 〖𝑃𝐶〗_𝑑𝑜𝑤𝑛 on the boundary caused by 〖𝐿𝑖𝑠𝑡〗_𝑡𝑎𝑝 of a given partition exceeds the threshold 𝜀_𝑡ℎ, its neighbor partitions are impacted.
Extracting 〖𝑃𝐶〗_𝑑𝑜𝑤𝑛:
  We calculate and extract 〖𝑃𝐶〗_𝑢𝑝 considering all the power pads in design.

## Slide 19: Algorithm
1: Partition the PDN and create the partition database;
2: Calculate original electrical features in the design;
3: Violations = getIRViolations;
4: While Violation > 0 do
5: If Macro/Cell Block Modification then
6: If Add/Move macro/cell block then
7: Update tap current sources location/value;
8: endif
9: Find set of modified partitions, Pmod;
10: Update electrical features in Pmod and Update electrical features of impacted partitions;
11: endif
12: if PDN structure or power pad modification then
13: if PDN structure modification then
14: Update PDN structure database and distribute tap current sources to new PDN power node;
15: endif
16: if power pad modification then
17: Update power pad database;
18: endif
19: Update electrical features of all partitions and Update electrical features of impacted partitions;
20: endif
21: if && then // Model update condition
22: Perform model prediction;
23: else
24: Update model with new DEF, LEF, RedHawk GSR, RedHawk Power Pad, and RedHawk IR report files.
25: endif
26: Violations = getIRViolations;
27:End while
Model prediction/update
Electrical Features Update
Initialization
Notes: This is our algorithm.
[Click] Firstly we partition the PDN and create the database.
[Click] Then, IncPIRD updates the database and extracts the electrical features based on different types of modifications.
Add/Move macro/cell block only needs to update the tap current source location or value.
PDN structure modification needs to update the PDN structure and redistribute the tap current sources to new PDN power nodes.
Power pad modification needs to update the power pad database.
[Click] After electrical feature extraction, IncPIRD will perform IR prediction or model update based on the model update condition.
Then, at an outer loop with the layout engineer, we can continue to make IR fixes in the PDN layout until there are no violations.
1:20

## Slide 20: Electrical Feature Extraction: Scaling Behavior
Name | Description | Name | Description
 | Number of metal layers used in PDN. |  | Number of tap current sources in partition p.
 | Number of power pads in the design. |  | Maximum number of tap current sources among partitions.
 | Number of tap current sources in the design. |  | Number of tap current sources in current load window of partition p.
 | Number of tracks on metal layer l. |  | Maximum number of tap current sources in current load window among all partitions.
 | Maximum number of tracks among L metal layers. |  | Number of partitions.
Name | Description | Name | Description
 | Number of metal layers used in PDN. |  | Number of tap current sources in partition p.
 | Number of power pads in the design. |  | Maximum number of tap current sources among partitions.
 | Number of tap current sources in the design. |  | Number of tap current sources in current load window of partition p.
 | Number of tracks on metal layer l. |  | Maximum number of tap current sources in current load window among all partitions.
 | Maximum number of tracks among L metal layers. |  | Number of partitions.
Complexity to find a min-resistance path in the PDN is
Complexity to calculate is
Complexity to calculate is
Electric Feature Extraction Complexity is
With fixed partition size, feature extraction roughly
scales as
Notes: Here are some comment about runtime behavior. Our runtime is separately helped by multithreading.
Using std map implementation, the complexity to find the via points between two metals is Big-O of the maximum number of tracks in a layer, times log of the maximum number of tracks in a layer.
Hence the complexity of finding a minimum-resistance path between two nodes is the number of layers between these two nodes , TIMES N log N where N is the maximum number of tracks in a layer.
Then, The complexity of Pullup Component calculation is N_tap times N_pad , times this complexity of finding a single minimum-resistance path.
[Point] Next, the complexity of PullDown Component calculation is the number of partitions , TIMES the number of tap current sources in the partition, TIMES the number of tap current sources in its current load window, TIMES the complexity of finding a minimum-resistance path.
Hence, with fixed partition size, our overall electrical feature extraction scales as shown here, and it depends chiefly on the number of layers and the maximum number of tracks in a layer in the partition.
13:40 ~ 14:00

## Slide 21: Outline
Background and Motivation
Related Work
Our Methodology
Experimental Setup and Results
Conclusion
Notes: I will now show our experimental results.

## Slide 22: Experimental Setup
150 SOC floorplan designs with different
  Power distributions
  PDN structures
  Power pad pitches
Technology | 28nm foundry technology | Intermediate Metal Layer Track Usage | 10 % - 20 %
Package | Flip Chip | Supply Voltage | 1V
Chip/Block Size | 6000 – 30000 | Power Pad Pitch | 250 – 1000
Power | 10 W – 20 W | Max Number of Instances | 759850
Technology | 28nm foundry technology | Intermediate Metal Layer Track Usage | 10 % - 20 %
Package | Flip Chip | Supply Voltage | 1V
Chip/Block Size |  | Power Pad Pitch | 
Power | 10 W – 20 W | Max Number of Instances | 759850
Name | # of Nodes (million) | Total Power (W) | # of tap current sources
Design1 | 5.4 | 10.87 | 95K
Design2 | 9.6 | 14.34 | 263K
Design3 | 17 | 19.27 | 481K
Design4 | 27 | 24.87 | 742K
Design5 | 10.6 | 14.34 | 183K
Design information
Generated Power distribution figure
Training data information
Notes: Here is our experimental setup.
We use 28nm foundry technology to generate the test cases.
[Optional]
The training data information table shows the package, range of chip size, power, intermediate metal layer track usage, supply voltage, power pad pitch, and max number of instances.
We generate 150 SOC floorplan designs with different
[Click] Power distributions, PDN structures, and power pad pitches to train our model.
[Click] We use 5 designs for the following experiments. The max number of Nodes is 27 MILLION and the max number of tap
Current sources is around 742 THOUSAND.

## Slide 23: Experiment 1: Model Accuracy
Mean average error: -mV
Standard deviation: 0.52mV
99.7% predicted IR drop errors < 1.5mV
+/- 5mV
+/- 5mV
Notes: Experiment 1 shows our model accuracy.
Figure (a) and (b) show the golden IR versus predicted IR of training set and testing set, respectively.
The middle blue solid line represents a perfect match of predicted IR and golden IR. Our predicted IR errors in training and testing set are within 5mV.
From the error distribution, the mean average error is -mV.
The standard deviation is 0.52mV.
99.7% of predicted IR drop errors are smaller than 1.5mV.
1 min
Now I am going to talk about the model accuracy.
Figure (a) and (b) show the golden IR versus predicted IR of training set and testing set, respectively.
The middle blue solid line represents a perfect match of predicted IR and golden IR. Our predicted IR error in training and testing set are within 5mV.
The mean average error is -4.26×〖10〗^(−3)mV , with standard deviation of 0.52mV. Hence, 99.7% of predicted IR drop values are within the 3-sigma range of +/-1.5mV.
1 min

## Slide 24: Experiment 2: Incremental IR Prediction
IR prediction for single incremental modification
22 to 919 speedup with < 1mV and < 5.07mV
Incremental modification table
PDN info | Modifications |  |  |  | RedHawk |  | Our Proposed Method (IncPIRD) |  |  |  |  |  | Speedup
Name |  |  | (%) | Power Pad Modification | Runtime (sec) | WIR (mV) | (sec) | (sec) | (mV) | (mV) | (mV) | (%) | RedHawk (X)
 | (%) | (mW) |  |  |  |  |  |  |  |  |  |  | 
Design 1 | 272 | 20.0 | - | - | 308 | 25 | 0.11 | 0.28 | 0.55 | 3.94 | 0.57 | 2.3 | 787
 | - |  | - | V | 308 | 25 | 5.76 | 0.27 | 0.32 | 2.51 | 0.45 | 1.9 | 51
 | - |  | 5 | - | 370 | 22 | 4.98 | 0.38 | 0.31 | 2.47 | 0.47 | 2.1 | 69
Design 2 | 200 | 50.0 | - | - | 562 | 24 | 0.75 | 0.55 | 0.29 | 3.40 | 0.44 | 1.8 | 432
 | - |  | - | V | 562 | 24 | 24.11 | 0.56 | 0.28 | 3.25 | 0.44 | 1.8 | 22
 | - |  | -10 | - | 473 | 21 | 10.13 | 0.34 | 0.45 | 3.70 | 1.40 | 6.7 | 45
Design 3 | 400 | 23.4 | - | - | 2021 | 27 | 0.48 | 1.72 | 0.34 | 4.16 | 0.32 | 1.2 | 919
 | - |  | - | V | 2021 | 26 | 48.84 | 2.26 | 0.33 | 5.07 | 0.12 | 0.5 | 40
 | - |  | -10 | - | 1489 | 31 | 32.65 | 1.42 | 0.39 | 4.07 | 1.13 | 3.7 | 44
Design 4 | 500 | 76.9 | - | - | 3273 | 21 | 0.70 | 3.34 | 0.27 | 3.04 | 0.41 | 2.0 | 810
 | - |  | - | V | 3273 | 19 | 72.94 | 3.01 | 0.27 | 3.84 | 0.53 | 2.7 | 43
 | - |  | -10 | - | 2653 | 22 | 52.10 | 1.87 | 0.29 | 3.90 | 1.27 | 5.9 | 49
PDN info | Modifications |  |  |  | RedHawk |  | Our Proposed Method (IncPIRD) |  |  |  |  |  | Speedup
Name |  |  |  | Power Pad Modification | Runtime (sec) | WIR (mV) |  |  |  |  |  |  | RedHawk (X)
 | (%) | (mW) |  |  |  |  |  |  |  |  |  |  | 
Design 1 | 272 | 20.0 | - | - | 308 | 25 | 0.11 | 0.28 | 0.55 | 3.94 | 0.57 | 2.3 | 787
 | - |  | - | V | 308 | 25 | 5.76 | 0.27 | 0.32 | 2.51 | 0.45 | 1.9 | 51
 | - |  | 5 | - | 370 | 22 | 4.98 | 0.38 | 0.31 | 2.47 | 0.47 | 2.1 | 69
Design 2 | 200 | 50.0 | - | - | 562 | 24 | 0.75 | 0.55 | 0.29 | 3.40 | 0.44 | 1.8 | 432
 | - |  | - | V | 562 | 24 | 24.11 | 0.56 | 0.28 | 3.25 | 0.44 | 1.8 | 22
 | - |  | -10 | - | 473 | 21 | 10.13 | 0.34 | 0.45 | 3.70 | 1.40 | 6.7 | 45
Design 3 | 400 | 23.4 | - | - | 2021 | 27 | 0.48 | 1.72 | 0.34 | 4.16 | 0.32 | 1.2 | 919
 | - |  | - | V | 2021 | 26 | 48.84 | 2.26 | 0.33 | 5.07 | 0.12 | 0.5 | 40
 | - |  | -10 | - | 1489 | 31 | 32.65 | 1.42 | 0.39 | 4.07 | 1.13 | 3.7 | 44
Design 4 | 500 | 76.9 | - | - | 3273 | 21 | 0.70 | 3.34 | 0.27 | 3.04 | 0.41 | 2.0 | 810
 | - |  | - | V | 3273 | 19 | 72.94 | 3.01 | 0.27 | 3.84 | 0.53 | 2.7 | 43
 | - |  | -10 | - | 2653 | 22 | 52.10 | 1.87 | 0.29 | 3.90 | 1.27 | 5.9 | 49
Note: stands for error
Notes: In Experiment 2, [click] We perform one incremental modification and validate the predicted IR drop with RedHawk.
[click] IncPIRD achieves 22 to 919x speedup compared with from-scratch analysis using the golden IR tool.
[click] The is less than 1mV and is around 5.07mV.
Since PDN modification needs to recalculate minimum-resistance paths, it takes longer runtime compared to macro/cell block and power pad modifications.
We perform one incremental modification and validate the predicted IR drop with RH.
IncPIRD achieves 22 to 919 speedup compared with the RH.
The 𝑒_𝑎𝑣𝑔 is less than 1mV and 𝑒_𝑚𝑎𝑥 is 5.07mV among these 4 test cases with different layout-based modifications.
Since PDN modification need to recalculate the shortest path resistance, it takes longer runtime compared to macro/cell block and power pad modifications.
Next I am going to show chain incremental modifications of Design5 result.
1 min

## Slide 25: Experiment 2: Incremental IR Prediction
IR prediction for chain incremental modifications of Design5
  Change the power of one cell block from 10mW to 100mW
  Move a macro
  Add a power pad
  Use denser intermediate metal layer
47 to 1112 speedup with < 1mV and < 3mV
Results from an example chain incremental modification
Moves | RedHawk |  | Proposed Method |  |  |  |  |  | Speedup
 | Runtime (sec) | WIR (mV) | (sec) | (sec) | (mV) | (mV) | (mV) | (%) | RedHawk (X)
1st Move | 640 | 53 | 0.20 | 0.43 | 0.23 | 1.93 | 0.67 | 3.76 | 1015
2nd Move | 634 | 53 | 0.19 | 0.38 | 0.23 | 1.93 | 0.67 | 3.76 | 1112
3rd Move | 638 | 52 | 8.68 | 0.35 | 0.23 | 2.12 | 0.04 | 0.24 | 71
4th Move | 2033 | 48.8 | 42.57 | 0.68 | 0.25 | 2.37 | 0.80 | 5.60 | 47
Moves | RedHawk |  | Proposed Method |  |  |  |  |  | Speedup
 | Runtime (sec) | WIR (mV) |  |  |  |  |  |  | RedHawk (X)
1st Move | 640 | 53 | 0.20 | 0.43 | 0.23 | 1.93 | 0.67 | 3.76 | 1015
2nd Move | 634 | 53 | 0.19 | 0.38 | 0.23 | 1.93 | 0.67 | 3.76 | 1112
3rd Move | 638 | 52 | 8.68 | 0.35 | 0.23 | 2.12 | 0.04 | 0.24 | 71
4th Move | 2033 | 48.8 | 42.57 | 0.68 | 0.25 | 2.37 | 0.80 | 5.60 | 47
Notes: Here, we perform four modifications in succession: (i) change the power of one cell block from 10mW to 100mW, (ii) move a macro, (iii) add a power pad, and (iv) use denser intermediate metal layer.
[click] IncPIRD achieves 47 to 1112 speedup compared with the golden IR tool to update the IR map after each of these modifications.
[click] After all four modifications, the final is less than 1mV and is less than 3mV.
Here, we perform four modifications in succession: (i) change the power of one cell block from 10mW to 100mW, (ii) move a macro, (iii) add a power pad, and (iv) use denser intermediate metal layer.
[click] IncPIRD achieves 47 to 1112 speedup compared with RH.
[click] The 𝑒_𝑎𝑣𝑔 is less than 1mV and 𝑒_𝑚𝑎𝑥 is less than 3mV.
20 sec

## Slide 26: Experiment 3: Robustness Experiment
To test model robustness, we vary:
  Power
  Intermediate metal layer track usage
  Power pad pitch
Range of values for each feature is found from the designs in training set
  If input feature of changed design is within
   is zero
  If input feature of changed design is outside of
  equals the distance of the input feature to closest end point of
Notes: In Experiment 3, we vary the (1) power, (2) intermediate metal layer track usage, and (3) power pad pitch to test the robustness of our model.
The range of values for each feature is found from the designs in training set.
If the input feature of the changed design is within
[Click] The is zero
If the input feature of the changed design is outside of
[Click] The equals the distance of the input feature to closest end point of .
To understand when will we update the model, we vary the (1) power, (2) intermediate metal layer track usage, and (3) power pad pitch to test the robustness of our model.
The range of values for each feature 𝑅_𝑓 are found from the designs in training set.
If the input feature of the changed design is (1) within 𝑅_𝑓 => 𝛿_𝑓𝑒𝑎𝑡𝑢𝑟𝑒 is zero; (2) outside of 𝑅_𝑓 => 𝛿_𝑓𝑒𝑎𝑡𝑢𝑟𝑒 equals the distance of the input feature to closest end point of 𝑅_𝑓.
The 𝐿_∞ norm of feature delta vectors is used to determine model update constraints.
The figures show varying power, intermediate metal layer track usage and power pad pitch respectively.
As the maximum error goes up, the delta Pulldown and Pullup are also growing.
We use 5mV maximum error as our threshold, and we can get the delta Pullup component and Pulldown component constraints as follows.
  𝐶𝑜𝑛𝑠𝑡𝑟𝑎𝑖𝑛𝑡 1: 𝛿_(〖𝑃𝐶〗_𝑑𝑜𝑤𝑛 )<0.0025
  𝐶𝑜𝑛𝑠𝑡𝑟𝑎𝑖𝑛𝑡 2: 𝛿_(〖𝑃𝐶〗_𝑢𝑝 )<0.4375
These two constraints are used to determine whether we need to update our model or not in the prediction flow.
2mins

## Slide 27: Experiment 3: Robustness Experiment
Use 5mV as max error tolerance
Model update condition
  Symbolic IR drop:
  Effective resistance:
Power |  | Intermediate metal layer track usage |  | Power pad pitch | 
0.0025 | - | - | - | 0.00846 | 0.4375
Power |  | Intermediate metal layer track usage |  | Power pad pitch | 
0.0025 | - | - | - | 0.00846 | 0.4375
Notes: The figures show varying power, intermediate metal layer track usage and power pad pitch respectively.
From varying power and power pad pitch experiment, when the maximum absolute error goes up, the delta Pulldown and Pullup are also growing.
The impact of different track usage of intermediate layer on our model accuracy is not so obvious.
Using 5mV as max error tolerance, we can observe the corresponding delta Pulldown and Pullup components in these three cases.
We pick the minimum delta Pulldown and Pullup component value among the three cases for our model update condition.
To understand when will we update the model, we vary the (1) power, (2) intermediate metal layer track usage, and (3) power pad pitch to test the robustness of our model.
The range of values for each feature 𝑅_𝑓 are found from the designs in training set.
If the input feature of the changed design is (1) within 𝑅_𝑓 => 𝛿_𝑓𝑒𝑎𝑡𝑢𝑟𝑒 is zero; (2) outside of 𝑅_𝑓 => 𝛿_𝑓𝑒𝑎𝑡𝑢𝑟𝑒 equals the distance of the input feature to closest end point of 𝑅_𝑓.
The 𝐿_∞ norm of feature delta vectors is used to determine model update constraints.
The figures show varying power, intermediate metal layer track usage and power pad pitch respectively.
As the maximum error goes up, the delta Pulldown and Pullup are also growing.
We use 5mV maximum error as our threshold, and we can get the delta Pullup component and Pulldown component constraints as follows.
  𝐶𝑜𝑛𝑠𝑡𝑟𝑎𝑖𝑛𝑡 1: 𝛿_(〖𝑃𝐶〗_𝑑𝑜𝑤𝑛 )<0.0025
  𝐶𝑜𝑛𝑠𝑡𝑟𝑎𝑖𝑛𝑡 2: 𝛿_(〖𝑃𝐶〗_𝑢𝑝 )<0.4375
These two constraints are used to determine whether we need to update our model or not in the prediction flow.
2mins

## Slide 28: Experiment 4: Model Accuracy on Different Designs
Ability to predict incremental IR drop in new designs without retraining
Design setup
  30 non-uniform power distribution
  30 uniform power distribution
Model is quite robust as long as the new extracted features satisfy the model update condition
Uniform power distribution test designs prediction error
Nonuniform power distribution test designs prediction error
Notes: In our last experiment, which is Experiment 4, we try to confirm the ability to predict incremental IR drop in new designs without retraining our model.
We generate 30 different non-uniform power distribution and 30 uniform power distribution test designs to test our model.
[Point] From the figures, when the maximum absolute error exceeds 5mV, the delta Pullup and Pulldown components also exceed the model update condition.
Our model is quite robust as long as the new extracted features satisfy the model update condition
20:32

## Slide 29: Outline
Background and Motivation
Related Work
Our Methodology
Experimental Setup and Results
Conclusion
Notes: I will now conclude my talk.

## Slide 30: Conclusion
Propose a learning-based incremental IR drop prediction method based on electrical and structural features
Compared to commercial golden IR analysis tool
  22-1000X speedup
  average error < 1mV
  max error ~ 5mV
Propose model update condition to improve the robustness
Ongoing / Future works
  Improvement of accuracy and speed (with better machine learning techniques)
  Extension of this work to dynamic voltage drop prediction
Notes: We propose a learning-based incremental IR drop prediction method based on electrical and structural features
Compared to a golden commercial IR analysis tool, IncPIRD achieves 22-1000X speedup with average error less than 1mV and maximum error around 5mV in our studies.
We propose a model update condition to improve the robustness of our model.
There are two main directions for future works.
The first one is Improvement of accuracy and speed. This can certainly include more research on machine learning techniques, and industry platforms such as ANSYS’s SeaScape big data framework look really interesting to us for this.
The second one is extension of this work to dynamic voltage drop prediction, which we know is a much harder prediction problem.

## Slide 31: Thank you!
UCSD ABKGroup is grateful to Qualcomm, Samsung, NXP, the IMPACT+/C-DEN centers, Mentor Graphics and the NSF for research support. We thank IMEC and Cadence for additional research enablements and collaborations.
Notes: Thank you for your attention!
22:00